## Slide 1: Background and motivation for further SL enhancement in Rel-19
3GPP RAN-Release 19 workshop
Taipei, June 15 - June 16, 2023
RWS-230XXXX
Agenda Item: RWS, 5
Source: OPPO
Document for: Discussion

## Slide 2: Outline
  SL-U RedCap
    Complexity Reduction
    Power Saving
  FR 2-1
  FR 2-2
  SL carrier aggregation

## Slide 3: Motivation for SL-U RedCap
  UEs operating in FR1 could be deployed as wearable device, in smart home and IIoT scenarios, etc. In network-less scenarios it is critical to keep cost and power consumption low.
  Currently, UE vendors are trying to minimize the cost and power consumption of their products in those scenarios. How to realize the communication and/or mutual discovery among UEs with various capabilities now becomes the most critical issue to commercialize for SL-U .
  In Rel-18 SL-U it is assumed all UEs will have equivalent capability, e.g. all of them may support up to 100MHz bandwidth, such SL-U UE requires high complexity and high power consumption.
  Rel-17 has specified support for Uu RedCap UEs, another WI to enhance Uu RedCap framework is under way in Rel-18, the 2 releases provide a solid foundation for SL-U RedCap.
  Open to discuss RedCap for SL on licensed band.

## Slide 4: Background Complexity reduction in Rel-17/18 Uu (FR1)
  Complexity reduction features evaluated in Rel-17: 20MHz instead of 100MHz, reduced number of UE Rx/Tx antennas, relaxed maximum modulation order, relaxed UE processing time, reduced number of layers, etc.
  Further BW reduction, relaxed processing time, and peak data rate reduction were studied in Rel-18, BW3 and PR1 will be supported.
Cost reduction for individual/combination of complexity reduction features |  |  | 
FR1 TDD UE complexity reduction technique(s) |  |  | 
20 MHz (instead of 100 MHz) |  |  | 
1 layer (instead of 4 layers) |  |  | 
1 layer, 1 Rx (instead of 4 layers, 4 Rx) |  |  | 
Double N1 and N2 (Not supported in Rel-17) |  |  | 
DL 64QAM (instead of DL 256QAM) |  |  | 
UL 16QAM (instead of UL 64QAM) |  |  | 
20 MHz, 1 layer, 1 Rx, DL 64QAM, UL 16QAM |  |  | 
Option BW3: 5 MHz BB bandwidth only for PDSCH (for both unicast and broadcast) and PUSCH with 20 MHz RF bandwidth for UL and DL. The other physical channels and signals are still allowed to use a BWP up to the 20 MHz maximum UE RF+BB bandwidth.
Option PR1: Relaxation of the constraint v_layer*Qm*f for peak data rate reduction from 4 to 1.
Cost reduction for individual/combination of complexity reduction features (Compared to Rel-17) |  | 
Options | TDD 1Rx | TDD 2Rx
BW3 | 7.66% | 7.68%
PR1 | 4.02% | 3.73%

## Slide 5: Options for complexity reduction in SL-U
  Candidate features for complexity reduction in SL:
Options for reduction | Rel-16 SL UE | SL-U RedCap
Maximum bandwidth | FR1: 100MHz | Reduced to ≤20MHz (refer to next slide)
Number of Rx/Tx antennas | 2 Rx antenna/1 Tx antenna | 1 antenna for both Rx/Tx
Number of Layers | 2 layers (up to UE capability) | 1 layer
Maximum modulation order | 256QAM (up to UE capability) | Can be reduced to 16QAM or QPSK
Peak data rate | No restriction on No restriction on maximum TBS | No specific restriction (reduced with max BW and max modulation order)
UE processing capability/time | sl-MinTimeGapPSFCH | Open to discuss
Options for reduction | Rel-16 SL UE | SL-U RedCap
Maximum bandwidth | FR1: 100MHz | Reduced to ≤20MHz (refer to next slide)
Number of Rx/Tx antennas | 2 Rx antenna/1 Tx antenna | 1 antenna for both Rx/Tx
Number of Layers | 2 layers (up to UE capability) | 1 layer
Maximum modulation order | 256QAM (up to UE capability) | Can be reduced to 16QAM or QPSK
Peak data rate |  | No specific restriction (reduced with max BW and max modulation order)
UE processing capability/time |  | Open to discuss

## Slide 6: BW reduction options
Options | Max BW for Rx/Tx | Cost reduction (compared to the reference UE indicated in the appendix) | Comments
SL BW0 | 20MHz for both BB and RF | 32.9% | Same as Rel-17 Uu Redcap; No impact to LBT, and IRB structure can be used to satisfy OCB/PSD requirement; Specification impact is LOW.
SL BW1 | Less than 20MHz for both BB and RF | 42.0% if reduced to 5MHz | LBT cannot be performed, means to exempt from LBT restriction is needed. OCB cannot be satisfied, if OCB exemption cannot be used, the feature can only be applied when no OCB requirement. Cost for both RF and BB can be further reduced comparing to SL BW0. Specification impact is much larger than SL BW0.
SL BW2 | 20MHz for RF Less than 20MHz for BB | 39.4% if BB reduced to 5MHz | No cost reduction on RF compared to SL BW0; For BB, the cost of Rx processing, LDPC decoder, HARQ buffer and Tx processing can be reduced compared to SL BW0; Specification impact is in the similar level as SL BW0. LBT can be performed; OCB requirement can be satisfied;

## Slide 7: Evaluation on complexity reduction features
  Estimated cost reduction compared to the reference device for individual or combination of complexity reduction features.
  (Definition of the SL-U reference UE and detailed analysis on cost reduction are indicated in the appendix)
Chart: Cost Reduction
| Option 1: SL BW0 | Option 2: SL BW1 | Option 3: SL BW2 | Option 4: 1 Rx/Tx antenna (instead of 2Rx/1TX) | Option 5: 16QAM (instead of 256QAM) | Option 6: SL BW0+1 Rx | Option 7: SL BW0+1 Rx + 16 QAM | Option 8: SL BW2+1 Rx+16 QAM
 | 0.329 | 0.42 | 0.394 | 0.34 | 0.079 | 0.484 | 0.516 | 0.528

## Slide 8: Background for power saving
  Power saving supported already in Rel-17:
    DRX;
    Partial sensing;
    Random resource selection;
    IUC scheme 1 (preferred resource set for UE w/o sensing result)
  No power saving scheme so far for the followings:
    For reception: no power saving scheme for a UE without DRX configuration.
    For transmission: no power saving scheme for channel access.
      Back-off counter for Type 1 LBT could be up to 1000 when CAPC=3 or 4, considerable power may be consumed in particular under congested channel.

## Slide 9: Options for power saving
  Limited bandwidth operation
    Transmitting/receiving on bandwidth smaller than SL BWP or resource pool;
  DRX enhancement, e.g., extended SL DRX, WUS + SL DRX.
  Power saving for channel access
    E.g. COT sharing enhancement, LBT exemption with low transmission power
  Reduced 1st/2nd stage SCI monitoring
    1st/2nd stage SCI monitoring account for 70% of power consumption to receive 1 slot;
    Unnecessary 1st/2nd SCI monitoring may cost up to 97.5% power of a UE in unicast ftp traffic, e.g. {50s, transmitting in 250 slots, receiving interested transmissions from peer UE in 250 slots，monitoring 1st/2nd stage SCI in all the other slots, 20MHz，30kHz SCS}
    Power-efficient manner is necessary for a UE to filter interested receptions.

## Slide 10: Scope for SL-U RedCap
  Study and specify mechanism(s) to reduce UE capability in SL-U, such as maximum bandwidth reduction, maximum modulation orders reduction, number of antenna(s) reduction, number of layer(s) reduction, etc..
  Study and specify supporting SL communication among UEs with different capabilities in SL-U.
  Study and specify power saving mechanisms for SL-U, including limited bandwidth operation, DRX enhancement, reduced 1st/2nd stage SCI monitoring, power saving for channel access, etc.

## Slide 11: FR 2-1
  Motivation
    FR2-1 study item will be finished in Rel-18, and can be converted to a work item in Rel-19.
  Scope
    Initial beam-pairing:
      Relationship between initial beam pairing and PC5-RRC connection setup procedure
      Reference signal for initial beam pairing: S-SSB and/or SL CSI-RS
      TX beam selection/reporting and RX beam selection
    Beam maintenance: beam measurement, new beam selection, etc.
    Beam failure detection, either one or both of Option 1/2
      Option 1: NR Uu as baseline: periodic CSI-RS, BFI determination and report to MAC, counter+timer based
      Option 2: SL RLF mechanism as baseline
    Transmission resource for beam failure reporting
    Beam failure recovery: new TX beam selection and reporting
    Necessary SL CSI-RS enhancement: periodic, standalone, multiple CSI-RS in one slot, etc

## Slide 12: FR 2-2
  Motivation
    The specification for support of NR Uu operation in FR2-2 (52.6GHz - 71GHz) has been completed in Rel-17, where new SCS and channel access schemes applicable for FR2-2 are introduced.
    The bandwidth of the unlicensed spectrum in FR2-2 is much wider than that in FR 1 or FR 2-1, while the interference is much less as there is no other RAT deployment for now, the spectrum is attractive for services demanding high throughput e.g. XR/cloud gaming.
  Scope
    Study and specify necessary enhancement to introduce new numerology (e.g. 480/960KHz ) for SL-U to support operation in FR2-2
      Enhance PHY channel structure and/or procedure based on new numerology
    Study and specify necessary enhancement (if any) for SL beam management introduced in FR 2-1
    Study and specify necessary enhancement (if any) for channel access mechanism.
      The channel access mechanisms (e.g. Type 1/2/3 CA) and directional LBT mechanism specified in NR Uu FR2-2 are taken as baseline.

## Slide 13: SL carrier aggregation (CA)
  Background
    A basic version of SL CA will be supported in R18 (based on a per-carrier operation principle) for ITS/V2X services
      Intra-band contiguous CA in Band n47 only
      Both data aggregation and packet duplication are included
      From RAN#99, 5GAA only interested in Mode 2 operation.
    In Rel-19, car OEMs would like to support non-contiguous CA in Band n47
    Further enhancement on CA is expected by companies, e.g., to support licensed+licensed, licensed+unlicensed, FR1+FR2, unlicensed+unlicensed, etc. Due to very limited interests to deploy SL in the licensed spectrum, the CA work could focus only on unlicensed+unlicensed scenario.
  Scope
    Enhancement of SL carrier aggregation could include enhanced/advanced features that are not included in R18, and applicable to interested spectrum combinations, meanwhile can fit into the limited time frame of Rel-19, such as (please refer to the Appendix):
      Different SCS in multiple carriers
      Limited transmission and reception capability
      intra-band and inter-band CA @ FR1 only

## Slide 14: Appendix

## Slide 15: Capability of reference SL-U UE for evaluation
  Capability of reference SL-U UE are defined as follows:
    Single RAT
    Single band
    Power class: PC3 (23dBm)
    Max bandwidth: 100MHz for FR1
    Antennas: 2Rx/1Tx
    Max modulation order: 256 QAM
  Cost breakdown of the reference UE is shown in the table on the right.
Functional block | cost
RF | 
Power amplifier | 38.5%
Filters | 11.5%
RF transceiver (including LNAs, mixer, and local oscillator) | 42.3%
Switch | 7.7%
RF: Total relative cost | 100%
Baseband | 
ADC / DAC | 8.3%
FFT/IFFT | 3.7%
Post-FFT data buffering | 9.2%
Receiver processing block | 26.6%
LDPC decoding | 8.2%
HARQ buffer | 11.0%
SL control processing & decoder | 7.3%
Synchronization | 8.3%
SL processing block | 9.2%
MIMO specific processing blocks | 8.2%
BB: Total relative cost | 100%
RF+BB: Total relative cost | 100%

## Slide 16: Detailed cost reduction of each Opt.
Functional block | Reference | Opt.1 | Opt.2 | Opt.3 | Opt.4 | Opt.5 | Opt.6 | Opt.7 | Opt.8
Power amplifier | 38.5% | 38.5% | 38.5% | 38.5% | 38.5% | 38.5% | 38.5% | 38.5% | 38.5%
Filters | 11.5% | 11.3% | 10.4% | 11.3% | 6.1% | 11.5% | 6.0% | 6.0% | 6.0%
RF transceiver (including LNAs, mixer, and local oscillator) | 42.3% | 40.8% | 38.6% | 40.8% | 21.5% | 38.5% | 27.3% | 24.8% | 27.3%
Switch | 7.7% | 7.7% | 7.7% | 7.7% | 7.7% | 7.7% | 7.7% | 7.7% | 7.7%
RF: Total relative cost | 100% | 98.3% | 95.2% | 98.3% | 73.8% | 96.2% | 79.5% | 77.0% | 79.5%
ADC / DAC | 8.3% | 1.7% | 0.8% | 1.7% | 5.5% | 8.3% | 1.1% | 1.1% | 1.1%
FFT/IFFT | 3.7% | 0.7% | 0.5% | 0.7% | 1.9% | 3.7% | 0.4% | 0.4% | 0.7%
Post-FFT data buffering | 9.2% | 1.8% | 0.7% | 1.8% | 4.6% | 9.2% | 0.9% | 0.9% | 1.8%
Receiver processing block | 26.6% | 5.3% | 3.1% | 3.1% | 13.8% | 20.7% | 2.7% | 2.1% | 1.6%
LDPC decoding | 8.2% | 1.6% | 0.8% | 0.8% | 4.2% | 6.2% | 1.6% | 1.2% | 0.4%
HARQ buffer | 11.0% | 2.2% | 0.8% | 0.8% | 5.5% | 11.0% | 1.1% | 1.1% | 0.4%
SL control processing & decoder | 7.3% | 7.3% | 6.0% | 6.0% | 7.3% | 7.3% | 7.3% | 7.3% | 6.0%
Synchronization | 8.3% | 8.3% | 8.4% | 8.4% | 4.6% | 8.3% | 4.6% | 4.6% | 4.6%
SL processing block | 9.2% | 9.2% | 5.7% | 5.7% | 9.2% | 6.4% | 9.2% | 6.4% | 5.7%
MIMO specific processing blocks | 8.2% | 8.2% | 6.5% | 6.5% | 4.2% | 8.2% | 4.2% | 4.2% | 3.3%
BB: Total relative cost | 100% | 46.3% | 33.3% | 35.5% | 60.8% | 89.3% | 33.1% | 29.3% | 25.6%
RF+BB: Total relative cost | 100% | 67.1% | 58.0% | 60.6% | 66.0% | 92.1% | 51.6% | 48.4% | 47.2%
Total reduction |  | 32.9% | 42.0% | 39.4% | 34.0% | 7.9% | 48.4% | 51.6% | 52.8%

## Slide 17: Potential Rel-19 SL CA features
 |  | Licensed +Licensed （inter-band or intra-band (non-)cont. @FR1） | Unlicensed + Unlicensed （inter-band or intra-band (non-)cont. @FR1） | Licensed + Unlicensed (inter-band @FR1) | FR1+FR2 (inter-band (un-)licensed)
Different SCS | Different SCS | Needed | Needed | Needed | Needed
Mode 1 | Mode 1 | Optional | Optional | Optional | Optional
Limited UE capability | Limited UE capability | Needed | Needed | Needed | Needed
Cross-carrier operation | Cross carrier scheduling/control | Optional | Better to have | Better to have | Better to have
 | Cross carrier HARQ-ACK feedback | Optional | Better to have | Better to have | Better to have
 | Cross carrier CSI feedback | Optional | Optional | Optional | Optional
 | Cross carrier SL RSRP feedback | Optional | Optional | Optional | Optional
 | Cross carrier re-tx/duplication | Optional | Better to have | Better to have | Better to have
 | Beam management assistance | NO | NO | NO | Better to have