## Slide 1
Huawei, HiSilicon
Overview of Release 19 proposals
3GPP TSG RAN Rel-19 workshop RWS-230319
Taipei, June 15 - 16, 2023

## Slide 2
3GPP Rel-19 timeline
Rel-19 duration: 18 month for core functional work in each RAN WGs
  e.g. for RAN1, from January 2024 to June 2025
Rel-19 ASN.1 freeze in December 2025
We are here
R18 RAN1
R18 RAN2/3/4
R18 RAN1 Func. Freeze
R18 RAN2/3/4 Func. Freeze
First R18 ASN.1 review
R18 RAN1 Maint
R18 RAN2/3/4 Maint
R19 RAN1
Func. Freeze
R19 Pkg
(RAN4)
2023
Q1
Q2
Q3
Q4
2024
Q1
Q2
Q3
Q4
R19 Pkg
(RAN1/2/3)
R18 ASN.1 Freeze
2025
Q1
Q2
Q3
Q4
R19 RAN2/3/4
R19 RAN1
R19 RAN2/3/4
Func. Freeze
R19 ASN.1 Freeze
Note: As endorsed in Rotterdam in RP-230050 and summarized in SP-230390.

## Slide 3
ELAA-MM
XR Pro
Ambient IoT
Sensing
URLLC
8T8R
Uplink Enh.
Multi-carrier Enh.
Positioning
eRedcap
F1
F2
F3
F4
V2X
Multi-modality
FR1 HBF
Rel-19 as the second release of 5G-Advanced
Rel-19 is a core release for 5G-Advanced, critical to ensure healthy global 5G deployments in coming years
Rel-19 projects should be commercially and deployment driven
Strive for a good balance between use cases expansion, enhancements of existing use cases/features, and study/work on future-looking features

## Slide 4
Rel-19 should be dedicated to 5G-Advanced
Rel-19 is not yet about 6G
No TSG-level or WG-level 6G studies during entire Rel-19 timeframe
Further considerations will be given to the potential need to start channel modeling activities earlier in preparation for 6G technical studies, e.g. considering outcome of WRC-23 and overall ITU timeline

## Slide 5
Network energy saving (WI)
RWS-230364
Important solutions studied but not included in Rel-18 WI due to workload:
1. SIB1/paging-less for non-anchor cell
2. On-demand SSB/SIB1 with WUS for BS
Ambient IoT (SI+WI)
RWS-230407
New IoT segment to support batteryless device and co-deployment with 5G.
Critical to enable the use case in Rel-19 for competitiveness with other technologies, with a focused scope in Rel-19.
(semi-)passive tags (indoor) and active tags (indoor and outdoor) in licensed FDD spectrum, with direct BS connection
AI/ML for Air-Interface
RWS-230323
Whether to continue study or to have normative work is dependent on the outcome of Rel-18 SI
Study more sub use case in Rel-19, e.g. Temporal-spatial-frequency domain CSI compression
Multi-carrier Further Enhancements (WI)
RWS-230322
1. Single PDCCH for different SCS
2. UL Gbps with low DL complexity: One cell configured with multiple SUL
3. ms-level DL carrier switching via L1
4. Multi-carrier CSI measurement enh.
5. Flexible cross-cell scheduling/re-tx
Duplexing Evo (WI)
RWS-230324
Subband full duplex (SBFD)
BS-BS CLI for flexible TDD and SBFD
UE-UE CLI (if time allows)
Low Power WUS (WI)
RWS-230408
Joint OOK+FSK+sequence WUS design and related procedures for idle/inactive and connected mode
MIMO (WI)
RWS-230320, RWS-230321
Enhanced Hybrid BeamForming Massive MIMO for FR1
Hybrid BF concurrent multi-beam reporting for FR1 (~6GHz IMT), with reduced CSI-RS and CSI feedback overhead for larger BS antenna array
FR2 (mmWave) evolution
1. FR1-assisted FR2 low latency BM, exploiting angle correlation across FRs
2. Enhanced CSI/BM for larger BS array
FR1 Massive MIMO evolution
BS arrays with 64 antenna ports or more:
1. FDD: 64 CSI-RS ports and corresponding codebook
2. TDD: interference reduction on SRS (e.g. more SRS root sequences), SRS based channel prediction enhancement
Use cases expansion
Enhancing existing use cases/features
Future-looking features
Integrated Sensing & Communications (SI+WI)
RWS-230186
RAN/CN support to enable wide-area network-based sensing.
AI/ML for NG-RAN (WI)
RWS-230187
Support more use cases
Further Mobility Enhancements (WI)
RWS-230411
Inter-gNB LTM for mobility latency reduction.
High throughput maintenance for PCell switch and SCell switch
RAN1-led topic
RAN2-led topic
RAN3-led topic
SON/MDT enhancements (WI)
RWS-230189
Consider more scenarios
Rel-19 RAN1/RAN2/RAN3 Contents
XR enhancements (SI+WI)
RWS-230410
1. Enhancement on XR to ensure latency requirement guaranteed in varying radio condition
2. Enhancement for Multi-modal XR on synchronization, reliability and radio resource efficiency

## Slide 6
FR1 Massive MIMO evolution (WI)
RWS-230320
1. MIMO detection enh.: interference measurement enhancements for UL/DL demodulation
2. gNB-aided low complexity 8Rx UE (2 groups of 4Rx antennas without joint processing capability)
NR Positioning enhancements (WI)
RWS-230325
1. mmWave pos enh.: SRS Tx BF based on path RSRP
2. Carrier Phase based positioning evolution: dual-subband RS on the same symbol for positioning purpose
Further Sidelink Evo (WI)
RWS-230409
1. Sidelink operation on FR2, incl. FR2-2
2. SL CA: unlicensed FR1 CA, unlicensed FR2 CA, cross-carrier operation
Multi-TRP evolution (WI)
RWS-230320
Joint Tx/Rx (CJT/CJR) for non-ideal backhaul:
1. UE assistance to reduce scheduling delay
2. Synchronized L2 Processing Architecture
3. UE-assisted synchronization (DL & UL)
4. Improved estimation of UL interference for better DMRS channel estimation in UL mTRP operation
Enhancements of existing use cases/features (Cont.)
Support for Emergency Service (WI)
RWS-230188
Flexible multi-hop and multi-path IAB network
Use cases expansion (Cont.)
RAN1-led topic
RAN2-led topic
RAN3-led topic
NTN LEO evolution (SI+WI)
DL coverage and mobility enhancements for operation with multi-beam per satellite
Rel-19 RAN1/RAN2/RAN3 Contents (cont.)
High Accuracy Timing Service (WI)
RWS-230412
Support for 250ns~1us 5GS sync budget to fulfill vertical requirements:
Timing accuracy enforcement by considering UE internal accuracy loss and NLOS environment
Mobility support across working clock domains
Further MBS work (WI)
RWS-230326
Support extended CP for better spectrum efficiency
Multicast optimization in RAN sharing scenario to reduce Uu resource consumption

## Slide 7
Immediate market demand comes from:
    Indoor use cases, e.g. from retail and clothing industries to more industries (e.g., logistics and manufacturing), from inventory to sensing
    Outdoor wide-area use cases, such as infrastructure monitoring and asset tracking in the on-going intelligentization of various industries (e.g. smart city and supply chain), where some pilots being or to be launched in recent years
RFID does not have sufficient coverage, even indoors, to support expansion beyond rather basic use cases such as tracking of clothing and retail items. This leaves sectors such as logistics, manufacturing, sensors, etc. unaddressed.
RFID does not provide functions that allow monetization from a cellular network, e.g. charging, authentication, cell planning, interference management, etc.
Unaddressed sectors with opportunities for 10s of billions of tags will not remain unaddressed for long! Non-3GPP competitors WiFi, BLE, LoRA exist.
    But such competitors will also not be integrated into cellular networks and, if adopted, will exclude the 3GPP ecosystem from entering
    Existing 3GPP technologies such as NB-IoT do not have sufficient lifetime, nor suitable form factor, or complexity for entering these spaces
Study and Work on Ambient IoT in Rel-19 (RWS-230407)
 |  | Customer | Use case | Requirement | Desired technology readiness | Values
Local area | Company A | White goods producer | Real-time visible production and logistics | Autonomous inventory, 99.99% success, 1-3m positioning, Extreme low cost tag | 2024 | Reduce logistics costs Reduce production line shutdown
 | Company B | Automobile manufacturers | Warehousing inventory and material container management |  | Urgent, as early as possible | 
 | Company C | E-commercials | Account management |  | ~2024 | Improve inventory efficiency
Wide area | Company A/C/D | Logistics and distribution | Real-time property monitoring and quality tracing | Continuous coverage, battery-less, No manual maintenance, 99.99% success | ~2024 | Real-time tracking of vulnerable goods and valuable assets
 | Bureau of city management | City Infrastructure | Health monitoring |  | Urgent, as early as possible | Battery-less Higher safety Save cost as no manual maintenance
 | Company E | Smart grid | Sensor data collecting |  | 2025 | 
Chart: Global RFID Market Revenue Forecast (Million $)
| Transportation | Logistics and Supply Chain | Manufacturing | Retail | Healthcare | Aerospace and Defense | Agriculture | Others
2017 | 869.2 | 967 | 541.6 | 1783.7 | 735.2 | 497.7 | 587.1 | 1919.7
2020 | 937.4 | 1055.8 | 586 | 1912.3 | 794.3 | 534.9 | 634.5 | 2034.5
2022 | 975 | 1107.7 | 610.8 | 1980.8 | 827.2 | 555.3 | 661 | 2090.9
2025 | 1134.3 | 1305.8 | 712.8 | 2290.1 | 964.1 | 644.6 | 770.8 | 2388.7
2028 | 1459.1 | 1702.5 | 919.6 | 2927.1 | 1242.3 | 828 | 993.6 | 3016.7
2031 | 2072.2 | 2451.2 | 1309.7 | 4130.4 | 1767.3 | 1174.6 | 1414.1 | 4205.5
Motivation
Rapid growth is foreseen in the near future for the IoT markets requiring ultra-low cost maintenance-free wireless devices

## Slide 8
  RAN1-led SI + WI for Rel-19 Ambient IoT
  Need to consider carefully the amount of specification work and commercial relevance of Rel-19 Ambient IoT features
  Tag categories: Target both (semi-)passive and active device tags in Rel-19
    (Semi-)Passive device more preferable for indoor use cases, while active device may be the only choice for direct link to outdoor BS
    Standardizing active and passive in the same release does not require two parallel streams of work. By removing or simplifying functions from active tag to make passive tag, the passive tag adds ~20% workload (see RWS-230407)
  Spectrum: Target licensed FDD in Rel-19
    Higher service availability and reliability in licensed spectrum, longer effective range and lower device power consumption in lower frequency bands
  RAN connectivity: Target gNB direct bidirectional communication with Ambient IoT device in Rel-19
    Baseline of cellular network to meet high service availability and reliability in large or wide areas
Study and Work on Ambient IoT in Rel-19 (RWS-230407)
2023 |  |  |  | 2024 |  |  |  | 2025 |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3
Ambient IoT RAN-level SI
RAN #100
Ambient IoT SA2 SI
SA2
WI
Ambient IoT RAN WG-level SI
WI
RAN1/2/3/4…
RAN Rel-18
RAN Rel-19
RAN
Ambient IoT CT WI
CT
May extended to Q3

## Slide 9
Integrated Sensing and Communications in Rel-19 (RWS-230186)
Sensing in bad weather
Accurate Risk Finding
Motivation and use cases
3GPP SA1 is studying use cases and requirements for integrated sensing and communications in NR
Prioritized use cases: Smart Transportation for better traffic monitoring and management on roads, and UAV invading detection for protecting safety in public areas
Stadium
Enterprises
Smart Transportation
UAV detection
RAN already support network-based sensing
Sensing and communication can be multiplexed in time-domain
The effectiveness for network-based sensing for transport and UAV scenarios have been verified by prototype (in FR2)
Comm.
Sensing symbol
Time
Freq.
Lane-level car sensing
1km distance UAV detection
Enabling E2E sensing service requires standardization work
RAN need to report sensing measurements to 5GC, and the data format for sensing measurements need to be specified between RAN3 and SA2
Sensing modes
For use cases that require wide range sensing capability, network-based sensing modes will be the most suitable choices as gNB has much higher transmit power, larger antenna array than UE, and the necessary coverage for these use cases can be guaranteed by suitable network deployment
Network-based Integrated Sensing and Communications, study and specify signaling interactions between RAN and CN to support new sensing service
…
RAN-CN
Interface
RAN
5GC
APP
Motivation and Prioritization
Verification and Proposal

## Slide 10
Sub-7 GHz MIMO evolution in Rel-19 (RWS-230320)
Massive MIMO further evolution
FDD: CSI-RS and CSI enh. for supporting 64Tx
TDD: SRS enh. for channel prediction and interference mitigation
Receiver: Interference measurement for data, and low complexity 8Rx
Hybrid Beamforming (HBF) enhancements
Hybrid beamforming for Sub-7GHz:
CSI overhead reduction for multiple analog beams
CSI-RS overhead reduction and beam sweep latency reduction
Sub7GHz MIMO evolution should consider enhancements to accommodate more use cases, advanced BS and UE antenna architectures and more practical network deployment, including:
Multi-TRP Enhancements
CJT/JR with non-ideal backhaul
UE assisted scheduling and precoding alignments
Data alignment for TRPs, and UE assisted calibration
UL MIMO Enhancements
Interference suppression for UL DMRS
Sub-band precoding for UL
High resolution of UL precoding

## Slide 11
Millimeter wave evolution in Rel-19 (RWS-230321)
In current deployment, there are still issues for coverage and mobility. To maximize the value of the mmWave spectrum, Rel-19 mmWave evolution should target to further enhancements for mmWave coverage and mobility.
Beam management enhancements for FR2
For large antenna array with narrower beams
CSI measurement enhancement with wide beams
Beam management with analog PMI reporting
DFT-s-OFDM for FR2 DL
Support DFT-s-OFDM for FR2 DL, where UL DFT-S-OFDM design could be reused for DL
UL coverage enhancements for FR2
Relax EVM for UE to enable more power transmission (i.e., less power back-off)
gNB with nonlinear receiver to address the non-linearity of UL signals
FR1 assisted low latency Beam management
Introduce new UE specific temporary RS to reduce the latency for FR2 unknown SCell activation
Support reduced number of gNB Tx beam sweepings with FR1 assistance

## Slide 12
Support for XR enhancements in Rel-19 (RWS-230410)
Proposal 1: SI+WI for further XR enhancements in Rel-19
  Proposal 2: The objectives of SI include:
  General enhancements for XR
    Latency
          An E2E mechanism to enable dynamic QoS adaptation to varying radio conditions [RAN2/RAN3]
          Enhancement of SR to reduce scheduling latency [RAN1/RAN2]
    Resource efficiency
          RLC ARQ enhancement to avoid the out-of-PDB RLC retransmissions [RAN2]
  Enhancements for multi-modal XR
    Synchronization
          Study enhancements to ensure sync requirement between different XR modal traffic (e.g. video and haptic) [RAN2/RAN3]
    Reliability
          Achieve distinct reliability requirements of different traffic (e.g. video and haptic) when transmitting them in a single slot [RAN1]
    Resource efficiency
          Resource-efficiency enhancements to dynamic scheduling and/or configured grants to support variable packet sizes [RAN1/RAN2]
          PDCP concatenation for small haptic packets [RAN2]
XR enhancements in Rel-19
XR evolution
  Higher data rate: Future XR service is supposed to provide better visual quality (e.g. higher definition and higher FPS)
  Multi-modality: More XR device modals can bring various sensation to improve the user immersive experience
Challenges for new XR requirements
  a) Higher data rate raises new challenge for transmission to guarantee latency requirement
XR
Multi-modal XR (Rel-18)
About -60%
System capacity
Motivation
Chart: XR Capacity via R18
| 30Mbps, 60FPS | 45Mbps, 60FPS
 | 8.6 | 3.2
*Dense Urban, MU-MIMO, GOP-based I/P multi-stream model [TR 38.838]
b) Requirements of multi-modal XR
  Co-existence of multiple modalities with different traffic characteristics/KPIs and additional sync requirement
  Higher reliability and latency requirements for haptic data (99.999%@5ms from [TS 22.261])
Larger data rate
Primary use cases of XR, such as cloud gaming, glass-free 3D have been commercialized and are foreseen to grow rapidly

## Slide 13
Network energy savings (NES) enhancements in Rel-19 (RWS-230364)
NES is a long term requirement, and techniques for that should be continually evolved in 3GPP
Rel-18 NES WI focus on UE-specific signals/channels
Spatial and power domain techniques are applicable for UE specific PDSCH only, as required by Rel-18 WID
Although a group common PDCCH is introduced for cell DTX/DRX, it does not affect common signals/channels (e.g. no impact on SSB as also required by Rel-18 WID)
Adaptation of common signals/channels are also beneficial, as observed/concluded in Rel-18 NES SI, but only SSB-less for CA case is within Rel-18 NES WI
Techniques that enables reduced SIB/Paging etc. were extensively evaluated with benefits shown, however, were not included in Rel-18 WI scope due to limited TU
As the static power consumption decreases due to hardware efficiency improvements, reduction on dynamic power consumption can be critical. However, dynamic power due to common signals/channels is not fully resolved in Rel-18 WI.
Rel-19 NES enhancements should prioritize techniques for reducing common signals/channels (applicable also for IDLE UEs)
Multi-carrier scenario: SIB1/paging-less for non-anchor cell, with SIB1/paging provided from an anchor cell
Single-carrier: on-demand SSB/SIB1 triggered by UE WUS on, e.g., new bands
SIB1-less for multi-carrier non-CA case
On-demand SSB/SIB1 for single-carrier case
Motivation
R19 NES Enhancements
NES gain for SIB1-less compared with baseline with different SIB1 periods

## Slide 14
Multicarrier operation enhancements in Rel-19 (RWS-230322)
Motivation
Rel-19 MC operation enhancements
More and more carriers will be available at the operators side with the spectrum refarming. Further multicarrier enhancements to enable efficient utilization of the available carriers is promising.
Multicarrier PDCCH enhancement
Motivation: Multi-cell PUSCH/PDSCH scheduling with a single scheduling DCI is only supported for same SCS among co-scheduled cells, which restricts the applicable scenarios, e.g., TDD (3.5/2.6G) + FDD (Sub3G).
UL Gbps with low UE complexity
Motivation: In Rel-18, MC configuration requests UE to support 3 or 4 CC DL CA, leading to relatively high complexity for DL and limiting availability of UE for MC deployment in real field.
Multicarrier PDSCH enhancement
Motivation: Typically the number of carriers available at the network side is more than that can be supported by UE CA capability. Network can decide the best carrier for PDSCH transmission and indicate UE to switch among carriers. However, the large interruption time of DL carrier switching has significant impact on user experience.
Multicarrier CSI measurement enhancement
Motivation: Massive MIMO in CA scenario requires high UE complexity of CSI computation in Rel-18, which will result in that UE cannot obtain full channel information with limited capability of CSI measurement.
Flexible cross-cell scheduling and HARQ retx
Motivation: Latency reduction can be achieved by cross-cell related features. Some cross-cell related features are already supported, but some are still missing.
  Single PDCCH for different SCS among co-scheduled cells
Benefits: Extension of the applicable scenarios for single DCI, e.g. TDD+FDD scenario with different SCS.
  One serving cell with multi-SUL and one NUL associated with the single DL carrier
Benefits: Enabling UL Gbps user experience with low UE DL complexity.
  Fast DL carrier switching via L1 signaling
Benefits: ms-level DL carrier switching across more carriers than that can be supported by UE CA capability
  Joint CSI measurement across multiple carriers
32T
32T
32T
CC1
CC2
CC3
32 ports CSI1
Multicarrier CSI measurement enhancement
Benefits: Obtain full CSI information with similar UE complexity as measurement of single carrier in R18.
  Flexible cross-cell scheduling and HARQ retx
  PCell cross-cell schedules SCell while the SCell can still schedule the SCell itself.
  Cross-cell HARQ retransmission
Multicarrier PDSCH enhancement
PCell
PDSCH1
PDSCH2
SCell1
PDSCH1
PDSCH2
1~2ms
SCell2
SCell3
Benefits: Lower latency and control load balance

## Slide 15
Annex
Other topics for consideration in Rel-19

## Slide 16
LP-WUS in Rel-19 (RWS-230408)
    Signal design of LP-WUS
LP-WUS is at least used to indicate PDCCH monitoring
The activation/deactivation of LP-WUS monitoring is in explicit way or implicit way, which is known by gNB
Paging information is carried by LP-WUS, as well as other information, e.g. ETWS, SI change, cell/area ID
At least serving cell measurement is performed by LP-WUR, which can be based on periodically LP-SS.
    LP-WUS for CONNECTED mode
    Low-power synchronization signal
    LP-WUS for IDLE/INACTIVE mode
Specify harmonized OOK+FSK to achieve FSK benefits on time/frequency error robustness, etc
Sequence based modulation is supported on top of OOK and FSK to improve demodulation performance
Low precision LO used by Low power receiver has frequency error as high as 200ppm. It causes high frequency error and accumulates timing error rapidly.
It is desirable the modulation scheme is robust against both frequency/time errors.
It is also important that the receiver is able to assist LO perform frequency error correction.
Support of periodic low power synchronization signal for
  Time/frequency correction for LP-WUS demodulation
  Further enabling of RRM measurement by LP-WUR
Coverage performance is degraded than MR due to large noise figure and 1Rx reception
Coverage enhancements are supported, e.g., channel coding ( polar or high-rate error correction codes), time domain interleaving, etc.
The frequency/time errors due to low precision LO cause demodulation performance degradation or link failure if not corrected.
LP-WUS contributes significant power saving gain for idle/inactive mode
To maximize power saving gain, it should avoid to switch back to MR for RRM measurement frequently.
PDCCH monitoring brings a significant part of power consumption in CONNECTED mode.
Motivations
Proposals
Directions

## Slide 17
Duplexing evolution in Rel-19 (RWS-230324)
Motivation
Uplink enhancement with duplex evolution
Duplex evolution in Rel-19
Subband full duplex：
  Enable uplink coverage extension by 4~6dB
  Benefits: Improved uplink coverage
  Key challenge: Strong gNB-gNB co-channel inter-subband interference including leakage and blocking
  Potential solutions: Uplink muting resource for gNB-gNB CLI measurement; gNB-gNB channel measurement for beam nulling
  Enable low latency application requiring <4ms latency
Specify solutions to enable gNB-gNB co-channel CLI management for SBFD and flexible/dynamic TDD [RAN1]
  UE uplink muting resources for gNB-gNB co-channel CLI measurement
  Enhanced CSI-RS for gNB-gNB co-channel CLI/channel measurement
Specify signaling and UE procedure to enable SBFD operation [RAN1]
  Time and frequency location configuration of UL/DL subband
  UE collision handling between UL transmission and DL reception for SBFD-aware UEs
  Enhancements to physical layer channels/signals and procedures for SBFD [RAN1]
  Frequency resource allocation of PDSCH/PUSCH in case of unaligned boundaries between RBG/PRG(s) and SBFD subband(s)
  Frequency resource allocation of CSI-RS and subband configuration of CSI reporting across DL subbands
  Enhancement to UL transmissions and DL receptions across SBFD symbols and non SBFD symbols in different slots
Specify gNB RF requirement to enable SBFD operation [RAN4]
Specify solutions to enable UE-UE co-channel CLI management for SBFD and flexible/dynamic TDD [RAN1] (if identified beneficial and TU allows)
  L1/L2 based UE-UE measurement and reporting
Outdoor Homogeneous SBFD
Out-indoor SBFD
Flexible TDD：
Outdoor-indoor Dynamic/flexible TDD
Benefit：Boosted uplink throughput
Key challenge: gNB-gNB co-channel intra-subband interference
Potential solutions: Uplink muting resources for gNB-gNB CLI measurement

## Slide 18
NTN enhancements in Rel-19
Motivation
NTN enhancements in Rel-19
  Study new satellite parameters and solutions for coverage extension [RAN1]
    Satellite antenna, Tx power, coverage target etc.
    Study on solutions for system-level coverage extension
    Evaluate DL/UL coverage gap and solutions for smaller elevation angel
  Mobility efficiency improvement with extended coverage [RAN2]
    Reduce handover interruption time and reduce the times of sending handover command
  Rel-18 focuses on link-level coverage enhancements and the supported coverage with a single satellite is very limited
  With limited number of onboard beams and large number of beam positions in one satellite coverage, beam sweeping is needed for coverage extension. Due to slow beam switching capability, parabolic antenna assumed in Rel-17 and Rel-18 for RAN1 may not be able to support efficient beam sweeping
  Link level coverage may still be an issue to support coverage extension with limited satellite Tx power
  With limited single-satellite coverage, handover interruption and signaling overhead may not a big issue in Rel-17 and Rel-18. While with extended coverage, reduction in handover interruption time and signaling is needed.
    Handover interruption time on the level of SMTC periodicity (e.g. 160 ms) is non-negligible
Study new satellite assumptions and solutions for
System-level coverage extension and mobility enhancement

## Slide 19
Mobility enhancements in Rel-19 (RWS-230411)
Rel-18 LTM can achieve short handover interruption time. However, it is only applicable to intra-gNB(CU) scenarios. When UE moves across gNBs, it still suffers from long interruption time.
In LTM, throughput degrades after cell switch due to lack of early beam refinement, TRS tracking and CSI. Besides, in DAPS, there also exists throughput degradation due to lack of timely MCS selection.
There are services (such as immersive XR/Metaverse) with the following requirements in outdoor:
  Short interruption
  High throughput
  Wide area mobility
To specify mechanism and procedures of inter-gNB LTM for mobility latency reduction.
  Xn interactions during preparation phase and LTM execution
  Enhanced L1 report framework
  L2 handling mechanism including security update
Motivation
Rel-19 enhancements
To specify mechanism and procedures for high throughput maintenance.
  Early beam refinement, TRS tracking and CSI acquisition for target PCell in LTM
  Enhanced SCell switch in LTM
  Timely MCS selection in DAPS
Short interruption
High throughput
Wide area
Rel-19 Mobility enhancement

## Slide 20
Views on AI/ML for PHY in Rel-19 (RWS-230323)
Overview of Rel-18
Views for Rel-19
Temporal-spatial-frequency domain CSI compression
Beam management for large antenna array
Progress of RAN1
  Select 6 representative sub use cases and draw some observations
  Identify main components for LCM framework and recognize some of the candidate solutions
  Remaining main open issues:
    Functionality/model identification, training collaboration, model transfer/delivery, and data collection
Progress of RAN2
  Discuss candidate directions/solutions of protocol aspects and procedures according to the outcome from RAN1
  Remaining main open issues:
    Functionality/model identification and control, model transfer/delivery, data collection, and UE capability
      Some aspects needs to be studied per sub use case
Progress of RAN4
  Study core/performance requirements and test metrics per use case
  Remaining main open issues:
    Test framework for two-sided model, testability of potential test metrics, and verification of generalization
  For Rel-19, whether to continue study or to have normative work is dependent on the outcome of Rel-18 study
Study more sub use cases in Rel-19
  Temporal-spatial-frequency domain CSI compression
  Beam management for large antenna array
SSB/CSI-RS
Accurate analog BF
RS measures
(RSRP + phase)
Optimal ABF

## Slide 21
AI/ML for NG-RAN in Rel-19 (RWS-230188)
The AI/ML principles achieved in Rel-18, as follows, apply to Rel-19
  AI/ML algorithms and models are out of 3GPP scope
  Details of AI/ML model's performance feedback are out of 3GPP scope
  Base on existing RAN architecture, data security and privacy should be respected
  Signalling procedures between network nodes (mainly on Xn so far) used for the exchange of AI/ML related information (e.g., input, output, feedback, …) are use case and data type agnostic
  Discuss and work on potential new use cases, e.g. RACH reporting enhancements, CCO, etc.
Proposals
Motivation
Continuation of Rel-18 work
Artificial Intelligence / Machine Learning (AI/ML) for NG-RAN was started in Rel-18 with study on framework, general principles and potential use cases; and then normative work on three selected use cases; Network Energy Saving, Load Balancing and Mobility Optimization
Consideration on potential new use cases
Rel-19 should enhance Rel-18 use cases if any, and continue to work on potential new use cases which benefit from using AI/ML techniques

## Slide 22
SON/MDT enhancements in Rel-19 (RWS-230189)
Support of leftover item from Rel-18 not completed on time
  i.e. Voice fallback redirection, SCG failure in MR-DC
  e.g. SON/MDT for NPN, Successful MCG fast recovery, pending to the progress
Support of SON/MDT enhancements for:
  NR mobility enhancements
  IAB
  SL Relay
  Sidelink V2X
Support of signaling based logged MDT for IAB, SL-Relay, Slicing and fast SCG (de)activation
Support MDT latency measurement for IAB
Proposals
Motivation
Continuation of Rel-18 leftover
Rel-18 will complete SON/MDT enhancements for many features, including SON features for MRO for MR-DC SCG failure scenario, and MRO enhancement for inter-system handover voice fallback, SON/MDT enhancements for MR-DC CPAC, Successful PScell change report, Successful Handover Report (e.g. inter-RAT), NPN, etc., and MDT enhancements for inter-RAT mobility from 4G to 5G, and so on.
Some of Rel-18 objectives, however, are down prioritized, such as Voice fallback redirection, SCG failure in MR-DC and SON/MDT for NPN
New Rel-18 features
In Rel-18, new features were introduced, e.g LTM, IAB, V2X, SL, SDT etc., for which some SON/MDT enhancements deserved; For example, consider successful or failed LTM, to introduce RLF report for SL, to introduce IAB backhaul RLF report, to evaluate too late handover for UAV, to consider logged MDT for SDT, etc…
It is proposed to continue potential Rel-18 leftovers

## Slide 23
NR positioning enhancements in Rel-19 (RWS-230325)
IIoT positioning evolution to support 10cm level accuracy for AGV
Single-TRP positioning for FR2 with reflection
Support UE to perform UL Tx beamforming based on path RSRP (RSRPP).
Study the identification/path tracking for the ground reflection or any other reflection type
Location evaluation InF-DH: 30GHz, 800MHz |  |  |  | 
 | Single-BS, RTT+AOA | Group delay error STD | 80% | 90%
Horizontal | LOS only | 2ns | 0.694 | 0.875
 | LOS + Ground reflection | 2ns | 0.043 | 0.084
Subband RS and subband RSCP
Specify dual-subband RS pattern on the same symbol
Specify multiple subband RSCP/RSCPD reporting
Location evaluation InF-SH: 3.5GHz 100MHz |  | 
InF-SH location error @90% | perf gNB loc | 2cm gNB loc error
UL-DPDOA | 0.0018 | 0.1355
Multi-Freq RS with subband RSCP | 0.0301 | 0.0536
R17
R18
IIoT positioning functionality: 0.5m@90%
IIoT positioning evolution: 1 year battery life & 0.2m@90%
R19
Centimeter accuracy: 0.1m@90%
Motivation
mmWave positioning enhancements
Carrier phase positioning enhancements

## Slide 24
Sidelink enhancements in Rel-19 (RWS-230409)
Proposals
Motivation
Rel-19 SL should continue to leverage the use of wider bandwidth in new spectrum for ~Gbps communications:
E.g. motived for support interactive applications (e.g. XR, gaming) between UEs, i.e. up to 10Gbps, with <10ms, 99.99% reliability, as per TS 22.261.
Rel-18 only focus on studying of beam management on FR2 spectrum, however, without considering reliability, i.e. no enhancement on resource allocation (RA). The current NR SL RA is designed to operate on FR1 spectrum. It is important that sidelink operation on FR2 spectrum can achieve at least the same reliability as that on FR1 spectrum.
  Support of FR2-2 unlicensed spectrum is more valuable for commercialization, taking into account on spectrum availability for SL operation.
  CA in Rel-18 is rather limited and is un-suitable for use cases apart from V2X applications. With support of FR1 and FR2 unsilenced spectrum, the UE should be able to maximize the spectrum unitization for higher data rate as well as reliability enhancement. Thus CA in Rel-19 should be supported beyond ITS spectrum.
Proposal 1: Specify enhanced sidelink operation on FR2 spectrum
Specify sidelink beam management
Specify mode 1 and mode 2 enhancement for improved reliability on FR2 spectrum
This includes SL operation on FR2-2 unlicensed spectrum.
Proposal 2: Specify sidelink carrier aggregation
Support CA between FR1 unlicensed CCs, and between FR2unlicensed CCs.
Support of cross-carrier operation.

## Slide 25
High Accuracy Timing Services (RWS-230412)
Sync loss in the ring is up to 750ns (15hops).
NLOS
Timing accuracy enforcement
  To further enhance E2E delay measurement and compensation for timing accuracy enforcement [RAN2, RAN1, RAN4]
    The UE indicates the related UE-side timing distribution accuracy to gNB for E2E timing accuracy enforcement.
    E2E delay measurement and compensation is enhanced by taking the UE indication into account.
    NOTE1: The UE-side timing distribution (in)accuracy can be up to 15hops/750ns as specified in TS 22.104.
  To mitigate the propagation delay errors in NLOS for timing accuracy enforcement [RAN2, RAN1]
    The UE RX-TX time difference is extended to consider multi-path to align the DL and UL paths for RTT-based PDC calculation.
Mobility support across working clock domains
  Awareness of working clock domain change by gNB to optimize the timing service performance due to UE’s mobility [RAN3, RAN2]
    NOTE2: coordination with SA2 is needed.
Motivations
  IIOT synchronization has been supported and enhanced since Rel-16 with the target of E2E synchronicity of 1us for some use cases.
  More requirements for various use cases need to be addressed to help deployments in practice: synchronicity of 250ns (e.g. IEC 61850 from SA1), accuracy loss in NLOS environment and mobility across working clock domains.
Targets
  To achieve E2E synchronicity 250ns-1us by considering
    UE-side time distribution accuracy (Smart Grid/IIOT with 15 hops/750ns)
    Outdoor/NLOS deployment (Smart Grid within 20km2 area)
    Mobility requirement (Mobile Robot moving across multiple working clock domains)
Motivations and Objectives
Potential Proposals

## Slide 26
Support for emergency services (RWS-230187)
Motivations and Objectives
Proposals
Motivations:
  In emergency scenarios such as earthquakes, fires, and floods, communication in remote areas and deep-coverage urban areas cannot be guaranteed.
  In China, "14th Five-Year Plan for National Emergency Response System" proposes to build a nationwide emergency broadband wireless network.
  On-spot personnel should be equipped with video capture devices with resolution higher than 720p.
Objective:
  Achieve 95% coverage for 2Mbps on-spot video backhaul in 20km area and urban deep coverage area.
Proposals:
  Study mechanism with minimum specification impact to support flexible multi-hop and multi-path topology based on IAB architecture only for intra-CU case:
  Flexible topology enhancement, allowing e.g., switch parent/child relationship, service continuity against node moving (leaving or joining), more than two paths, …
  Intermediate node selection of better path based on path QoS
  BAP duplication forwarding to ensure the same date routed in different path
  Slice-specific backhaul configuration
Underground floor
High-rise building
1-hop IAB (Rel-16)
Multi-hop IAB (Rel-16)
Multi-hop & Multi-path IAB (Rel-17)
path 3 (Rel-19)

## Slide 27
MBS enhancements (RWS-230326)
Motivation
Further efficiency improvement for both broadcast and multicast
MBS enhancements in Rel-19
  Support Extended CP length for better spectrum efficiency
    Extend CP length for 15 kHz SCS and 30 kHz SCS
  Support multicast session optimization in RAN Sharing scenario to reduce Uu resource consumption
Broadcast：
  SFN is supported in Rel-17/Rel-18 within one single gNB by network implementation
  TV/video broadcast services can benefit from SFN to achieve better performance at cell edge.
  The CP length limits the size of SFN area and the size of SFN area limits the spectrum efficiency gain.
Multicast：
  MBS Multicast is not enhanced for RAN sharing (while MBS broadcast is being enhanced in Rel-18). In consequence, for the same MBS Multicast service, in shared RAN (with different PLMNs’ CNs), there will be multiple copies of MBS Multicast packets delivered over Uu.
UE group in CN1
UE group in CN2
CN1
CN2
MBS service
PTM
sharing node
TMGI 1
TMGI 2