## Slide 1
Huawei, HiSilicon
Millimeter wave evolution in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230321
Taipei, June 15 - 16, 2023

## Slide 2
Overviews on mmWave Evolution
In current deployment, there are still issues for coverage and mobility. To maximize the value of the mmWave spectrum, Rel-19 mmWave evolution should target further enhancements for mmWave coverage and mobility.
Beam management enhancements for FR2
For large antenna array with narrower beams
CSI measurement enhancement with wide beams
Beam management with analog PMI reporting
DFT-s-OFDM for FR2 DL
Support DFT-s-OFDM for FR2 DL, where UL DFT-S-OFDM design could be reused for DL
UL coverage enhancements for FR2
Relax EVM for UE to enable more power transmission (i.e., less power back-off)
gNB with nonlinear receiver to address the non-linearity of UL signals
FR1 assisted low latency Beam management
Introduce new UE specific temporary RS to reduce the latency for FR2 unknown SCell activation
Support reduced number of gNB Tx beam sweepings with FR1 assistance

## Slide 3
BM with A-PMI reporting for mmWave ELAA
Issues of BM for large antenna array
BM latency degrades mobility performance
1024 AE
4096 AE
UE obtains optimum BS beam by BM-CSI-RS measurements
UE acquires CSI (PMI/CQI/RI) for the selected beam
PXSCH transmission between UE and BS
With large number of narrow beams, several issues occur
  UE measurements: UE needs to measure more CSI-RSs (4x)
  RS overhead: BS needs to transmit more BM-CSI-RS
  Mobility: Narrow BS beams degrade the mobility performance
Beam management
CSI acquisition
PXSCH transmission
Baseline (R18)
30km/h
60km/h
Ideal
R18
Ideal
R18
-18.5%
-27.6%
DL UPT for mobile UEs
BM-CSI-RS transmitted by BS: 256
BM-CSI-RS measured by UE: 32
BM-CSI-RS transmitted by BS: 1024
BM-CSI-RS measured by UE: 128
Due to large latency, the mobile UE cannot always be served by the optimum beam, which degrades the performance
ELAA is an effective way to enhance the DL/UL coverage of mmWave; however, there are some issues to be solved
Baseline
ELAA
Large latency
To enhance the coverage of mmWave, increasing the antenna elements (ELAA, extremely large antennas) is a straightforward way, which provides much higher beamforming gain. However, due to the narrow beams, the system will cost more RS overhead for beam measurement and also cause mobility issues.
Observation 1: For coverage enhancement with large antenna array for mmWave, several issues need to be addressed, especially for RS overhead for beam measurement, mobility issues with narrow beams.

## Slide 4
Preliminary evaluation results
Step 1: Virtually split the array without introducing more TRX to get wider beam for BM and CSI acquisition
Step 2: UE reports Analog PMI to combine the split arrays to get the narrow beam for transmission
Beam management
CSI acquisition
PXSCH transmission
Beam management
APMI+CSI acquisition
Baseline (R18)
Enhancement
Wider beam results in fewer measurements (lower UE power consumption) and smaller RS overhead
A-PMI aided beam refinement ensures UE can obtain optimum beam with lower latency
PXSCH transmission
Reduce the RS overhead and UE measurements by up to 75%
Improve the DL UPT by ~15% (@30kmph) and ~25% (@60kmph) for mobile UEs
Using the wide beam for channel measurement, and UE report A-PMI (PMI reporting for Analog beamforming) instead of beam sweeping. Then, a narrow beam could be reconstructed by the A-PMI with combining the wide beams in gNB.
Baseline
Enhancement
Wide beam with sub-array antennas and A-PMI reporting
To address the issues of RS overhead and mobility, one simple way is to use wide beam with sub-array antennas in the beam measurement, and to use PMI reporting for Analog beams (A-PMI) instead of analog beam sweeping, which is also beneficial for latency reduction for beam management procedure.
Proposal 1: Support to use PMI reporting for Analog beams (A-PMI) with wide beam measurement to address the issues for RS overhead and mobility in mmWave.
BM with A-PMI reporting for mmWave ELAA

## Slide 5
DFT-s-OFDM for PDSCH in mmWave
DFT-s-OFDM is beneficial for coverage and PA efficiency
DFT-s-OFDM for DL in mmWave
EVM vs. output power
~3dB
ACLR vs. output power
~4dB
With same RF requirements (EVM and ACLR), DFT-s-OFDM can obtain ~3dB transmission power gain due to the lower PAPR
PDCCH (OFDM)
PDCCH (OFDM)
DMRS
PDCCH (OFDM)
PDCCH (OFDM)
DMRS
PDSCH (OFDM)
PDSCH (DFT-s-OFDM)
OFDM
DFT-s-OFDM
DFT-s-OFDM exists for UL transmissions, so the specification efforts for introducing DFT-s-OFDM for DL is very limited. The RS design for low PAPR for UL could be reused for DL.
OFDM and DFT-s-OFDM can be TDM without backward compatibility issues
DFT-s-OFDM is beneficial for low PAPR, which means better coverage performance of DFT-s-OFDM in the coverage limited scenarios. So, in mmWave, to enhance the coverage for DL, DFT-s-OFDM also could be used.
Proposal 2: Support to introduce DFT-s-OFDM for DL transmission to enhance the coverage in mmWave.

## Slide 6
Uplink Coverage Enhancement
MPR of mmWave terminal reduces UL coverage
 | pi/2-BPSK | QPSK | 16QAM | 64QAM | 256QAM
DFTs | 0dB | 2dB | 3.5dB | 5.5dB | 10dB
OFDM | - | 4dB | 5dB | 7.5dB | 12dB
Motivation: UL coverage of mmWave is limited by large MPR of terminals
  UE SINR can be improved significantly by the high BS large antenna array
  However, UL coverage is limited by PA/RF imperfect effects
  Due to the PA nonlinearity, the large power back-off is expected for mmWave terminal
Max power reduction of mmWave terminals (38.101)
ACLR vs. output power
FR1
FR2
EVM vs. output power
FR1
FR2
For coexistence reason, the transmitted signal should meet ACLR requirements
  For FR2: Even if ACLR requirement is met, the EVM is worse than requirement of QPSK
UE transmitter
BS receiver
DAC
ADC
EQ
NLC
UE transmitter: Relax the EVM requirement for large transmission power (small MPR)
BS receiver: Perform receiver nonlinearity compensation to improve the EVM
Uplink receiver nonlinearity compensation: improve uplink coverage by reducing the MPR of terminals
Uplink nonlinearity compensation to improve UL coverage
Simulation: Performance gain=power gain (MPR reduction)+demodulation gain
64QAM BLER
3.5dB gain=
3dB MPR+0.5dB require SNR
baseline
NLC
6dB gain=
4dB MPR+2dB require SNR
baseline
NLC
256QAM BLER
Enabling UE side to transmit more power (with less power back-off) is also a way to enhance the UL coverage in mmWave, i.e., reduce MPR with relax EVM requirements for mmWave terminals. Accordingly, gNB side needs to support non-linear receiver to match the nonlinearity of signals.
Proposal 3: To enhance the UL coverage in mmWave, support relaxed EVM on UE transmission to reduce MPR with non-linear receiver at gNB

## Slide 7
Low Latency Beam Management
In FR1 and FR2 CA cases, FR2 SCell may not always be in active state due to high UE power consumption. However, keeping FR2 SCell as inactive unknown state will require long activation time (shown as following hundreds milli-seconds).
Observation 2: The large latency for FR2 unknown SCell activation needs to be addressed for FR1 and FR2 CA cases.
Issues for FR1 and FR2 CA cases
Rel-19 Low Latency Beam Management (LL-BM): Keep FR2 inactive with low UE power consumption, and fast activate FR2 when it is available or burst packet arrives to achieve good user experience.
[1] System assumption: the packet size is 5Mbyte and the packet arrive rate is 0.2s/packet. The UE power consumption model is referred to TR 38.840.
Chart: 
| FR1-only | FR1+ 1 active FR2 (non-dormant) | FR1+ 1 active FR2 (dormant)
5M | 1 | 3.1 | 1.7
① If keeping one or more FR2 SCell in active state,
  Even with dormant BWP, beam management and measurement resulting in 1.7X~3X higher UE power consumption than FR1-only
  Long activation delay still needed if blockage happens or moving to FR2 unavailable area.
UE power consumption [1]
3.1X
1.7X
Active
Active
Inactive
FR1 100M
FR2 400M
FR2 400M
Throughput
> 600ms Delay
Big packet arrival, or FR2 coverage is available
FR2 SCell activated
Time
② If keeping FR2 SCell in inactive unknown state,
  No beam management and measurement is needed for low UE power consumption, but bad user experience when burst packet arrives due to long activation delay.
Active
Inactive
Inactive
FR1 100M
FR2 400M
FR2 400M

## Slide 8
Low Latency Beam Management
To address the latency issue for FR2 SCell activation in the deployment of co-located FR1 and FR2 CA, UE-specific reference signal (Temporary RS) can be introduced for fast SCell activation, and number of gNB Tx beam sweepings can be reduced with FR1 assistance by utilizing the high correlation on the beam direction/angle between FR1 and FR2.
Proposal 4: Support to introduce new UE-specific temporary RS along with reduced number of gNB Tx beam sweepings to reduce the latency for FR2 unknown SCell activation.
Latency reduction for FR2 beam management in FR1 and FR2 CA cases
Rel-18 baseline Large delay for activating FR2 SCell in non-active unknown state, which is caused by long beam sweeping and SSB period.
Rel-19 LL-BM Reduced delay for activating FR2 SCell in non-active unknown state, by reducing the beam sweeping and periodicity.
Periodicity is reduced from 20ms to 2ms by introducing new UE-specific temporary RS (T-RS) instead of cell-specific SSB.
②
5~8 * 2ms T-RS period = ~16ms delay
…..
…..
gNB Tx beam
UE Rx beam
Rx1~Rx8
Rx1~Rx8
Rx1~Rx8
Rx1~Rx8
AGC1
Rx1~Rx8
AGC2
Rx1~Rx8
Coarse Sync.
Rx1~Rx8
L1 meas.
Rx1~Rx8
Functionality
AGC1
AGC2
Coarse Sync.
L1 meas.
T-RS Period 1 (2ms)
1st candidate Tx beam based on FR1 channel
T-RS Period 8 (2ms)
8th candidate Tx beam based on FR1 channel
The number of FR2 candidate gNB Tx beams is reduced from 32 to 5~8 with FR1 assistance based on the angle correlations.
①
…..
…..
…..
SSB Period 1
SSB Period 8
32 * 20ms SSB period = ~640ms delay
…..
…..
…..
SSB Period 9
SSB Period 16
…..
…..
…..
SSB Period 17
SSB Period 24
…..
…..
…..
SSB Period 25
SSB Period 32
gNB Tx beam
UE Rx beam
AGC1
Rx1
Rx8
Tx1~Tx32
AGC2
Coarse Sync.
L1 meas.
Functionality

## Slide 9
Low Latency Beam Management
In following evaluations, it shows that, with FR1 assistance,
Significant gain could be obtained with new T-RS, especially for big data packets.
Top 8 beams will cover the best beam direction for FR2 with probability of 95%~97%.
Performance Evaluation
Simulation assumption
Parameters | FR1 | FR2
Bandwidth | 100 MHz | 400 MHz
BS antenna [Mg, Ng, M, N, P] | [1,1,4,8,2] | [1,1,16,16,2]
BS antenna location | FR1 and FR2 co-located | 
Height of antenna | BS: 25 m; UE: 1.5 m | 
Channel model 1 | 3GPP channel model (Uma, correlation modelling for multi-frequency simulations) | 
Channel model 2 | Measurement Calibrated channel model | 
Data composition | Mixed LOS&NLOS | 
Chart: 
| NLOS/LOS
Top 5 | 0.91
Top 8 | 0.95
Chart: Average UPT
| 2 | 5 | 10 | 30 | 50
R18 | 0.92615 | 0.94373 | 0.97266 | 1.0798 | 1.1759
New TRS without FR1-aided BM | 0.92615 | 0.94373 | 1.194 | 1.999 | 2.3953
New TRS with FR1-aided BM | 1.0315 | 1.6147 | 2.1347 | 2.8176 | 3.0238
2.57X
2.61X
1.11X
1.71X
2.19X
2.04X
1.85X
1X
1X
1.23X
Beam prediction based on FR1 channel info.
Top 8 beam training based on T-RS
It takes 640ms to fall back to remaining beams if activation is unsuccessful.
It takes 20ms if activation is successful.
95% (3GPP channel model)
/ 97% (Measurement channel model)
5% (3GPP channel model)
/ 3% (Measurement channel model)
FR2 activation command
System setting
Algorithm
3GPP channel model
Measurement channel model
FR2 beam prediction accuracy
FR2 beam prediction accuracy
Chart: 
| NLOS/LOS
Top 5 | 0.93
Top 8 | 0.97
Chart: Average UPT
| 2 | 5 | 10 | 30 | 50
R18 | 0.92615 | 0.94373 | 0.97266 | 1.0798 | 1.1759
New TRS without FR1-aided BM | 0.92615 | 0.94373 | 1.194 | 1.999 | 2.3953
New TRS with FR1-aided BM | 1.0337 | 1.6289 | 2.1595 | 2.856 | 3.0659
2.61X
2.64X
1.12X
1.73X
2.22X
2.04X
1.85X
1X
1X
1.23X
R18 (32 * 20ms SSB period = 640ms)
New T-RS without FR1-aided BM (32 * 2ms T-RS period = 64ms)
New T-RS with FR1-aided BM (8 * 2ms T-RS period = 16ms)

## Slide 10
Conclusions
In mmWave enhancements, we have the following observations and proposals,
Observation 1: For coverage enhancement with large antenna array for mmWave, several issues need to be addressed, especially for RS overhead for beam measurement, mobility issues with narrow beams.
Observation 2: The large latency for FR2 unknown SCell activation needs to be addressed for FR1 and FR2 CA cases.
Proposal 1: Support to use PMI reporting for Analog beams (A-PMI) with wide beam measurement to address the issues for RS overhead and mobility in mmWave.
Proposal 2: Support to introduce DFT-s-OFDM for DL transmission to enhance the coverage in mmWave.
Proposal 3: To enhance the UL coverage in mmWave, support relaxed EVM on UE transmission to reduce MPR with non-linear receiver at gNB.
Proposal 4: Support to introduce new UE-specific temporary RS along with reduced number of gNB Tx beam sweepings to reduce the latency for FR2 unknown SCell activation.