## Slide 1: Views on Intra-band non-collocated EN-DC/NR-CA in Release 19
KDDI Corporation, LG Uplus, NTT DOCOMO INC., SoftBank Corp.
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 – 16, 2023
RWS-230360

## Slide 2: Motivation
In Release 16, Intra-band non-contiguous non-collocated EN-DC (DC_42A-n77A, DC_42A-n78A) Type 2 UE functionality has been developed in RAN4. Additionally in Release 18, Intra-band non-contiguous non-collocated NR-CA (CA_n77(2A), CA_n78(2A)) Type 2 UE functionality is being developed currently.
On the other hand, in Apr. 2023, RAN4 agreed to propose RAN Plenary postponing following functionalities to the future release.
  Intra-band non-contiguous non-collocated EN-DC/NR-CA
    Type 3 and Type 4 UE
  Intra-band contiguous non-collocated EN-DC/NR-CA
    Type 2, Type 3 and Type 4 UE
In the 5G era, the non-collocated scenarios for B42 and n77/n78 as shown in the next slide still occur in some countries/operators. From this operators point of view, it is desirable to standardize some enhancements in Release 19 from operators.

## Slide 3: Background – Spectrum point of view in Japan

## Slide 4: Background – Spectrum point of view in Korea and Italy
Korea
Italy

## Slide 5: Potential enhancement area
In Apr. 2023, RAN4 agreed to propose RAN Plenary postponing following functionalities to the future release.
Type 2 : 2x2/cc, Separated 4Rx Chain
gNB(cc#1)
gNB(cc#2)
Conditions bw. gNBs
MRTD (33us)
Power imbalance (25dB)
Deployment scenario
Non-collocated
Different antenna pattern
UE
2 Rx Chain
2 Rx Chain
Power imbalance ≦25dB
Type 3 : 4x4/cc, Shared 4Rx Chain
Conditions bw. gNBs
MRTD ([??]us)
Power imbalance ([??]dB)
Deployment scenario
Non-collocated
Different antenna pattern
UE
4 Rx Chain
Type 4 : 4x4/cc, Separated 6/8Rx Chain
Conditions bw. gNBs
MRTD ([??]us)
Power imbalance ([25?]dB)
Deployment scenario
Non-collocated
Different antenna pattern
UE
4 Rx Chain
4 Rx Chain
Power imbalance ≦[25?]dB
gNB(cc#1)
gNB(cc#2)
gNB(cc#1)
gNB(cc#2)
Rel-18
Rel-19
Rel-19
Power imbalance ≦[??]dB

## Slide 6: Potential objectives
The core part of the work item includes:
Phase I:
  Study the feasibility to support non-co-located scenarios for both FR1 inter-band EN-DC with overlapping and FR1 intra-band NR-CA, except for 2-layer case already specified in Rel-16, 17 and 18.
    Investigate the tolerable power imbalance between carriers
    Investigate the required arrival time difference between CCs
    Investigate the additional impacts of contiguous case and non-contiguous 3cc case, if time units are available.
    Evaluate the UE performance under the power imbalance and arrival time difference
      Discuss and decide reference UE architecture considering the UE capability of 4-layer MIMO case for both EN-DC/NR-CA
      NOTE : For UE capable of supporting 4-layer MIMO, 2-layer MIMO power imbalance assumption can be considered as a base line but another value or the same power imbalance with different throughput performance requirement is not precluded.
    Work is limited to CA/EN-DC for EN-DC/NR-CA for bands 42, n77/n78
    Investigate whether the power imbalance should be explicitly (e.g. as an RF requirement) or implicitly specified (e.g. through a demodulation performance test). Specify the power imbalance based on the outcome of the investigation.
    If any change in RAN1 or RAN2 spec is needed, it will be triggered by RAN4 LS
Phase II:
  Phase II work will get started after the feasibility in phase I is confirmed
  Specify MRTD and MTTD requirements and other identified RRM requirement impact(s) (if any) in non-collocated deployment
  Discuss and decide if the different requirements will be specified based on UE capability of interBandMRDC-WIthOverlapDL-Bands-r16.

## Slide 7: Potential objectives
The performance part of the work item includes:
Phase II:
  Phase II work will get started after the feasibility in phase I is confirmed
  Specify PDSCH demodulation requirements for non-collocated scenarios for intra-band non-contiguous EN-DC and NR-CA
    Define PDSCH demodulation performance requirement based on the applicable MRTD and power imbalance values.