## Slide 1: Motivation of further SL Relay Enhancement in Rel-19
3GPP TSG RAN Release 19 workshop
Taipei, June 15-16, 2023
RWS-230393
Agenda Item: 5
Source: Lenovo
Document for: Discussion

## Slide 2: Rel-19 Sidelink Overview
Sidelink relay for L2 U2N relay
  Multi-path Enhancement
    More indirect paths
  Mobility with Multi-path
    Multi-path can be configured by target gNB
  Path Switching Enhancement
    Conditional path switching
    DAPS based path switching
  Group based Mobility

## Slide 3: Rel-19: Sidelink Relay
Multi-path Enhancement for single-hop L2 U2N relay
  Background: Intra-gNB based Multi-path is supported in Rel-18. Namely, A UE is connected to the same gNB using one direct path and one indirect path.
Proposals:
  Proposal 1: More indirect paths can be configured in multi-path case.
    Case 1: A UE is connected to the serving gNB using one direct path and multiple indirect paths.
    Case 2: A UE is connected to the serving gNB using multiple indirect paths.
Case 1
Case 2

## Slide 4: Rel-19: Sidelink Relay
Multi-path Enhancement for single-hop L2 U2N relay
  Background: Intra-gNB based Multi-path is supported in Rel-18. Namely, A UE is connected to the same gNB using one direct path and one indirect path.
Proposals:
  Inter-gNB mobility with multi-path should be supported if it is not addressed in Rel-18.
    Multi-path configuration can be configured in target gNB.
    Indirect path, direct path or both can be configured in source gNB.

## Slide 5: Rel-19: Sidelink Relay
Legacy Mobility for single-hop L2 U2N relay
  Intra-gNB/Inter-gNB indirect-to-direct (i2d) path switching
  Intra-gNB/Inter-gNB direct-to-indirect (d2i) path switching
  Intra-gNB/Inter-gNB indirect-to-indirect(i2i) path switching
Proposals:
  Condition based mobility for remote UE can be supported for i2d/d2i/i2i path switching.
  Condition based mobility for relay UE e.g CHO based relay handover can be supported.
  DAPS mechanism can be extended to the inter-gNB for i2d/d2i/i2i path switching.
Fig. DAPS based i2d path switching

## Slide 6: Rel-19: Sidelink Relay
Mobility enhancement for single-hop L2 U2N relay
  Background: In Rel-17/18, if the relay UE performs handover, relay UE will indicate to the served remote UE(s). Then, the remote UE performs re-establishment procedure and selects a suitable relay or cell for re-establishment.
    Proposals:
    Group based mobility e.g combination of relay UE and remote UE(s) can be supported.

## Slide 7: Thanks
thanks