## Slide 1: Views on NR MIMO in Release 19
KDDI corporation
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 – 16, 2023
RWS-230398

## Slide 2: Motivation
In Release 18, UL MIMO functionality has been enhanced, especially in UL SU-MIMO with up to 8 layers to improve peak throughput, in addition to DL MIMO enhancements.
In the 6G era, it is anticipated that many TRPs will be more widely distributed within the service area, allowing UEs to communicate freely with some of them to enjoy the desired communication quality anytime and anywhere without being aware of cell boundaries, in other words, a “cell-free architecture”.
From this perspective, it is desirable to standardize some MIMO techniques in the Release 19 MIMO enhancement to bring NR closer to the cell-free architecture envisioned in the 6G era.

## Slide 3: Potential enhancement area of NR MIMO
To approach the cell-free architecture of 6G era, the following enhancements will be required in Rel. 19.
The number of beams from many antenna array that UE needs to recognize may increase. ⇒The number of CSI-RS ports needs to be increased to be able to identify more beams.
UE needs to measure more beams. ⇒Since beam measurement will take more time, it is necessary to consider mechanisms to measure beams with low latency.
The precoding process for CJT will be performed between TRPs of different sites. ⇒Calibration between TRPs of different sites needs to be realized.
A larger number of channel estimations with accuracy between the UE and multiple TRPs will be required for downlink CJT. ⇒Further improvement of channel estimation by SRS is needed by additional works for leftover SRS enhancement in Rel. 18.
TRP
UE
UE
TRP
A),B)
C)
D)

## Slide 4: Potential objectives
Potential objectives should include the following.
  Study, and if justified, specify larger number of CSI-RS ports per resource.
    The number should be more than that in Rel-18, i.e. 32.
  Study, and if justified, specify low latency beam management scheme.
    UE-initiated beam management (selection/indication) scheme can be considered.
  Study, and if justified, specify inter-site antenna calibration scheme for CJT.
  Study, and if justified, specify further SRS enhancement to enhance SRS capacity and accuracy of channel estimation with SRS between UE and multiple TRPs.
    Enhancement of SRS power control toward multi-TRP, randomized transmission of SRS and other SRS enhancements dropped during Rel.18 discussion should be further considered to manage inter-TRP cross-SRS interference targeting TDD CJT.