## Slide 1
CBN，CATT
NR MBS enhancement for Rel-19
3GPP TSG RAN Rel-19 Workshop Meeting, June 15 - 16, 2023
Agenda item: 5
RWS-230403

## Slide 2
Rel-19 MBS：Extended CP support for NR MBS
Background:
The specification only allows normal CP for the 15kHz and 30kHz subcarrier spacing so far, which unnecessarily imposes the limits to the deployments of MBS with low spectral efficiency.
Support of extended CP has been motivated and discussed as in RWS-210446 and RWS-210330 when scoping Rel-18 but was precluded in the end due to leveraging several aspects including available TU and the proposed enhancements scope.
Chart: 0.7GHZ/Reserved cell，SINR / SFN size
| 7(12) | 19(18) | 37(24) | 61(30)
4.7us | 2.9 | 4.5 | 4.9 | 5.8
16.7us | 7.6 | 11.2 | 12.6 | 14.6
Radio Network：
Specify support for multicast/broadcast with extended CP for 15kHz and 30KHz SCS for DL and UL[RAN1,RAN2]

## Slide 3
Rel-19 MBS： Enhancement for RedCap UE
Background：
Only one broadcast bandwidth is support in Rel-17.
Additional CFR for RedCap UE has been agreed in Rel-18.
Radio Network：
Resource efficiency enhancement for RedCap UE[RAN1,RAN2]
Alternative 1：Single MTCH with separated MCCH for legacy UE and (e)RedCap UE
Alternative 2：Single MCCH with separated MTCH for legacy UE and (e)RedCap UE

## Slide 4
Rel-19 MBS： RAN sharing for multicast
Background:
R18 only specifies the enhancement for broadcast session in RAN sharing scenario.
Radio Network:
RAN sharing for multicast[RAN3,RAN2]
Based on the solution of enhancement for broadcast in Rel-18, discuss whether the similar solution can be applied to
multicast to identify a same multicast service from different PLMNs from RAN perspective.
The enhancement for loss-less handover procedure in such scenario, which is not required for broadcast service, and with
quite a few impacts on 5GC procedures, e.g. SN alignment among the DL packets of the involved PLMN.

## Slide 5
Summary of NR MBS enhancement for Rel-19
Continuous improvements are demanded based on strong market requirements for NR MBS deployment.
Proposal:
Extended CP support for NR MBS
—Specify support for multicast/broadcast with extended CP for 15kHz and 30KHz SCS for DL and UL[RAN1,RAN2]
Enhancement for RedCap UE
—Resource efficiency enhancement for RedCap UE[RAN1,RAN2]
RAN sharing for multicast[RAN3,RAN2]