## Slide 1
Huawei, HiSilicon
Scope of Ambient IoT work in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230407
Taipei, June 15 - 16, 2023

## Slide 2
R19 Ambient IoT Scope
  RAN1-led SI + WI for Rel-19 Ambient IoT
  Need to consider carefully the amount of specification work and commercial relevance of Rel-19 Ambient IoT features
  Tag categories: Target both (semi-)passive and active device tags in Rel-19
    (Semi-)Passive device more preferable for indoor use cases, while active device may be the only choice for direct link to outdoor BS
    Standardizing active and passive in the same release does not require two parallel streams of work. By removing or simplifying functions from active tag to make passive tag, the passive tag adds ~20% workload (see Annex)
  Spectrum: Target licensed FDD in Rel-19
    Higher service availability and reliability in licensed spectrum, longer effective range and lower device power consumption in lower frequency bands
  RAN connectivity: Target gNB direct bidirectional communication with Ambient IoT device in Rel-19
    Baseline of cellular network to meet high service availability and reliability in large or wide areas

## Slide 3
RFID Grows Rapidly – Technology Constraints Limit RFID Value to Industries
Volumes of RFID tag 20B in 2022 and 49B in 2031，UHF takes 65%
Total addressed market of RFID up to $18.5B
Chart: Global RFID Market Volume Forecast (Million Units)
| 2017 | 2020 | 2022 | 2025 | 2028 | 2031
LF | 1746.3 | 1828.7 | 1851.9 | 2096.2 | 2655.1 | 3745.5
HF | 4661.5 | 5155 | 5421.2 | 6506.1 | 8761.7 | 13183.9
UHF | 10143.5 | 11494.9 | 12287.6 | 15114.3 | 20864.6 | 32187
2.4G | 138.3 | 147.9 | 153.6 | 170.1 | 196.9 | 234.3
~49 Billion
UHF
65%
27%
8%
~20 Billion
Chart: Global RFID Market Revenue Forecast (Million $)
| Transportation | Logistics and Supply Chain | Manufacturing | Retail | Healthcare | Aerospace and Defense | Agriculture | Others
2017 | 869.2 | 967 | 541.6 | 1783.7 | 735.2 | 497.7 | 587.1 | 1919.7
2020 | 937.4 | 1055.8 | 586 | 1912.3 | 794.3 | 534.9 | 634.5 | 2034.5
2022 | 975 | 1107.7 | 610.8 | 1980.8 | 827.2 | 555.3 | 661 | 2090.9
2025 | 1134.3 | 1305.8 | 712.8 | 2290.1 | 964.1 | 644.6 | 770.8 | 2388.7
2028 | 1459.1 | 1702.5 | 919.6 | 2927.1 | 1242.3 | 828 | 993.6 | 3016.7
2031 | 2072.2 | 2451.2 | 1309.7 | 4130.4 | 1767.3 | 1174.6 | 1414.1 | 4205.5
RFID only fits limited scenario, does not meet key industry requirements
Continuous coverage
1-3m positioning
99.99% inventory success
Source: Global RFID Sensor Market, Global Industry Analysis, Size, Share, Growth, Trends and Forecast, 2021–2031
RFID only fits short range single-point operation, still needs human resource






RFID does not support large area continuous coverage, infeasible to meet industry demand of whole-process automation
 |  | Customer | Use case | Requirement | Desired technology readiness | Values
Local area | Company A | White goods producer | Real-time visible production and logistics | Autonomous inventory, 99.99% success, 1-3m positioning, Extreme low cost tag | 2024 | Reduce logistics costs Reduce production line shutdown
 | Company B | Automobile manufacturers | Warehousing inventory and material container management |  | Urgent, as early as possible | 
 | Company C | E-commercials | Account management |  | ~2024 | Improve inventory efficiency
Wide area | Company A/C/D | Logistics and distribution | Real-time property monitoring and quality tracing | Continuous coverage, battery-less, No manual maintenance, 99.99% success | ~2024 | Real-time tracking of vulnerable goods and valuable assets
 | Bureau of city management | City Infrastructure | Health monitoring |  | Urgent, as early as possible | Battery-less, higher safety Save cost as no manual maintenance
 | Company E | Smart grid | Sensor data collecting |  | 2025 | 

## Slide 4
  Missing the opportunity in the fast-growing market would lead to high barriers to entry for 3GPP in the future
  Industries are also looking for other non-3GPP based solutions for long-life maintenance-free device, such as WiFi, Bluetooth, and LoRa
  AMbient Power (AMP) is “a new TIG/SG within the IEEE 802.11 working group that will address the problem of support of Ambient Power communication in 802.11 network” [1]
Competitors will not wait!
    AMP TIG has been started and completed in July 2022 and Mar 2023, respectively
    AMP SG was approved in Mar 2023, with first meeting to be in May 2023
  Many start-ups put efforts in Bluetooth Low Energy based batteryless device
  LoRa nano-tag is “a disposable, ultrathin and low-cost tag that can be integrated into disposable systems or attached to assets to communicate a specific trigger of an event” [2]
  Once the huge amount of connections been captured, it is uncertain 3GPP technologies can regain the market share
  Opportunity exists for a new 3GPP IoT segment below NB-IoT, supporting long-life batteryless devices
  Currently, RFID is only suitable for personal area or gate-type coverage due to limited communication range
  E.g. RFID is not attractive to “track assets around factory sites” [3]
  The device power consumption of WiFi and BLE is still incompatible with energy harvesting
  The key point for the success of Ambient IoT is to support 5G cellular network coverage based on batteryless device
[1] “Status of IEEE 802.11 Ambient Power (AMP) TIG/SG” (https://www.ieee802.org/11/Reports/amp_update.htm)
[2] “Disposable LoRa enabled Nano-tag for IoT Applications”, IoT adda, (http://www.iotadda.com/disposable-lora-enabled-nano-tag-for-iot-applications/)
[3] 5G FOR SMART MANUFACTURING (GSMA report, April 2020) — INSIGHTS ON HOW 5G AND IOT CAN TRANSFORM INDUSTRY, PA Knowledge Limited, April 2020

## Slide 5
Rel-19 Ambient IoT Should Support both Indoor and Outdoor Deployment
  Indoor / Personal scenarios from SA1 study
  Functionalities
  Inventory: 10 use cases
    Automated warehousing, automobile manufacturing, logistics, supply chain, etc.
  Sensors: 6 use cases
    Smart homes, smart agriculture, smart pig farm, etc.
  Positioning: 6 use cases
    Lost item finding, personal belonging finding, positioning in shopping centre, museum guide, etc.
  Command: 5 use cases
    Electronic shelf label, elderly health care, device deactivation, etc.
  Connections
  Cost for each connection should be sufficiently low to be comparable with e.g. barcode and RFID, especial for inventory
  Main motivation for (semi-)passive device
  Outdoor scenarios from SA1 study
  Functionalities
  Inventory: 4 use case
    Airport terminal / shipping port asset tracking, medical instruments management, etc.
  Sensors: 5 use cases
    Smart grid, forest fire monitoring, manhole cover safety monitoring, bridge health monitoring, dairy farming, etc.
  Positioning (in public area): 3 use cases
    Personal belonging finding, remote lost item finding, etc.
  Command (in public area): 4 use cases
    Controller in agriculture, elderly health care, device deactivation, etc.
  Connections
  The connection may be with higher value, especially for sensors
  Main motivation for active device

## Slide 6
RFID
Coverage: 8m*8m
Ambient IoT
Coverage: 18m*18m
Positioning:1~3m@90%
Ambient IoT 20~30m
RFID~10m
RFID in dock area
6581 Readers and 800,000 tags
1300 Readers and 800,000 tags
30 Readers @ 20 gates; 800,000 tags
To cover a total area of 1300*18m*18m, the cost of RFID and Ambient IoT are as follows
RFID has been commercially deployed in the dock area :
  Short communication range is not a problem as all tags go through gates
Commercial deployment of RFID in dock area of factory
Typical plant covers a total area of around 400,000 ~ 600, 000 square meters
Extension to all areas of factory
1
2
1
2
223X | 7.6X | 4.6X | 235.2X
44X | 7.6X | 4.6X | 56.2X
Equipment | Maintenance | Tag | Total
Equipment | Maintenance | Tag | Total
X | 2X | 4.6X | 7.6X
Ambient IoT for Intralogistics in Automobile Manufacturing
Dock
Fast Reading for non-stop forklift
100 tags/s
In/out detection of forklift
Tag moving direction
Floor, Sorting area, Production line
Block detection of containers
Positioning to detect the block in which a dedicated tag is placed, with accuracy of 1~3 meters
Seamless coverage
Simple deployment and network planning
Real-time inventory
Thousands of tags read in a few minutes
RFID is only suitable to be deployed in dock area, a small part of factory
Seamless coverage and positioning are key requirements for mature solution

## Slide 7
Bridge Health Monitoring
Wide Area Network: City Infrastructure Health Monitoring, Battery-less Enables Safety and Reduces Manual Maintenance
Customer request:
No manual maintenance at least 10 years. Low cost tag
<100Byte@per hour/day
POC in 2023, expect commercialization in near future
Temperature monitoring of ultra-high voltage power equipment
Customer request:
No manual maintenance at least 10 years. Low cost tag
Property assessment :
  <50B@per day
  2024 pre-commercial, 2025 commercialization in small-scale
AC current transformer
AC switch
AC breaker
Disadvantages of other solutions
Machine vision: conditions such as rain or night monitoring result low accuracy which is not enough to meet the demands
Wired sensor: reliable, but the layout cost is high and complex, and the cost of monitoring equipment up to be hundreds of thousands RMB
Bureau of a city management in China
Smart gird
Disadvantages of other solutions
Infrared solution: heat map based on surface temperature measurement which cannot directly locate the accurate point, low accuracy
The maintenance of ultra-high voltage equipment is complicated and the labor cost is high (it cannot be monitored under working conditions)
Types of sensor used for monitoring status of bridge: displacement, strain, deflection, tilt, cable tension, temperature, acceleration, wind direction and speed, corrosion, crack etc.
various sensors

## Slide 8
Disposable plastic foam boxes are widely used in the distribution of agricultural products
Wide Area Network：E2E Tracking and Status Monitoring of Returnable Transport Items
Current situation:
~400,000 disposable plastic foam crates are used per day in one wholesale market
Top requests: enable recycling crates monitoring, cost and efficiency improvement, food safety and tracing
Recycling crates E2E management
Future:
Recycling crates as manageable assets
E2E recycling management includes automatic stock in/out inventory and status tracking
Global returnable transport items (crates and pallets) could be up to hundreds of billions
Example use case in China
UC1: Stock in/out
Inventory
UC2: Status tracking during Transport
UC3: Checkpoint
Stock in/out, automatic inventory accuracy 99.99%
Automatic reading of crates in check point, accuracy 99.99%
Continuous monitoring and update of crates’ temperature, location etc.
Packaging
Farm
Transport
Processing
Re-load
Shelves
Disposal
Recycling crates
tag attached
Enabled by Ambient IoT

## Slide 9
The difference between passive and semi-passive lies in the device implementation e.g. without or with power amplifier.
Same air interface for passive and semi-passive device is feasible and recommended.
(Semi-)Passive device is preferable for indoor scenarios due to the lower power consumption and cost, while active device may be the only choice to reach the effective communication range for direct link to basestation in outdoor scenarios.
Rel-19 Ambient IoT should include device types for both indoor and outdoor deployments.
Rel-19 Ambient IoT Should Include (semi-)passive and active devices
Device A & B (Passive)
Device B (Semi-passive)
Device C (Active)
Tag
BS
Transmitted signal from tag
Tag
BS
Backscattered signal
Carrier wave
Tag
BS
Backscattered signal
Carrier wave
  Common: RF envelope detection for receiving & Backscattering for transmitting
  Difference: without and with power amplifier for passive and semi-passive device, respectively
  Ultra-low power RF LO: no need of external CW
  Heterodyne transceiver: actively transmit RF signal

## Slide 10
Rel-19 Ambient IoT Focus on Licensed FDD Spectrum
Licensed FDD spectrum has the following advantages for Ambient IoT
      Communication reliability and service availability in licensed spectrum is always higher than unlicensed spectrum
        Unlicensed spectrum has low transmit power, and very limited interference management
      FDD supports larger coverage than TDD, while the tag activation threshold does not vary with frequency band
        TDD has higher carrier frequency → smaller coverage
        TDD indoors has no additional beamforming gain in micro/pico-cells
      FDD has better compatibility with ambient IoT traffic patterns than TDD
        Ambient IoT UL load is much higher than DL, e.g. 800 bits of sensing info vs. tens of bits for DL control
      FDD allows lower tag power consumption and complexity than TDD
        Lower frequency bands than TDD allows lower power consumption in RF components
        TDD requires rapid UL/DL switching which adds complexity to baseband processing

## Slide 11
Topology (4): direct link to UE
Topology (1): direct link to basestation
Topology (2): relay
Topology (3-1): Assisted data transmitting to device
Topology (3-2): Assisted data receiving from device
Rel-19 Ambient IoT Focus on the RAN Topology of Direct Link to BS
  Topology (1) is the baseline of cellular network, which is essential for high service availability and reliability in large/wide areas.
  Rel-19 Ambient IoT focuses on Topology (1), with forward compatibility to the other topologies.
    The physical signals and higher layer signaling processed by Ambient IoT device, including transmitting and receiving, should be the same
  The other connectivity topologies can then be considered in later releases, where the differences may focus on the connections between BS/intermediate or assistant node/UE/CN/server

## Slide 12
Summary
  RAN1-led SI + WI in Rel-19
    Need to consider carefully the amount of specification work and commercial relevance of Rel-19 Ambient IoT features
  Tag categories: Target both (semi-)passive and active device tags in Rel-19
    (Semi-)Passive device can be more preferable for indoor use cases, e.g. intralogistics in manufacturing, warehousing, supply chain, etc.
    Active device may be the only choice for direct link to outdoor BS, e.g. monitoring in smart city / agriculture / livestock farming, asset / personal belonging tracking, etc.
  Spectrum: Target licensed FDD in Rel-19
    Higher service availability and reliability in licensed spectrum
    Longer effective range in lower frequency bands
    Lower device power consumption and complexity in lower frequency bands
    More compatible to Ambient IoT traffic e.g. UL-heavy
  RAN connectivity: Target gNB direct bidirectional communication with Ambient IoT device in Rel-19
    Baseline of cellular network to meet high service availability and reliability in large or wide areas
    With forward compatibility to the other topologies
      Physical signals and higher layer signaling processed by Ambient IoT device, including transmitting and receiving, should be the same

## Slide 14
Workload of Normative Work for Multiple Device Categories Can be Minimized
  The workload of standardizing both passive and active device can be ≤1.2x of only standardizing active device.
Physical layer |  | Additional work for passive compared to active? | Notes
DL | FEC | Possibly | [Neither may need FEC]
 | Modulation | No | 
 | Line code | No | 
 | Preamble | Yes | 
 | Reference signal | No | 
 | Repetition | No | 
 | Signal bandwidth | No | Same BW assumed
 | SSB | No | SSB only for active
 | Carrier wave signal | Yes | Needed for passive
UL | FEC | No? | [Could be same]
 | Modulation | Possibly | 
 | Line code | No | 
 | Preamble | Possibly | 
 | Reference signal | No? | 
 | Repetition | No | 
 | Signal bandwidth | No | 
 | Power control | No | PC only for active
Higher layer functions | Needed for active? | Needed for passive? | Notes
System information | Yes | No | 
Paging | Yes | Yes | 
Connection establishment | Yes | Yes | Simplified (e.g., no DO for passive)
Connection control & Associated signaling | Yes | Yes | Simplified
Acknowledgement (e.g. HARQ) | Yes | Yes | 
Mobility functionality | Yes | No | 
Transfer of application data | Yes | Yes | 
Power saving mode | Yes | No | 
  Compact design is expected for both active and passive device, due to the strict constraints on device power consumption and complexity
  For the active device design, benefits can be expected from evaluations of LP-WUS e.g., modulation, waveform, synchronization
  Much of passive device design is either removed or simplified from active device design, i.e. standardizing active devices completes a large part of the effort for passive devices without parallel or additional work streams
  Device A (passive w/o energy storage) and Device B (passive w/ energy storage) can share the same air interface
  The differences lie in the implementation of device, especially the RF front-end, e.g., w or w/o power amplifier, capacitor or supercapacitor