## Slide 1
Huawei, HiSilicon
Scope of LP-WUS in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230408
Taipei, June 15 - 16, 2023

## Slide 2
LP-WUS in Rel-19: Objectives
    Signal design of LP-WUS
LP-WUS is at least used to indicate PDCCH monitoring
The activation/deactivation of LP-WUS monitoring is in explicit way or implicit way, which is known by gNB
Paging information is carried by LP-WUS, as well as other information, e.g. ETWS, SI change, cell/area ID
At least serving cell measurement is performed by LP-WUR, which can be based on periodically LP-SS.
    LP-WUS for CONNECTED mode
    Low-power synchronization signal
    LP-WUS for IDLE/INACTIVE mode
Specify harmonized OOK+FSK to achieve FSK benefits on time/frequency error robustness, etc.
Sequence based modulation is supported on top of OOK and FSK to improve demodulation performance
Low precision LO used by LP-WUR has frequency error as high as 200 ppm. It causes high frequency error and accumulates timing error rapidly.
It is desirable the modulation scheme is robust against both frequency/time errors.
It is also important that the receiver is able to assist LO perform frequency error correction.
Support of periodic low power synchronization signal for
  Time/frequency correction for LP-WUS demodulation
  Further enabling of RRM measurement by LP-WUR
Coverage performance is degraded than MR due to large noise figure and 1Rx reception
Coverage enhancements are supported, e.g., channel coding ( polar or high-rate error correction codes), time domain interleaving, etc.
The frequency/time errors due to low precision LO cause demodulation performance degradation or link failure if not corrected.
LP-WUS contributes significant power saving gain for idle/inactive mode
To maximize power saving gain, it should avoid to switch back to MR for RRM measurement frequently.
PDCCH monitoring brings a significant part of power consumption in CONNECTED mode.
Motivations
Proposals
Directions

## Slide 3
R19 LP-WUS/WUR: Waveform/modulation
  FSK is robust to time/frequency error and the related FSK receiver can naturally perform frequency error estimation
  Harmonized OOK and FSK provides balances between frequency diversity gain and robustness against time error
  Both OOK and FSK can be demodulated based on the same parallel receiver architecture including RF/IF processing, i.e. BPF at low IF to filter out the signal on each channel, followed by envelope detection and ADC
  Optimized waveform, e.g. concentrated waveform, can further improve the performance with respect to timing error etc.
OOK+FSK
x1
xn
y1
yn
REs for legacy NR signal
REs for LP-WUS
IFFT
&
CP
……………
BPF(f0)
BPF(f1)
ED
ED
ADC
ADC
Digital processing
OOK+FSK demodulation
Receiver
Transmitter
  Sequence correlation has better performance if time/frequency are synchronized, e.g. within 1 us and 30kHz frequency error
  LP-WUR can utilize the correlation to improve the performance, or to carry additional information:
    Specify the generation sequence of OOK/FSK waveform  improved performance
    Some information bits can be carried by different sequences (on top of OOK/FSK)  increase data rates;
The waveform/modulation of R19 LP-WUS/WUR
Specify harmonization of OOK/FSK to achieve benefits on time/frequency error robustness, etc.
Sequence based modulation is supported on top of OOK and FSK to improve demodulation performance
OOK
FSK
Envelope detector
Receives bit stream 1
I/Q receiver
Receives both bit stream 1&2
Bit stream 1
(OOK/FSK modulated)
Bit str 2
Bit str 1: 0 1
Bit str 1: 0 1
Bit str 2
BPF
ED
ADC
ADC
ADC
Supporting harmonized OOK and FSK
Sequence based modulation on top of OOK and FSK
Bit stream 2
(Sequence modulated)

## Slide 4
R19 LP-WUS/WUR: Coverage and synchronization design
The coverage performance of LP-WUS is limited by
  High noise figure (e.g. 15 dB)
  1 RX
  Lack of sophisticated signal processing
The following enhancements can be considered at least to match coverage requirement with Msg3
  Power boosting
  Time domain method, e.g. interleaving
  Frequency domain method, e.g. frequency hopping
  Channel coding, where decoding should be low complexity and low power, e.g. polar, or high-rate error correction codes
  Code domain method, e.g. spreading code of LP-WUS
When polar coding with 1/4 coding rate is used together with frequency hopping, 8.5 dB gain can be achieved.
Coverage enhancements of LP-WUS
Synchronization signal for LP-WUS
BLER vs. SNR of UE ID transmission by a rate-1 error correction code based on identification coding.
8.5dB gain
Periodic SYNC (LP-SS) is preferred due to the following advantages:
  Reliable sync source even with sparse traffic
  Reliable source for RRM measurement/triggering switching to MR
  Enable duty-cycle based monitoring of LP-WUS
  Can carry ‘cell specific’ info to reduce overhead
Parallel OOK/FSK receiver is capable of frequency error estimation and correction by utilizing its multiple branches
Periodicity requirement: 200~400ms is enough for T/F error correction
The resource overhead of LP-SS is 0.13%, and the additional network consumption introduced by LP-SS is 0.08%
  The periodicity of LP-SS is 320ms, BW of LP-SS is 5MHz, and LP-SS is FDMed with SSB/SIB1; channel BW is 100MHz.
Receiver architecture to support frequency error estimation/correction
95 probability the residual frequency error can be within ±2.5 ppm.

## Slide 5
R19 LP-WUS/WUR: IDLE and INACTIVE modes
UE
gNB
WUR
WUS(UE specific paging information）
trigger
Perform random access
MR
UE
gNB
WUR
LP-WUS (group/subgroup）
trigger
If paged, perform random access
MR
if not paged, unnecessary wake-up leads to power wasting
Legacy paging operation
UE specific paging info
UE group/subgroup paging info
OR
ETWS information
Reduce ETWS latency
SI change information:
Reduce the latency of SI update
Cell area ID:
Cell ID used to distinguish the cell
Tracking area/RAN area ID to let UE be synchronized with network
Serving cell: Performed by LP-WUR, which can be based on periodical LP-SS.
New metrics needs to be defined for new waveform, e.g. LP-RSRP and LP-RSRQ.
Neighbor cell: two options can be considered
Option 1: Performed by MR if the serving cell results satisfy certain conditions, e.g. LP-RSRP is less than a threshold.
Option 2: Performed by LP-WUR, where interference from different cells should be minimized
MR to LP-WUR: LP-WUS is configured by gNB
LP-WUR to MR:
Indicated over LP-WUS
A fallback mechanism: when the channel condition of LP-WUS is not sufficient
Paging information
Other information
Switch between MR and LP-WUR
RRM measurement

## Slide 6
R19 LP-WUS/WUR: CONNECTED mode
Reuse the signal(s) design of LP-WUS for IDLE/INACTIVE mode, i.e. the same waveform/modulation design as in IDLE/INACTIVE mode to enable the same receiver architecture
Reuse the design of LP-SS for IDLE/INACTIVE mode, e.g. the sequence for LP-SS, the periodicity.
LP-WUS is at least used to indicate PDCCH monitoring
UE monitors LP-WUS (by LP-WUR) instead of PDCCH (by MR) to reduce power consumption
The activation/deactivation of LP-WUS monitoring is in explicit way or implicit way, which is known by gNB
At least UE power-saving techniques in time domain are considered, e.g. C-DRX, DCP, PDCCH adaptation
LP-WUS design for connected mode
Functionality and basic procedure
Relationship with legacy UE power saving techniques