## Slide 1
Huawei, HiSilicon
Sidelink and V2X enhancements in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230409
Taipei, June 15 - 16, 2023

## Slide 2
Contents
Overview (P3)
Technical considerations
SL operation in FR2 spectrum, including FR2-2 unlicensed spectrum (P4)
SL carrier operation, including aggregation of FR1 unlicensed CCs, aggregation of FR2 unlicensed CCs (P5)
Proposals (P6)

## Slide 3
Overview
Rel-19 SL should continue to leverage the use of wider bandwidth in new spectrum for ~Gbps communications
  Specify SL FR2, starting from the Rel-18 study phase outputs
    Include FR2-2 unlicensed spectrum
  Specify a full version of SL carrier aggregation, not limited to start from the Rel-18 V2X CA

## Slide 4
Use Cases | Characteristic parameter (KPI) |  | 
 | Max Allowed E2E latency | Service bit rate: user-experienced data rate | Reliability
Gaming or Interactive Data Exchanging NOTE: Communication includes direct wireless links (UE to UE). | 10ms | 0.1-[1] Gbps supporting visual content (e.g. VR based or high definition video) with 4K, 8K resolution and up to120fps content. | 99.99%
Consume VR content via tethered VR headset NOTE: The performance requirement is valid for the direct wireless link between the tethered VR headset and its connected UE. | [5 -10] ms | 0.1-[10] Gbit/s | [99.99%]
Extra-high data rate short-range direct communication is motivated to support interactive applications (e.g. XR), i.e. KPIs such as high data rate, low latency and high reliability, as per SA requirement.
Motivation
Rel-19 consideration
SL operation in FR2 (incl. FR2-2 unlicensed)
Rel-18 has a SI-only objective for SL FR2 licensed, which was activated for WG discussions starting from Q1 2023.
The study scope only focuses on:
  SL beam management, including beam initial pairing, maintenance, failure detection and recovery, and SL CSI framework.
  Rel-19 can use Rel-18 SI outcome as a starting point to complete normative work for sidelink operation on FR2 spectrum.
In addition to beam management, which is fundamental for operation over mmW spectrum, reliability is also critical. The current NR SL resource allocation, i.e. mode 1 and mode 2, is designed to operate on FR1 spectrum. It is important that sidelink operation on FR2 spectrum can achieve at least the same reliability as that on FR1 spectrum.
Both sidelink mode 1 and mode 2 need be supported on FR2 spectrum, with enhancements to facilitate beam-domain scheduling and sensing for reliability.
Rel-19 should focus on SL FR2-2 (52.6 - 71 GHz) for SL operation, given FR2-2 includes 60 GHz unlicensed spectrum, which is more valuable for commercialization, taking into account the spectrum availability for SL operation.
Further design considerations for FR2-2 unlicensed
  New numerology
  Physical channel (S-SSB/PSCCH/PSSCH/PSFCH) & procedure enhancements
  Channel access for FR2-2 unlicensed including directional LBT, etc.

## Slide 5
Motivation
Rel-19 consideration
SL carrier aggregation
Since the specification of NR sidelink in Rel-16, additional bands/spectrums have been defined/proposed for SL operation, e.g. unlicensed band in both FR1 and FR2.
SL CA is one of the objectives in Rel-18, however, due to workload and TU management, it is activated only late in Rel-18 for WG discussions.
In RAN#99 decided to start CA specification work with a very constrained scope after completion of coexistence objective.
The value of SL CA work in Rel-18 is therefore rather limited and is unsuitable for the majority of use cases, e.g. anything apart from specific V2X applications.
Rel-19 SL CA should not be restricted based on the SL CA work in Rel-18.
In most of spectrum, bands are scattered and non-contiguous. In the unlicensed (FR1 and FR2) bands, much larger bandwidth is available. However, single-carrier operation is too limited for sidelink, and is unable to fully utilize spectrum resources, particularly in the unlicensed band.
 | Rel-19 SL CA | Notes
RA mode | Mode 1 CA Mode 2 CA | SL CA operation should be operational under RA modes.
Band consideration | Intra-band CA in FR1 unlicensed, e.g. n46 Intra-band CA in FR2 unlicensed, e.g. n263 | CCs can be contiguous/non-contiguous for intra-band CA.
Cross-carrier operation | CC1: PSCCH + CC2: PSSCH for unicast CC1: PSSCH + CC2: PSFCH for unicast | This is beneficial for improved reliability, in case of channel access failure, consecutive reception loss, different TX and RX capability, etc.
PCC/SCC differentiation | PCC and SCC differentiation for unicast | Configuration via PC5 RRC for management of PCC/SCC.
Following can be prioritized in Rel-19 for SL carrier aggregation

## Slide 6
Proposals
Proposal 1: Specify enhanced sidelink operation on FR2 spectrum
Specify sidelink beam management.
Specify mode 1 and mode 2 enhancements for improved reliability on FR2 spectrum.
Specify SL operation on FR2-2 unlicensed spectrum.
Proposal 2: Specify sidelink carrier aggregation
Specify CA between FR1 unlicensed CCs, and between FR2unlicensed CCs.
Specify cross-carrier operation.