## Slide 1
3GPP TSG RAN Rel-19 Workshop RWS-230441
Taipei, June 15 – 16, 2023
Considerations on Ambient IoT Agenda Item: 5
Notes: Pas de S à science, digital science.

## Slide 2
Motivation
Identified use cases not addressed by existing 3GPP LPWA/IoT technology
  Inventory (automated warehouse, automobile manufacturing, …)
  Sensors (Smart agriculture, smart grid, …)
  Positioning (Asset tracking, indoor positioning,…)
  Command (Device activation/deactivation,…)
Enabling ultra-low cost battery-less devices within 3GPP cellular technology has a lot of benefits
  Massive number of connections
  Improved coverage compared to RFID
  Devices managed within 5G cellular network

## Slide 3
Background
Ambient IoT device complexity
Observations
  Ultra-low power reception for Devices B and C
    Non-coherent receivers with envelope detection
    Limited processing capabilities (channel decoding, …)
  Two types of UL transmission
    Back-scattering (Devices A & B) of ambient RF source
    Independent transmission (Device C)
  Devices B & C have similar power consumption targets as LP-WUR (< 1 )
Property | Device A | Device B | Device C
Tx/Rx | Tx | Tx or Tx/Rx | Tx/Rx
Energy storage | None | E1 | E2 (E2>E1)
Independent Tx | No | No | Yes
Power consumption | <[1-10] | Hundreds of | <[1-10]
Property | Device A | Device B | Device C
Tx/Rx | Tx | Tx or Tx/Rx | Tx/Rx
Energy storage | None | E1 | E2 (E2>E1)
Independent Tx | No | No | Yes
Power consumption |  |  | 

## Slide 4
Proposals
Study PHY layer aspects for UL and DL of Ambient IoT devices
  DL waveform and channel coding for ultra low-power reception
  UL waveform & coding for low-power transmission
  PHY security aspects, e.g. secure UL transmission
  L1 procedures (start/stop of transmission/reception, synchronization, measurements,…)
Consider synergies with SI on low-power wake-up radio (LP-WUR)
  DL waveform design for low-power/complexity receiver
    E.g. reception of OOK/FSK waveform with envelope detection
  Measurements performed by ultra-low power device
  Evaluation results for different receiver architectures as starting point (Device types B & C have similar power consumption targets as LP-WUR)