## Slide 1: WF on UE Coverage Improvements
CMCC, Vodafone
3GPP TSG RAN WG1 #74 R1-133956
Barcelona, Spain, 19th – 23rd August 2013
Agenda 7.2.4

## Slide 2: Proposal
UE coverage improvement target is to strive to maintain same MCL between TDD (at least UL-DL config. 1 and 2) and FDD after coverage improvements
  Meanwhile strive to have common TDD/FDD solutions
  UE capability indicator for enhanced coverage will not need TDD/FDD differentiation

## Slide 3
Physical channel name | PUCCH (1A) | PRACH | PUSCH | PDSCH | PBCH | SCH | PDCCH (1A)
MCL (FDD) | 147.2 | 141.7 | 140.7 | 145.4 | 149.0 | 149.3 | 146.1
MCL (TDD) | 149.4 | 146.7 | 147.4 | 148.1 | 149.0 | 149.3 | 146.9
Note1: eNB is assumed with 2 Tx and 2 Rx in FDD systems. Note2: eNB is assumed with 8 Tx and 8 Rx in TDD systems. Note 3: PHICH is neglected and the function of PHICH can be implemented by PDCCH in case of cell edge. |  |  |  |  |  |  | 
Channel | PUCCH (1A) | PRACH | PUSCH | PDSCH | PBCH | SCH | PDCCH (1A)
MCL (FDD) | 147.2 | 141.7 | 140.7 | 141.4 | 145 | 145.3 | 142.1
MCL (TDD) | 149.4 | 146.7 | 147.4 | 144.1 | 145 | 145.3 | 142.9
reference
MCL for category 1 UE in TR 36.888
MCL for low complexity UE in TR 36.888