## Slide 1: WF on PRACH power ramping in dual connectivity
Ericsson, NEC, Nokia Corporation, Nokia Networks, Qualcomm, LGE, Samsung, Huawei, HiSilicon
R1-145337
3GPP TSG RAN WG1 #79
San Francisco, USA, 17th – 21st November 2014
Agenda item 6.2.2

## Slide 2: Background
Alt.1: Not to increase it if PRACH is dropped
Alt.2: Not to increase it if either PRACH is dropped or power-scaled
Alt.3: No change in the current spec – increase it even if PRACH is dropped or power-scaled
Alt.4: It would increase the counter but in calculating the new power, maximum power of previous PRACH is taken into account
Alt.5: It is up to UE implementation to increment or not to increment in case PRACH is power-scaled including it is dropped
Alt.6: Not to increment it if PRACH is dropped; it is up to UE implementation to increment or not to increment in case PRACH is power-scaled

## Slide 3: Proposal
Alt.6:
  Not to increment preamble power if PRACH is dropped;
  It is up to UE implementation to increment or not to increment in case PRACH is power-scaled
It is up to RAN2 to decide how to capture in specification
  RAN1 does not discuss handling of counter related to RACH preamble