## Slide 1: WF on coverage enhancement targets for MTC
Ericsson, AT&T, InterDigital, MediaTek, NEC, Nokia Networks, Nokia Corporation, Orange, Panasonic, Qualcomm, Sierra Wireless, Sony, Verizon, ZTE
R1-145348
3GPP TSG RAN WG1 #79
San Francisco, USA, 17th – 21st November 2014
Agenda item 6.3.1.1.1

## Slide 2: Proposal
For FDD, the target MCL is 155.7 dB for Rel-13 low complexity UEs as well as other UEs utilizing the coverage enhancements.
For TDD, the target MCL is 155.7 dB [for UL-DL configuration 1] for Rel-13 low complexity UEs as well as other UEs utilizing the coverage enhancements.
The above targets are assuming that the maximum transmission power P [dBm] of the new UE power class is ≥20 dBm.
  If RAN4 agrees that P < 20 dBm, the target uplink MCL for the new UE power class is reduced correspondingly to 155.7 - (20 - P) dB.
When applicable, the MCL targets are valid under the assumptions in TR 36.888 subclauses 5.2 and 5.2.1.2
  The reference system has 10 MHz system bandwidth and no power boosting.