## Slide 1: Way forward on the number of antenna element rows M and columns N for Phase 2 evaluations For: Decision AI: 6.3.3.1
Ericsson, Intel, ZTE, AT&T
3GPP TSG-RAN WG1 #79 R1-145357
San Francisco, USA, November 17-21, 2014

## Slide 2: Background
Studied array antennas can have tall (M>N), wide (M<N) and square (M=N) apertures
    M is the number of rows of antenna elements
    N is the number of columns of antenna elements
Several companies have observed large gains with the wide apertures compared to tall
  Observations are that N>4 gives significant improvement compared to N=4 in the studies scenarios when area (N*M) is kept constant
The antenna orientation used in practice depends on installation circumstances, expected traffic distribution etc
  Installations with wide orientations exists already today despite lack of horizontal beamforming.
A study item should not artificially exclude relevant and promising antenna configurations

## Slide 3: Way forward
The number of rows (M) and columns (N) of antenna elements for Phase 2 evaluations in this SI are
  M,N ={1,2,4,8,16}
  max(M*N) = 32