## Slide 1: Proposal for RAN4 guidance on retuning time
Huawei, HiSilicon
R1-145366
3GPP TSG RAN WG1 #79
San Francesco, USA, 17th – 21st Nov 2014
Agenda item 6.3.1.1.2

## Slide 2: Background
WID points
  Reduced UE bandwidth of 1.4 MHz in downlink and uplink.
    Bandwidth reduced UEs should be able to operate within any system bandwidth.
    Frequency multiplexing of bandwidth reduced UEs and non-MTC UEs should be supported.
    The UE only needs to support 1.4 MHz RF bandwidth in downlink and uplink.
    The allowed re-tuning time supported by specification (e.g. ~0 ms, 1 ms) should be determined by RAN4.
RAN4 is tasked to investigate retuning time in 1Q 2015
  ~0ms corresponds to an implementation of bandwidth reduction composed of wideband RF filter and narrowband baseband
  1ms corresponds to an implementation of bandwidth reduction composed of narrowband RF and baseband

## Slide 3: Observation
RAN4 needs no guidance to begin their investigation into retuning time
If guidance is desired, RAN4 could be provided the following
  Retuning is necessary as retuning is supported between the narrowband for common messages and the narrowband for unicast
  The majority of companies in RAN1 consider an implementation composed of narrowband RF and baseband (and e.g. 1ms retuning time)
  Some companies in RAN1 consider an implementation composed of wideband RF and narrowband baseband (and e.g. ~0ms retuning time)
  In the discussion of retuning time and multiplexing of UE, RAN4 should also discuss DC subcarrier locations and duplex distance issues for FDD