## Slide 1: WF on SIBs for MTC
Huawei, HiSilicon, ALU, ASB, CATT, Ericsson, Intel, InterDigital, MediaTek, NEC, NTT DOCOMO, Sony, Sierra Wireless, ZTE
R1-145392
3GPP TSG RAN WG1 #79
San Francisco, USA, 17th – 21st Nov 2014
Agenda item 6.3.1.1.2

## Slide 2
Proposed agreement:
RAN1 will make observations on the efficiency of different TBS support for broadcast
RAN1 recommends that RAN2 consider introducing new SIB(s) for Rel-13 low complexity UEs in normal and enhanced coverage.
  Rel-13 low complexity UEs do not need to read legacy SIBs
  A Rel-13 low complexity UE will not be able to
    Receive SI-messages in more than 6 contiguous PRBs
    Receive PDCCH which schedules transmissions of legacy SIBs in system BW greater than 1.4 MHz
  Maximum TBS, SIB Exact size(s) and time-domain aspects including e.g. SI-windows and SIB update rate(s) can be decided jointly with RAN2
  This does not preclude the possibility of using a subset of the new SIB(s) for normal coverage or enhanced coverage
  FFS whether UEs of other category in enhanced coverage can use this SIB(s)
Send the above recommendation and the WA from RAN1#78bis on TBS in an LS to RAN2