## Slide 1: Way forward on further details of evaluation methodology for MUST
MediaTek, CHTTL, III, ITRI, NTT DoCoMo, ZTE
3GPP TSG RAN WG1 #81
Fukuoka, Japan, 25th – 29nd May 2015
Agenda item 6.2.7.2
R1-153442

## Slide 2: Proposals for UE Receiver Assumptions
  In baseline scheme,
    MMSE-IRC is assumed for inter-cell interference suppression
    MMSE-IRC is assumed for inter-spatial-layer interference suppression
  In MUST scheme,
    For all users, MMSE-IRC is assumed for inter-cell interference suppression
    For MUST near-users the following is assumed
      Either SLIC/R-ML or CWIC for intra-spatial-layer interference cancellation
      MMSE-IRC for inter-spatial-layer interference suppression
    For other users, MMSE-IRC is assumed for inter/intra-spatial-layer interference suppression
  Each company should describe UE receiver assumptions in details if other UE receiver assumptions are applied in MUST scheme

## Slide 3: Proposals for System-level Evaluation
  Baseline scheme is defined as follows
  2x2: CRS-based SU-MIMO transmission schemes
  Other antenna configurations: DMRS-based SU/MU-MIMO transmission schemes with dynamic switching
  Release 12 dual codebook is used for 4Tx
  Baseline and MUST schemes should be compared under the same packet arrival rate corresponding to the targeted RU for the baseline scheme
  For MUST evaluation, system-level performance metrics should include
    5/50/95%ile and mean user perceived throughput (UPT)
    Ratio of served cell throughput over offered cell throughput
Notes: No latency

## Slide 4: Proposals for System-level Evaluation
  Each company should provide the following information together with system-level results
    Throughput versus SNR curves using link-level simulation and link-to-system mapping for the validation of link-to-system mapping
    Detailed method of link-to-system mapping applied in the system-level evaluation
    Assumptions on CSI feedback and network assisted signaling

## Slide 5: Proposals for Remaining Details
  For antenna configurations, the following is used for evaluation
    Mandatory: 2Tx/2Rx, 4Tx/2Rx
    Optional: 4Tx/4Rx, 8Tx/2Rx
  For UE speed, the following are used for evaluation
    Outdoor UEs: 3, 60 km/hr
      Imperfection due to Doppler effect should be considered for high-mobility case
    Indoor UEs: 3 km/hr