## Slide 1: WF on UL LBT for LAA
Ericsson, Motorola
3GPP TSG RAN WG1 #82 R1-154831
Beijing, China
24th – 28th August 2015
Agenda item: 7.2.4.1
Document for decision

## Slide 2: Proposal
For self-carrier scheduling, one or more of the following UL LBT procedure should be supported
  A CCA duration of 25 us before the transmission burst
    The sensing duration can be less than the CCA duration
    FFS whether the transmission burst starts at the UL subframe boundary or after the UL subframe boundary
  A category 4 LBT scheme with a defer period of 25 µs including a defer duration of 16 us followed by one CCA slot, and a minimum and maximum contention window size of 1 and 3, respectively
    The random backoff counter is generated at the eNB and is signalled to the UE
  FFS: Transmission without LBT when UL transmission burst follows DL transmission burst with a gap of at most 16 µs between the two bursts

## Slide 3: Proposal
For cross-carrier scheduling, one or more of the following UL LBT procedure should be supported
  A CCA duration of 25 us before the TTI
    The sensing duration can be less than the CCA duration
    FFS whether the TTI starts at the subframe boundary or after the subframe boundary
  A category 4 LBT scheme with a defer period of 25 µs including a defer duration of 16 us followed by one CCA slot, and a minimum and maximum contention window size of 1 and 3, respectively
    The random backoff counter is generated at the eNB and is signalled to the UE