## Slide 1: CSI-Process Reporting Class B for EB/FD-MIMO
CATT, AT&T, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell,
CMCC, Ericsson, Huawei, Nokia, Qualcomm,
NTT DOCOMO, Samsung, ZTE
3GPP TSG-RAN WG1#82 R1-154902
Beijing, China, August 24-28,2015
Agenda Item: 7.2.5.1.2

## Slide 2: Agreement
A CSI-process can be configured with either of two CSI reporting classes
  Class A: UE reports CSI according to W=W1W2 codebook based on {[8],12,16} CSI-RS ports
  Class B: UE reports L port CSI assuming one of the four alternatives below
      Alt.1: Indicator for beam selection and L-port CQI/PMI/RI for the selected beam. Total configured number of ports across all CSI-RS resources in the CSI process is larger than L.
      Alt.2: L-port precoder from a codebook reflecting both beam selection(s) and co-phasing across two polarizations jointly. Total configured number of ports in the CSI process is L.
      Alt.3: Codebook reflecting beam selection and L-port CSI for the selected beam. Total configured number of ports across all CSI-RS resources in the CSI process is larger than L.
      Alt.4: L-port CQI/PMI/RI. Total configured number of ports in the CSI process is L. (if CSI measurement restriction is supported, it is always configured)
      Note: A “beam selection” (whenever applicable) constitutes either a selection of a subset of antenna ports within a single CSI-RS resource or a selection of a CSI-RS resource from a set of resources
      Note: The reported CSI may be an extension of Rel.12 L-port CSI
      Details such as possible values of L are FFS
      Further down-selection/merging of the four alternatives is FFS
  Study further for CSI measurement restriction

## Slide 3: Proposal
Study the following aspects for CSI-process reporting class B, including but not limited to
  Number of antenna ports L for CSI (e.g., 2, 4, 8)
  Class B Alt-1: (L-port CSI, total CSIRS ports > L)
    Beam selection indicator (BI) definition, e.g. RSRP or CSI based, wideband vs. subband, short-term vs. long-term
    BI bitwidth (related to K)
    Support for rank>2 UE specific beamforming
    UCI feedback mechanisms on PUCCH/PUSCH
  Class B Alt-2: (L-port CSI, total CSIRS ports = L)
    Codebook for beam selection and co-phasing (either derived from legacy codebook(s) or codebook components, or newly designed)
      Along with the associated PMI (e.g. assuming W = W2 in the newly designed or legacy codebook)
    UCI feedback mechanisms on PUCCH/PUSCH
    Class B Alt-3: (L-port CSI, total CSIRS ports >L)
      Codebook for beam selection and CSI
        PMI contains the information of selected beam and the precoding matrix for the L-port within the selected beam
      UCI feedback mechanisms on PUCCH/PUSCH
    Class B Alt-4: (L-port CQI/PMI/RI)
      Measurement restriction mechanism; may be also applicable to Alt-1 to 3.
  Other aspects not precluded