## Slide 1: WF on Physical Channel Timing Relationships
Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, [Ericsson], [Sequans], [Marvell], …
R1-154947
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th - 28th August 2015
Agenda item 7.2.1.1

## Slide 2: Proposal
Timing relationships between M-PDCCH and PDSCH
  In FDD and HD-FDD with cross-subframe scheduling, the PDSCH starts in subframe n+k, where n is:
    OPTION A: n is the last subframe of the search space
    OPTION B: n is the last subframe belonging to the last M-PDCCH candidate in the monitored search space
    OPTION C: n is the subframe where the repetitions of the decoded M-PDCCH message ends
    k is defined by previous agreements
Timing relationships between M-PDCCH and PUSCH
  In FDD and HD-FDD, the PUSCH starts in subframe n+k, where n is:
    OPTION A: n is the last subframe of the search space
    OPTION B: n is the last subframe belonging to the last M-PDCCH candidate in the monitored search space
    OPTION C: n is the subframe where the repetitions of the decoded M-PDCCH message ends
    FFS: If k=4 or k=5
  FFS: For HD-FDD multiple DL ACK/NACK responses are bundled over PUSCH.

## Slide 3: Proposal
Timing relationships between PDSCH and PUCCH
  In FDD and HD-FDD, if PDSCH transmission ends in subframe n, PUCCH carrying HARQ-ACK starts in subframe n+k
    FFS: If k=4 or k=5
  FFS: For HD-FDD multiple DL ACK/NACK responses are bundled over PUCCH.