## Slide 1: WF on subframes with MBSFN structure in LAA
Qualcomm, ALU, ASB, Nokia Networks, Huawei, HiSilicon, ETRI, [Panasonic]
3GPP TSG RAN WG1 #82 R1-155012
Beijing, China
24th – 28th August 2015

## Slide 2: Background
LAA may support both CRS and DMRS based TMs
In current LTE, subframes with CRS only in first (two) symbol can be used for DMRS based transmission without CRS overheard thus increasing transmission efficiency.
In MBSFN subframes in LTE, the PDSCH starts from the second symbol.
However, in LAA, we can additionally increase efficiency by starting PDSCH transmission in the second symbol if the control region duration is only one symbol.

## Slide 3: Proposal
Transmission of DL subframes (or TTI) with CRS only in the first (first two) symbol(s) is supported in LAA
  Note: CRS is present in 1/2 symbols when (1 or 2)/4 port CRS is configured
  PDSCH mapping from the second symbol is allowed in such subframes (or TTI)
  This applies to any subframe (or TTI) in a DL transmission burst
    FFS restrictions to ensure fine synchronization. For e.g., first subframe (or TTI) in a DL transmission burst
    FFS configuration/signalling of such subframes (or TTI)
    FFS: partial subframes