## Slide 1: Proposed Harmonized WF on LAA DL LBT ED Threshold Adaptation Rule (Functionality of Detecting On-going 802.11 a/n/ac tx)
Cisco Systems, Broadcom
3GPP TSG RAN WG1 #82bis R1-156360
Malmo, Sweden
5th – 9th October 2015
Agenda item: 7.2.3.1
Document for decision

## Slide 2: Proposal
For the functionality when an LAA eNB is capable of detecting and attempts to detect, for LBT, the presence (including start and duration) of 802.11a/n/ac transmission on the same channel that the LAA eNB intends to transmit on, then
  Detection Threshold for detecting the presence (including start and duration) of 802.11 a/n/ac transmission = -82 dBm in the absence of interference
    Note: This rule does not mandate that an LAA device satisfying above functionality, must apply a detection threshold of -82 dBm, upon detecting another LAA device.
  Baseline maximum single channel ED threshold = -62 dBm (20 MHz, 23 dBm EIRP)
    FFS: other values of maximum single channel ED threshold (subjected to regional regulations)
  Upon detecting presence of an ongoing 802.11a/n/ac transmission (including start and duration), the LAA eNB should regard the channel as busy for the purpose of Cat-4 LBT for the duration of the 802.11a/n/ac transmission