## Slide 1: Way forward on scheduling mechanism for sTTI
Ericsson, Intel, Nokia, Alcatel-Lucent Shanghai Bell
R1-165571
AI 6.2.10.1
3GPP RAN WG 1 #85
23rd – 27th May2016, Nanjing , P.R. China

## Slide 2: Background
To allow full scheduling flexibility and large latency reduction, Downlink Control Information (DCI) needs to be sent for each sTTI.
To minimize control overhead in frequent sTTI, it is beneficial to apply a two-step DCI transmission
  The first step is transmitted on a longer scale
  The second step is transmitted in each sTTI

## Slide 3: Proposal
Two-level DCI is recommended to be supported for sTTI scheduling, whereby:
  DCI for sTTI scheduling can be divided into two types:
    “Slow DCI”: DCI content which applies to more than 1 sTTI, is common for multiple UEs and is carried on legacy PDCCH
    “Fast DCI”: DCI content which applies at least to one specific sTTI and is carried on sPDCCH
    For a sPDSCH or a sPUSCH in a given sTTI, the scheduling information is obtained from the combination of slow DCI and fast DCI