## Slide 1: 3GPP TSG RAN WG1 Meeting #85 R1- 165644 Nanjing, China 23rd - 27th May 2016 Agenda item 6.1.6
WF on clarification for timing of DL transmission
ZTE ,MTK, HW,HiSilicon,Sony…

## Slide 2: background
In the email discussions after RAN1 NB-IoT ad-hoc#2 meeting, the following was agreed:
Introduce uplink transmission gaps for long uplink (i.e. NB-PUSCH/NB-PRACH) transmissions.
The agreed CR for TS 36.211 implements this agreement with the following placeholder text:
Section 10.1.3.6:
In case of NPUSCH repetitions, after transmissions of [X] slots, a gap of [Y] slots shall be inserted where the NPUSCH transmission is postponed.
In RAN1 #84bis meeting, the following agreements on DL transmission delay were made：
The start of a DL transmission is >=3ms later than the end of any NPUSCH transmission for the same UE
we need to clarify “the start of a DL transmission”if NPUSCH UL gap is inserted during NPUSCH transmission,

## Slide 3: Proposals
  If NPUSCH UL Gap is inserted at the end of NPUSCH transmission, the start of a DL transmission is from the end of the UL gap.