## Slide 1: WF on hybrid UE antenna modelling
Intel, Samsung, LGE
R1-165712
3GPP TSG RAN1 #85
Nanjing, China, May 23 - 27, 2016
Agenda Item: 7.1.6

## Slide 2: Background
In R1-163863 and R1-163923, directional UE antenna has been agreed for NR above 6GHz.
For UE with multiple directional antenna panels, naturally those panels have different orientations in order to have full field of view (FOV).
In R1-162383/R1-164192, it is proposed that UE has two directional antennas with opposite orientations.
In R1-163987, more detailed modeling of UE antenna placement and orientation is given as well as other detailed UE antenna configuration parameters
In R1-164554, another way of modeling UE antennas with different orientations and giving more freedom to antenna panel placement is given
In R1-164190, the RSRP modelling defined in TR 36.873 has been extended to consider UE side beamforming.
In this way forward, possible agreements with regard to UE antenna shapes, orientation, RSRP modelling are proposed.

## Slide 3: Proposal 1
For UE with () directional antenna panels.
  Introduce for orientation of the panel , , where the orientation of the first panel is the same as UE orientation, is the array bearing angle and is the array downtilt angle[1].
  For NR MIMO evaluation:
    Config 1: () = (1, 2);; ()=(0,0)
    Config 2: () = (1, 4);,,; ()=(0,0)
    Other configurations can have panel specific position offset (). Note in this case the notation of () does not leads to rectangular shape.
  UE orientation for mobile device =(U(0,360), 90); UE orientation for customer premise equipment (CPE) can be optimized
  Each antenna array has shape dH=dV=0.5λ
    Config a: (M, N, P) = (2, 4, 2), the polarization angles are 0 and 90
    Config b: (M, N, P) = (4, 4, 1) , the polarization angle for even panel is 0 and for odd panel is 90
    Other configurations, e.g. (M, N, P) = (4, 4, 2) or (M, N, P) = (4, 8, 1) can be considered for 70GHz band
  The antenna elements of the same polarization of the same panel is virtualized into one TXRU
  FFS: one TXRU can connect to different subarrays dynamically
  Note: The channel coefficients for each UE panel can be generated using spatial channel model
[1] TR 36.873

## Slide 4: Proposal 2
For cell association with UE side beamforming, the RSRP modeling in TR 36.873 is extended to include UE side beamforming; RSRP of Tx antenna port p is measured from U Rx antenna ports; FFS how to choose U Rx antenna ports
  Note: In beam-centric operation, RSRP can be calculated per Tx-Rx beam pair
Where for NLOS path for n=1,…,N
And for LOS path

## Slide 5: Proposal 2 (continued)
where:
is the complex weight applied to rx antenna r of rx antenna port u on a panel
  E.g., 2D oversampled DFT weights are used for ;
  other weights FFS