## Slide 1: WF on aperiodic beam sweeping and CSI reporting
3GPP TSG RAN WG1 Meeting #86 R1-167961
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda Item: 8.1.5
ZTE Corporation, ZTE Microelectronics, ASTRI, InteI Corporation

## Slide 2: Proposal-1
  Study the following aspects of aperiodic beam sweeping:
  Three types of beam sweeping for both UL and DL:
      TRP beam sweeping only, keeping a fixed UE beam
        supporting measuring multiple TRP beams by the same UE beam
      UE beam sweeping only, keeping a fixed TRP beam
        supporting measuring the same TRP beam with multiple UE beams
          E.g. by time domain replica waveform. TRP Tx using the same TRP beam and UE receives using one UE beam per replica
          E.g. by multiple wider sub-carrier spacing based OFDM symbols. TRP Tx using the same TRP beam and UE receives each symbol with different UE beam
      Joint TRP and UE beam sweeping
  Indication of TX and/or RX beam on control/feedback signaling:
      Indication is per beam or per beam group
  Content of aperiodic CSI report e.g. RSRP, RI/PMI/CQI, beam ID
  NOTE: support various mobility scenarios
  Others are not precluded

## Slide 3: Proposal-2
  Study aperiodic CSI in conjunction with aperiodic RS transmission:
  Dynamic indication of aperiodic reference signal and interference measurement resource including
      Aperiodic reference signal for channel measurement for CSI feedback and beam selection/training
      Aperiodic interference measurement resource for interference measurement, including using non-zero power reference signal
      Resource pool sharing for aperiodic channel and interference measurement resources
  DMRS based CSI feedback including CQI adjustment and beam refinement
    Study the timing requirement among aperiodic CSI triggering, aperiodic RS transmission and CSI feedback.
      Timing between CSI triggering and aperiodic RS transmission X
      Timing between aperiodic RS transmission and CSI/beam feedback Y
  Others are not precluded