## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-168176 Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on RS for CSI Acquisition and Demodulation in NR
Huawei, HiSilicon

## Slide 2: Background
Following WF has been agreed in RAN1#85:
  In NR multi-antenna schemes, studies on RS design and CSI acquisition considering following use cases
    Non-UE-specific RS use case for CSI measurement
    UE-specific RS use case for CSI measurement
      Note: functionally may be analogous e.g.: to R13/14 UE-specific beamformed CSI-RS (with dynamic beamforming)
      Note: maybe relevant to UE receiving beam sweeping
    Use of a joint operation among multiple RS from the same or different use cases
    RS for interference measurement use cases
    RS for channel reciprocity use cases
    Other use cases is not precluded
  Note: including measurement over aperiodic/periodic/semi-persistent RS
  Note: Subband RS is not precluded

## Slide 3: Proposal-1
RS design in NR
  CRS functionalities need to be supported by NR Signal(s)
    CRS functionalities include fine time/frequency synchronization, RRM measurement, and digital AGC
  Study QCL based on NR signals (other than CRS)
  Introduce RS to support beam management
  Introduce RS to support phase noise mitigation
  Consider the impact of different numerologies

## Slide 4: Proposal-CSI-RS
At least following RS configurations for CSI acquisition are supported in NR
  Aperiodic RS
  FFS: Semi-persistent RS, periodic RS
Requirements of RS for CSI measurement in NR at least include
  RSs are mapped on a few consecutive symbols
  RS is located at the earlier part of a “time interval X” in order to leave sufficient time for CSI measurement and report
    FFS: RS located at other part of a “time interval X”
Study on configurable density of RS in frequency domain
Study on Multi-level RS should be considered
  E.g. functionally analogous to R13/14 hybrid non-precoded/beamformed CSI-RS and beamformed CSI-RS
  Note: here the definition of 'time interval X' follows the agreements in RAN1#85 meeting

## Slide 5: Proposal-SRS
Studies on RS for channel reciprocity in NR at least include
  Beamformed RS
  Dynamic indication of number of RS symbols in a “time interval X”
  Dynamic indication of the bandwidth for SRS hopping
    total SRS hopping bandwidth within a “time interval X”
    bandwidth for each SRS hopping instance

## Slide 6: Proposal-DMRS
DMRS is precoded with the same precoding vector as associated data with some exceptions
  Exception includes transmit diversity.
Studies on design of RS for demodulation in NR at least include
  DMRS is concentrated within one or a few consecutive symbols at beginning part of a “time interval X”
    FFS: additional DMRS located at middle part of a time interval
  Configuration/indication of density of DMRS in frequency/time domain