## Slide 1
Way Forward on asynchronous UL HARQ for 1ms TTI and reduced processing time
Ericsson, Nokia and Alcatel-Lucent Shanghai Bell
R1-168187
3GPP TSG RAN WG1 Meeting #86
Göteborg, Sweden, 22rd - 26th Aug 2016
Agenda item 7.2.12.1

## Slide 2: Background
Reduced processing time for 1ms TTI is to be specified for FS1, FS2 and FS3
If an eNB serves UEs with different processing times PHICH collisions can happen with synchronous UL HARQ
Due to the lack of PHICH resources in all DL subframes synchronous UL HARQ may limit the gains of reduced processing time with 1ms TTI for FS2

## Slide 3: Proposal
PHICH-less asynchronous HARQ for UL is supported for 1 ms TTI with shortened processing time
  For FS1 and FS2, bit fields are added in the applicable DCI messages to indicate HARQ processes ID and RV
  No change in FS3 asynchronous UL HARQ operation