## Slide 1: WF on Integrated Backhaul and Access
Huawei, HiSilicon, AT&T, Samsung, Qualcomm, Ericsson, ASTRI, […]
3GPP TSG RAN WG1 Meeting #86 | R1-168429
Gothenburg, Sweden, 22 – 26 Aug 2016 | 

## Slide 2: Background
Companies have shown common interests in integrated operation of backhaul and access at a TRP or a relay node (RN) or network-level, sharing the time and/or frequency and/or antenna resources
  R1-163220: Access-integrated backhaul (AIB)
  R1-166115: Flexible backhauling
  R1-167119: Integrated access and backhaul (IAB)
  R1-167267: Self-backhauling
  R1-167220: Joint access and backhaul (JAB)
  R1-166887: Flexible resource sharing
  between access and backhaul link
  …
Preliminary agreements have been achieved on integrated backhaul and access, focused on multiplexing of backhaul and access links on the same or different frequencies
  NR should allow for efficient same frequency operation between the access link and backhaul link
  NR should also allow for efficient operation when the backhaul link and access link are on different frequencies. This includes:
    Operation of backhaul link and access link on different frequencies in the same band
    Operation of backhaul link and access link in different bands
  Note: The term ‘backhaul link’ does not make any assumption on NR RAN architecture design options
R1-167267

## Slide 3: Background (Contd)
Up to this meeting, different views and proposals for integrated backhaul and access have been provided, including
  Support dynamic resource allocation among backhaul and access links
    For efficient resource utilization and to be adaptive to traffic fluctuations
    To be enabled by TDM and/or FDM and/or SDM approaches
    R1-166115, R1-166488, R1-166881, R1-167267, R1-167119, R1-166763
R1-167220
  R1-166488

## Slide 4: Background (Contd)
The views and proposals on integrated backhaul and access further includes
  Support multi-hop backhauling and multi-site connectivity in backhauling
    Multi-hop backhauling to enable flexible deployment extension
    Multi-site connectivity: Maintain backhaul connections with multiple TRPs
      To be robust against variations in propagation conditions
    R1-166115, R1-166488, R1-166887, R1-167119, R1-167267, R1-167799
  Provide forward compatibility to support full duplex operation of integrated backhaul and access
    To relax the scheduling constraints imposed by half-duplex and improve efficiency
    R1-166488, R1-166887, R1-167267
R1-167119
R1-166488

## Slide 5: Background (Contd)
Companies have also provided views on the feasibility and requirements on mobile TRP/RNs carrying integrated backhaul and access functionalities
  R1-162187
    Mobile relay is important for supporting e.g., the use cases of bus and (high-speed) train, but special considerations would be needed to support mobility. Feasibility of supporting mobile relay at mmWave especially for (very) high speed would be questionable, however feasibility at slow/moderate speed also requires further study.
  R1-163220
    Robust handover procedures of access-integrated backhaul connections for mobile relays and for load balancing purposes
  R1-166887
    RAN1 needs to discuss how to determine the TTI boundary of the access link. This discussion needs to take into account time-varying TTI boundary of the backhaul link and its impact on the synchronization maintenance of the UEs connected to the relay node in the mobile relay cases.
  R1-167119
    For mobile relay nodes, the response mechanism to accommodate topological changes are generally more stringent.

## Slide 6: Proposals
From the commonality in views and proposals from companies, it is proposed that
  Integrated backhaul and access should be supported by NR, including
    Support dynamic resource allocation among backhaul and access links, including TDM and FDM and SDM approaches under half-duplex constraint
    Support multi-hop backhauling and multi-site connectivity in backhauling
    Mechanism for integration of new TRPs/RNs carrying integrated backhaul and access functionalities
    Mechanisms for discovery and management of backhaul links for the connected TRP/RNs with integrated backhaul and access
    Other aspects/functionalities such as forward compatibility to support full duplex operation on backhaul and/or access links are FFS
Regarding the support of mobile TRPs/RNs carrying integrated backhaul and access functionalities, it is proposed that
  RAN1 should strive for a common mobility handling and beam management framework for mobile TRP/RNs carrying integrated backhaul and access functionalities and the usual UEs