## Slide 1
3GPP TSG RAN WG1 Meeting #86bis R1-1610491 Lisbon, Portugal, 10th - 14th Oct 2016
Agenda item: 8.1.4.4
WF on NR DMRS
Huawei, HiSilicon,……

## Slide 2: Background
Following agreements on NR DMRS has been made in RAN1#86:
  Demodulation reference signal for transmit diversity, if supported, could be
    UE-specific RS (if supported by NR)
    Shared (by two or more UEs)-RS (if supported by NR)
    Other types of RS are not precluded
  At least 8 orthogonal DL DMRS ports is supported for MU-MIMO scheduling
  In addition to the front-loaded RS agreed to study in RAN1#85, same or extended/additional RS is studied in NR of at least the following:
    Estimate/compensate Doppler parameters

## Slide 3: Proposal
Separate design of demodulation RS for broadcast channel, control channel and data channel
Studies on design of demodulation RS for data channel at least include
  The same principle for UL and DL RS pattern design
  DM RS mapped in one or a few consecutive symbols
  Additional RS located at middle part of a slot
  Up to 16 orthogonal DL DMRS ports for MU-MIMO scheduling