## Slide 1
3GPP TSG RAN WG1 Meeting #86bis R1-16xxxxx
Lisbon, Portugal, 11st - 14th Oct 2016
Agenda item: 8.1.5.1
WF on Synchronization Signal for NR Initial Access
Huawei, HiSilicon, […]

## Slide 2: Background
The following agreements have been reached at RAN1#86:
  For subcarrier spacing of each synchronization signal (e.g. NR PSS, SSS) in a NR carrier, the following alternatives should be studied
    Alt 1: Subcarrier spacing is predefined in the specification for a given frequency range
      Ex: 15kHz for sub-6GHz, 60kHz for over-6GHz
      Note that there are more than one frequency ranges
    Alt 2: Subcarrier spacing is selected by NR BS
    Alt 3: Single subcarrier spacing is predefined in the specification for all frequency ranges
    Other alternatives are not precluded
  NR synchronization signal is based on CP-OFDM
    Note that DFT-spread-OFDM based design is not precluded

## Slide 3: Proposal
SS for initial access is a predefined subcarrier spacing according to the spectrum range
SS for initial access can be transmitted in predefined frequency locations other than the centre of a carrier
For SS with multiple beams, at least TDM of the SS over different beams is supported;
  FDM and CDM in addition to TDM of the SS are not precluded