## Slide 1: WF on Unified RACH Procedure
ZTE, ZTE Microelectronics, NTT DOCOMO, Nokia, Alcatel-Lucent Shanghai Bell, Sharp, Intel
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal 10th –14th October 2016
Agenda: 8.1.5.2
R1-1610962

## Slide 2: Background
Agreements:
When Tx/Rx reciprocity is available at gNB at least for multiple beams operation, the following RACH procedure is considered for at least UE in idle mode
  Association between one or multiple occasions for DL broadcast channel/signal and a subset of RACH occasions resources is informed to UE by broadcast system information or known to UE
    FFS: Signaling of “non-association”
    Detailed design for RACH preamble should be further studied
  Based on the DL measurement and the corresponding association, UE selects the subset of RACH occasionsresources
    FFS: Tx beam selection for RACH preamble transmission
  At gNB, the DL Tx beam for the UE can be obtained based on the detected RACH preamble and would be also applied to Message 2
    UL grant in message 2 may indicate the transmission timing of message 3
For the cases with and without Tx/Rx reciprocity, the common random access procedure should be strived
When Tx/Rx reciprocity is not available, the the following could be further considered for at least UE in idle mode
  Whether or how to report DL Tx beam to gNB, e.g.,
    RACH preamble/resource
    Msg. 3
  Whether or how to indicate UL Tx beam to the UE, e.g.,
    RAR

## Slide 3: Background
Agreements:
RACH resource:
  A time-frequency resource to send RACH preamble
Whether UE needs to transmit one or multiple/repeated preamble within a subset of RACH resoueces can be informed by broadcast system information
  For example, to cover gNB RX beam sweeping in case of NO Tx/Rx reciprocity at the gNB

## Slide 4: Intention
Overcome the red-marked limitation in Slide 2.
Use green-marked framework in Slide 2 also for gNB non-reciprocity.
 unifed random access framework for different gNB reciprocity.

## Slide 5: Proposal
Regardless of whether Tx/Rx reciprocity is available or not at gNB at least for multiple beams operation, the following RACH procedure is considered for at least UE in idle mode
  Association between one or multiple occasions for DL broadcast channel/signal and a subset of RACH resources is informed to UE by broadcast system information or known to UE
    FFS: Signaling of “non-association”
    Detailed design for RACH preamble should be further studied
  Based on the DL measurement and the corresponding association, UE selects the subset of RACH resources
    FFS: Tx beam selection for RACH preamble transmission

## Slide 6: Examples
DL
DL
DL
...
Full
gNB
reciprocity
RACH resource
...
Association
Sub-set of
RACH resources
DL
DL
DL
...
Non
gNB
reciprocity
Association
Time
RACH resource
RACH resource
RACH resource
...
RACH resource
RACH resource
...
RACH resource
...
Sub-set of
RACH resources
RACH resource
RACH resource
RACH resource
...
RACH resource
RACH resource
...
DL
DL
DL
...
Partial
gNB
reciprocity
Association
RACH resource
...
Sub-set of
RACH resources
RACH resource
RACH resource
RACH resource
...
RACH resource
RACH resource
...
...
...
...