## Slide 1: WF on signaling details for MUST Case 3
Qualcomm, Nokia, ASB, NEC
3GPP TSG RAN1 #87
Reno, USA Nov 14 - 18, 2016
Agenda Item: 6.2.3.2
R1-16113355

## Slide 2: Background
MUST case 3 is a natural extension to legacy MU-MIMO operation
  A useful operating mode for MUST case 3 is a mixed pairing of MUST case 3 capable UE with legacy MU-MIMO capable UE
Legacy MU-MIMO does not have RA alignment restriction
  Restricting to aligned RA for MUST case 3 will restrict the flexibility for

## Slide 3: Proposal 1
MUST Case 3 operation without resource allocation (RA) alignment between co-scheduled UEs is supported.
  The common assistance DCI for MUST Case 3 contains
    RA header: Common to all UEs, defining the RA type
    OCC type (2 or 4): Common to all UEs
  The common assistance DCI for MUST Case 3 contains following information of each co-scheduling blocks
    RA: Only need to cover the overlapping parts with the same spatial layer usage structure
    nSCID
    Per layer description: On/off or modulation order

## Slide 4: Proposal 2: Example Design of Contents of MUST case 3 assistant DCI
Common header
  RA type – 2 bits: Type 0, Type 1, Type 2 localized VRB, Type 2 distributed VRB
  OCC type – 1 bit: OCC2 or OCC4
Per record
  RA – 9 bits
  nSCID – 1bit
  Mod order and on/off – 8 bits: 2 bits per DMRS port
    For OCC4 case, sequentially for port 7,8,11,13
    For OCC2 case, sequentially for port 7,8 (only read the first 4 bits)
    For each port: 00  Not used; 01QPSK; 1016QAM; 1164QAM or higher order modulation