## Slide 1
3GPP TSG RAN WG1 Meeting #87 R1-1613440
Reno, USA, 14th-18th November 2016
Agenda item: 7.1.3.1
WF on multi-panel based MIMO for DL and UL transmissions
Huawei, HiSilicon, Xinwei, …

## Slide 2: Background
Study at least the following different multi-panel structures at both TRP and UE
  Uniform array: antenna elements with the same polarization from multiple panels are uniformly distributed in horizontal and vertical dimensions respectively (see Fig.1(a) in R1-1610893 as an example)
  Non-uniform array: antenna elements with same polarization from multiple panels are not uniformly distributed in horizontal or vertical dimension (see Fig.1(b) in R1-1610893 as an example)
Study the coherent/non-coherent MIMO transmission based on uniform/non-uniform array structure at TRP or UE
  E.g., Codebook design, calibration accuracy, interference measurement, advanced receiver design, interference hypothesis

## Slide 3: Proposals
For multi-panel based downlink transmission
  Support both uniform and non-uniform array
  Support both coherent and non-coherent MIMO transmission for multi-panel antenna arrays
  Support multiple QCL assumptions / indications
  Support reporting of receiver capabilities
  Study the following issues:
    The maximal number of CWs for one UE, e.g., one, two or more
    CW to layer mapping:
      LTE-like mapping
      New flexible mapping
For multi-panel based uplink transmission
  Support non-coherent transmission in order to improve both reliability and capacity
  Study practical issues including multiple timing advances, power control, beam procedure with/without the help of existing well paired beams and so on