## Slide 1: Discussion on SLSS
Ericsson
3GPP TSG RAN WG1 Meeting #88 R1-1703608
Athens, Greece, 13th - 17th February 2017
Agenda item – 7.2.1.4

## Slide 2: Background
SLSS transmitted from UE B and UE D are not distinguishable
SLSS transmitted from UE C and UE B (or UE D) are distinguishable based on the used resource
Distinguishing UE C and UE D or UEs further in the sync chain is not required by the existing agreements
UE D
UE C
UE B
UE A
Resource 3
SLSSID 0
PSBCH from preconfig.
Priority 4
Resource 2
SLSSID X
PSBCH from preconfig.
Priority 5
Resource 1
SLSSID X
PSBCH from preconfig.
Priority 6
Resource 2
SLSSID X
PSBCH from preconfig.
Priority 6

## Slide 3: Conclusion
A UE searching for Sync Ref that receives:
  SLSS on Resource 1 (SLSSID=X, InC=0, PSBCH from preconf)
  SLSS on Resource 2 (SLSSID=X, InC=0, PSBCH from preconf)
always follows the second signal.
It is not necessary to change any parameter (SLSSID, InC bit, etc.) to meet the existing agreements on Sync Priority
  No need to ensure distinguishability between SLSS transmitted by UE B and UE D.