## Slide 1: WF on Indication of actually transmitted SS blocks
ZTE, ZTE Microelectronics, InterDigital
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, 3rd – 7th April 2017
Agenda: 8.1.1.1.2
R1-1706830

## Slide 2: Background
Agreement (RAN1 #88):
The maximum number of SS-blocks, L, within SS burst set may be carrier frequency dependent
  For frequency range category #A (e.g., 0 ~ 6 GHz), the number (L) is TBD within L ≤ [16]
  For frequency range category #B (e.g., 6 ~ 60GHz), the number is TBD within L ≤ [128]
  FFS: L for additional frequency range category
The position(s) of actual transmitted SS-blocks can be informed for helping CONNECTED/IDLE mode measurement, for helping CONNECTED mode UE to receive DL data/control in unused SS-blocks and potentially for helping IDLE mode UE to receive DL data/control in unused SS-blocks
  FFS whether this information is available only in CONNECTED mode or in both modes
  FFS how to signal the position(s)

## Slide 3: Proposal
The position(s) of actually transmitted SS blocks can be informed in remaining minimum SI.
At least the following schemes are considered
  Indicating the number of actually transmitted SS blocks
  Indicating a bitmap of actually transmitted SS blocks
  Other schemes are not precluded.
Consider flexibility and signaling overhead.