## Slide 1: WF on NR-PBCH transmission scheme and DMRS design
NTT DOCOMO, InterDigital, ZTE
3GPP TSG RAN WG1 Meeting #89 R1-1709221
Hangzhou, China
15th – 19th May, 2017
Agenda item: 7.1.1.2.1
Document for decision

## Slide 2: Background
Working assumption:
NR-PSS, NR-SSS and NR-PBCH are presented in every SS block
  FFS: deactivated cell case (if defined)
Working assumption:
For NR-PBCH transmission, NR supports a single antenna port based transmission scheme only.
  FFS: Same or different antenna port(s) are defined for NR-PSS, NR-SSS and NR-PBCH within an SS block
  Companies are encouraged to further evaluate NR-PBCH performance
Agreements:
PBCH BW: 288 subcarriers, 2 OFDM symbols (additional symbols if MIB size larger than assumed)
PBCH phase reference: DMRS
PBCH TTI: 80 msec

## Slide 3: Background
Many evaluation results show that UE transparent single antenna port based transmission scheme can achieve enough performance
Using same antenna port for NR-SSS and NR-PBCH makes it possible to use each other as supplementary RS
Two column DMRS symbols should be supported for NR-PBCH demodulation to guarantee high speed NR-PBCH performance

## Slide 4: Proposal
For NR-PBCH transmission, NR supports a single antenna port based transmission scheme only.
  Same antenna port is defined for NR-PSS, NR-SSS and NR-PBCH within an SS block
  Single antenna port based transmission scheme for NR-PBCH is transparent to UEs
DMRS for NR-PBCH is mapped on every NR-PBCH symbol
  Down select RE mapping scheme for the DMRS
    Option 1: DMRS sequence is mapped on subcarriers with equal interval
    Option 2: DMRS sequence is mapped on subcarriers with unequal interval (e.g., less or no mapping within NR-SSS transmission bandwidth)
  At least, DMRS sequence and/or resource is(are) different among different cells according to different cell IDs
  Down select further DMRS sequence design principle
    Option 1: DMRS sequence is common among different SS blocks within a same cell
    Option 2: DMRS sequence is different among different SS blocks within a same cell
    Option 3: DMRS sequence is different among different SS blocks within a same SS burst within a same cell
      FFS definition of SS burst (e.g., maximum number of SS blocks within SS burst)