## Slide 1: WF on Number of Base Graphs for LDPC Codes
Ericsson, Qualcomm, Intel, Samsung, LG, AT&T
R1-1709275
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.4.1.2

## Slide 2: Background (1)
Agreement (RAN1#88bis Apr 2017):
The base graph design is selected from the following alternatives:
Alt 1: One base graph covering ~1/5 <= R <= ~8/9
Alt 1a: Two nested base graphs, where:
Base graph #1
  Covers info block size K:
Kmin1 <=K<= Kmax1, Kmin1 > Kmin, Kmax1 =Kmax
  Covers code rate R: ~1/3 <= R <= ~8/9; FFS whether Rmin can be ~1/5
Base graph #2
  Nested within base graph #1
  Covers info block size K:
Kmin2 <=K<= Kmax2, Kmin2 =Kmin, Kmax2 < Kmax, where 512<=Kmax2<=2560
  Covers code rate R: ~1/5 <= R <= ~2/3
  Kbmax =16 is the starting point; lower values in the range 10<=Kbmax<16 are encouraged if feasible.
Alt 2: Two base graphs, where:
Base graph #1
  Covers info block size K:
Kmin1 <=K<= Kmax1, Kmin1 > Kmin, Kmax1 =Kmax
  Covers code rate R: ~1/3 <= R <= ~8/9; FFS whether Rmin can be ~1/5
Base graph #2
  Not nested within base graph #1
  Covers info block size K:
Kmin2 <=K<= Kmax2, Kmin2 =Kmin, Kmax2 < Kmax, where 512<=Kmax2<=2560
  Covers code rate R: ~1/5 <= R <= ~2/3
  Kbmax = 10 is the starting point; higher values in the range 10<Kbmax<=16 can also be considered if necessary.

## Slide 3: Background (2)
There are throughput benefits to Alt. 1a and 2 compared to Alt 1 when base graph #2 is used for smaller code blocks.
Small code blocks dominate in the uplink in terms of packet frequency
Alt 2 allows for more design freedom compared to Alt 1a

## Slide 4: Proposal
Choose an LDPC design based on Alt. 2 for eMBB.