## Slide 1: WF on PDCCH
NTT DOCOMO, INC., Huawei, HiSilicon, Ericsson, ZTE, InterDigital, KT Corp., LG Electronics, ETRI, OPPO, NEC
3GPP TSG RAN WG1 #89
Hangzhou, P.R. China, 15th – 19th May 2017
Agenda: 7.1.3.1
R1-1709375

## Slide 2: Proposals
CCE = 6 REGs (confirm WA)
One of following is configured for REG-to-CCE mapping for a 1-symbol CORESET:
  Opt.1: No interleaving – 6 REGs for a given CCE are grouped to form a REG bundle and all REGs for a given CCE are consecutive
    CCE(s) of one PDCCH is/are also consecutive
    FFS: Whether the UE can assume the same precoder across multiple REG bundles
  Opt.2: Interleaving – [2 or 3 or 6] REGs for a given CCE are grouped to form a REG bundle and REG bundles are interleaved in the CORESET
    FFS: Whether the UE can assume the same precoder across multiple REG bundles
    FFS: down selection among {2}, {3}, {2,6}, or {3,6}
  Note: UE can assume the same precoder within a REG bundle

## Slide 3: Proposals
For REG-to-CCE mapping for a CORESET with more than 1-symbol;
  REG bundle is defined in time and frequency-domain
  At least support following:
    Time-first mapping where one of the following is configured
      Support REG bundle in time-domain being equal to the CORESET semi-statically configured time duration
        Opt.1: Non interleaving - 6 REGs for a given CCE are grouped to form a REG bundle and all REGs for a given CCE are time and frequency localized
          FFS: Whether the UE can assume the same precoder across multiple REG bundles
        Opt.2: Interleaving – [2 or 3 or 6] REGs for a given CCE are grouped to form a REG bundle and REG bundles are interleaved in the CORESET
          FFS: Whether the UE can assume the same precoder across multiple REG bundles
  FFS: time-domain precoder-cycling
    Support REG bundle in time-domain being equal to 1 symbol, or;
    Support following:
      REG-to-CCE mapping is exactly same as the case where a CORESET with 1 symbol
      A PDCCH candidate can be mapped across OFDM symbols