## Slide 1: Way forward on reduced system acquisition time
Huawei, HiSilicon, Neul, [….]
R1-1709591
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, May 15-19, 2017
Agenda item 6.2.7.5

## Slide 2: Background
Agreements at RAN1#88bis
For reduced system acquisition time for NB-IoT, at least the following candidates can be considered
  Enhancement(s) to NPSS/NSSS
  Enhancement(s) to MIB-NB
  SIB1-NB accumulation across multiple SIB1-NB TTIs (with or without specification impact)
  New mechanism allowing to skip SIB1-NB and/or SI messages and/or MIB-NB reading
  Additional SIB1-NB is transmitted on other subframes in addition to the existing SIB1-NB transmission
  Use of physical signal/channel in agenda item 7.2.7.1.1 (if introduced)
  FFS on other SIBx-NB
  Details of all solutions are FFS
  Solutions need to be backwards compatible and take care of impacts to Rel-13/Rel-14 networks

## Slide 3: Proposals
Enhancements to NPSS/NSSS are considered as follows:
  NPSS/NSSS acquisition enhancement without additional transmission in new subframe(s) on anchor carrier for in-band, guard-band and standalone
Enhancements to SIB1-NB acquisition at times when acquisition is required are considered as follows:
  Additional repetitions of SIB1-NB on an anchor carrier in subframe #4 and/or subframe #9, for in-band
  Additional repetitions of SIB1-NB on anchor carrier, for standalone and guard-band
Enhancement to reduce occasions when SIB1-NB is required to be acquired, e.g. signaling to avoid acquisition
Enhancements to MIB-NB acquisition are considered as follows:
  Using unused 3-OFDM symbols in existing subframe#0 on anchor carrier for stand-alone and guard band modes