## Slide 1: WF on SIB1-NB transmission on a non-anchor carrier in TDD
LG Electronics, Ericsson, Lenovo, Motorola mobility
R1-1805348
3GPP TSG RAN WG1 Meeting 92bis
Sanya, China, April 16th – 20th, 2018
Agenda item 6.2.7.6.1

## Slide 2: Background (agreements on non-anchor carrier SIB1-NB)
From RAN1#90bis
  Periodicity of SIB1-NB in TDD is the same as FDD (i.e. 2560ms)
  One transport block of SIB1-NB is transmitted over 8 SIB1-NB subframes (i.e. same as FDD)
Recommended Proposal after the offline discussion in RAN1#92bis
  For 16 and 8 repetitions of SIB1-NB on a non-anchor carrier, the starting radio frame is as follows:
  SIB1-NB transmission on a non-anchor carrier in all operation modes is in subframe #0 and #5
  Check the transmission details within this week (ZTE)
Number of SIB1-NB repetitions | PCID | Starting radio frame number for SIB1-NB repetitions (nf mod 256)
16 | PCID mod 2 = 0 | 0
 | PCID mod 2 = 1 | 1
8 | PCID mod 2 = 0 | 0
 | PCID mod 2 = 1 | 16

## Slide 3: Background
UL/DL configurations and subframe allocations for SIB1-NB
#Subframe |  |  | #0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | #0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9
MBSFN |  |  | X | X | X |  |  | X | X |  |  |  | X | X | X |  |  | X | X |  |  | 
Anchor-carrier | 0 | 5ms | D | S | U | U | U | D | S | U | U | U | D | S | U | U | U | D | S | U | U | U
 | 1 | 5ms | NSSS | S | U | U | SIB1 | NPSS | S | U | U | MIB | SIB1 | S | U | U | SIB1 | NPSS | S | U | U | MIB
 | 2 | 5ms | NSSS | S | U | D | SIB1 | NPSS | S | U | D | MIB | SIB1 | S | U | D | SIB1 | NPSS | S | U | D | MIB
 | 3 | 10ms | NSSS | S | U | U | U | NPSS | D | D | D | MIB | SIB1 | S | U | U | U | NPSS | D | D | D | MIB
 | 4 | 10ms | NSSS | S | U | U | SIB1 | NPSS | D | D | D | MIB | SIB1 | S | U | U | SIB1 | NPSS | D | D | D | MIB
 | 5 | 10ms | NSSS | S | U | D | SIB1 | NPSS | D | D | D | MIB | SIB1 | S | U | D | SIB1 | NPSS | D | D | D | MIB
 | 6 | 5ms | D | S | U | U | U | D | S | U | U | D | D | S | U | U | U | D | S | U | U | D
Non-anchor carrier | 0 | 5ms | D | S | U | U | U | D | S | U | U | U | D | S | U | U | U | D | S | U | U | U
 | 1 | 5ms | SIB1 | S | U | U | D | SIB1 | S | U | U | D | SIB1 | S | U | U | D | SIB1 | S | U | U | D
 | 2 | 5ms | SIB1 | S | U | D | D | SIB1 | S | U | D | D | SIB1 | S | U | D | D | SIB1 | S | U | D | D
 | 3 | 10ms | SIB1 | S | U | U | U | SIB1 | D | D | D | D | SIB1 | S | U | U | U | SIB1 | D | D | D | D
 | 4 | 10ms | SIB1 | S | U | U | D | SIB1 | D | D | D | D | SIB1 | S | U | U | D | SIB1 | D | D | D | D
 | 5 | 10ms | SIB1 | S | U | D | D | SIB1 | D | D | D | D | SIB1 | S | U | D | D | SIB1 | D | D | D | D
 | 6 | 5ms | D | S | U | U | U | D | S | U | U | D | D | S | U | U | U | D | S | U | U | D
When #rep=16 and PCID mod 2 = 0
When #rep=16 and PCID mod 2 = 1
All other cases
When PCID mod 2 = 0
or #rep=16
When PCID mod 2 = 1
and #rep=16

## Slide 4: Background
When one TB of SIB1-NB is transmitted over 8 SIB1-NB subframes (i.e. same as FDD)
  8 SIB1-NB subframes carry encoded bits of SIB1-NB continuing reading them from circular buffer.
One codeword of SIB1-NB
1/3 TBCC endcoding
Rate matching
A | B | C | D | E | F | G | H
Starting address
A sub-block
B sub-block
C sub-block
D sub-block
continuing
Circular buffer for one codeword of SIB1-NB
will be mapped into 8 subframes
A | B | C | D | E | F | G | H
will be mapped into the next 8 subframes
Case-B
When one TB of SIB1-NB is transmitted over 16 SIB1-NB subframes (i.e. same as FDD)
  16 SIB1-NB subframes carry encoded bits of SIB1-NB continuing reading them from circular buffer.
One codeword of SIB1-NB
1/3 TBCC endcoding
Rate matching
A | B | C | D | E | F | G | H
Starting address
A sub-block
B sub-block
C sub-block
D sub-block
continuing
Circular buffer for one codeword of SIB1-NB
will be mapped into 8 subframes
I | J | K | L | M | N | O | P
will be mapped into the next 8 subframes
Not compliant with
the previous agreement
but additional SIB1-NBs in FDD carry these sub-blocks
Case-A

## Slide 5: Background
Example for SIB1-NB transmissions on a non-anchor carrier when the repetition number is 8
0
256
512
768
1024
1280
1536
1792
2048
2304
2560
2816
3072
3328
3584
3840
Possible boundaries of modification for SystemInformationBlockType1-NB (40.96s)
SFN
ID%2=0 | ID%2=1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
16
32
48
64
80
96
112
128
144
160
176
192
208
224
240
SIB1-NB TTI where TBS and the number of repetitions are indicated by schedulingInfoSIB1 in MIB-NB (2.56s)
A |  |  |  |  | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  | C |  |  |  |  | D |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  | G |  |  |  |  | H |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I |  |  |  |  | J |  |  |  |  |  |  |  |  |  |  |  |  |  |  | K |  |  |  |  | L |  |  |  |  |  |  |  |  |  |  |  |  |  | 
M |  |  |  |  | N |  |  |  |  |  |  |  |  |  |  |  |  |  |  | O |  |  |  |  | P |  |  |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  | C |  |  |  |  | D |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  | G |  |  |  |  | H |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I |  |  |  |  | J |  |  |  |  |  |  |  |  |  |  |  |  |  |  | K |  |  |  |  | L |  |  |  |  |  |  |  |  |  |  |  |  |  | 
M |  |  |  |  | N |  |  |  |  |  |  |  |  |  |  |  |  |  |  | O |  |  |  |  | P |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
5
10
40ms
15
20
25
30
35
39
40
79
80
119
120
159
160
199
200
239
240
279
280
319
320ms(=40ms x 8)
SIB1-NB subframe for PCID%2=0
SIB1-NB subframe for PCID%2=1
A |  |  |  |  | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  | C |  |  |  |  | D |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  | G |  |  |  |  | H |  |  |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  | C |  |  |  |  | D |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  | G |  |  |  |  | H |  |  |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  | C |  |  |  |  | D |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  | G |  |  |  |  | H |  |  |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  | C |  |  |  |  | D |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  | G |  |  |  |  | H |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0
39
40
79
80
119
120
159
160
199
200
239
240
279
280
319
320ms(=40ms x 8)
SIB1-NB subframe for PCID%2=0
SIB1-NB subframe for PCID%2=1
for Case-A
for Case-B

## Slide 6: Background
Example for SIB1-NB transmissions on a non-anchor carrier when the repetition number is 16
0
256
512
768
1024
1280
1536
1792
2048
2304
2560
2816
3072
3328
3584
3840
Possible boundaries of modification for SystemInformationBlockType1-NB (40.96s)
SFN
0
16
32
48
64
80
96
112
128
144
160
176
192
208
224
240
SIB1-NB TTI where TBS and the number of repetitions are indicated by schedulingInfoSIB1 in MIB-NB (2.56s)
A |  |  |  |  | B |  |  |  |  | A |  |  |  |  | B |  |  |  |  | C |  |  |  |  | D |  |  |  |  | C |  |  |  |  | D |  |  |  | 
E |  |  |  |  | F |  |  |  |  | E |  |  |  |  | F |  |  |  |  | G |  |  |  |  | H |  |  |  |  | G |  |  |  |  | H |  |  |  | 
I |  |  |  |  | J |  |  |  |  | I |  |  |  |  | J |  |  |  |  | K |  |  |  |  | L |  |  |  |  | K |  |  |  |  | L |  |  |  | 
M |  |  |  |  | N |  |  |  |  | M |  |  |  |  | N |  |  |  |  | O |  |  |  |  | P |  |  |  |  | O |  |  |  |  | P |  |  |  | 
A |  |  |  |  | B |  |  |  |  | A |  |  |  |  | B |  |  |  |  | C |  |  |  |  | D |  |  |  |  | C |  |  |  |  | D |  |  |  | 
E |  |  |  |  | F |  |  |  |  | E |  |  |  |  | F |  |  |  |  | G |  |  |  |  | H |  |  |  |  | G |  |  |  |  | H |  |  |  | 
I |  |  |  |  | J |  |  |  |  | I |  |  |  |  | J |  |  |  |  | K |  |  |  |  | L |  |  |  |  | K |  |  |  |  | L |  |  |  | 
M |  |  |  |  | N |  |  |  |  | M |  |  |  |  | N |  |  |  |  | O |  |  |  |  | P |  |  |  |  | O |  |  |  |  | P |  |  |  | 
0
5
10
40ms
15
20
25
30
35
39
40
79
80
119
120
159
160
199
200
239
240
279
280
319
320ms(=40ms x 8)
SIB1-NB subframe for PCID%2=0
SIB1-NB subframe for PCID%2=1
A |  |  |  |  | B |  |  |  |  | A |  |  |  |  | B |  |  |  |  | C |  |  |  |  | D |  |  |  |  | C |  |  |  |  | D |  |  |  | 
E |  |  |  |  | F |  |  |  |  | E |  |  |  |  | F |  |  |  |  | G |  |  |  |  | H |  |  |  |  | G |  |  |  |  | H |  |  |  | 
A |  |  |  |  | B |  |  |  |  | A |  |  |  |  | B |  |  |  |  | C |  |  |  |  | D |  |  |  |  | C |  |  |  |  | D |  |  |  | 
E |  |  |  |  | F |  |  |  |  | E |  |  |  |  | F |  |  |  |  | G |  |  |  |  | H |  |  |  |  | G |  |  |  |  | H |  |  |  | 
A |  |  |  |  | B |  |  |  |  | A |  |  |  |  | B |  |  |  |  | C |  |  |  |  | D |  |  |  |  | C |  |  |  |  | D |  |  |  | 
E |  |  |  |  | F |  |  |  |  | E |  |  |  |  | F |  |  |  |  | G |  |  |  |  | H |  |  |  |  | G |  |  |  |  | H |  |  |  | 
A |  |  |  |  | B |  |  |  |  | A |  |  |  |  | B |  |  |  |  | C |  |  |  |  | D |  |  |  |  | C |  |  |  |  | D |  |  |  | 
E |  |  |  |  | F |  |  |  |  | E |  |  |  |  | F |  |  |  |  | G |  |  |  |  | H |  |  |  |  | G |  |  |  |  | H |  |  |  | 
0
39
40
79
80
119
120
159
160
199
200
239
240
279
280
319
320ms(=40ms x 8)
SIB1-NB subframe for PCID%2=0
SIB1-NB subframe for PCID%2=1
for Case-A
for Case-B

## Slide 7: Proposals
When SIB-NB is transmitted on a non-anchor carrier,
  The total number of subframes carrying SIB1-NB is equal to 16 within 160msec
  Two subframes (i.e., subframe #0 and #5) are used for SIB1-NB transmission in every other radio frame
The mapping of the TBS of SIB1-NB has two alternatives
  Alt.1) One TBS is mapped to 8 SIB1-NB subframes, and the actual number of repetitions is doubled compared to the anchor carrier
  Alt.2) One TBS is mapped to 16 SIB1-NB subframes, i.e., by continuing reading from the virtual circular buffer