## Slide 1
3GPP TSG RAN WG1 Meeting #93 R1-1807734
Busan, Korea, May 21st – 25th, 2018
Agenda item: 7.1.1.2.2
Remaining Issue on RMSI CORESET Configuration
Samsung

## Slide 2: Background
In the last RAN4 meeting, the SS raster design for <3 GHz has been revised to
This contribution discusses the potential changes to the RMSI CORESET configuration based this revised SS raster design.
Frequency range | SS Block frequency position SSREF | GSCN | Range of GSCN
0 – 3000 MHz | N * 1200kHz + M * 50 kHz, N=1:2499, M ϵ {1,3,5} (Note 1) | [3N + (M-3)/2] | [2 – 7498]
3000-24250 MHz | 2400 MHz + N * 1.44 MHz N = 0:14756 | [7499 + N] | [7499 – 22255]
NOTE 1: The default value for operating bands with SCS spaced channel raster is M=3. |  |  | 
Table 5.4.3.1-1: GSCN parameters for the global frequency raster

## Slide 3: {SSB SCS, RMSI SCS} = {15kHz, 15kHz}, CORESET BW = 24, CH BW = 5 MHz
For a given channel raster, the associated valid SS raster location with RE alignment is only one from the 3 shifts with a cluster (e.g. the SS rasters and channel rasters are classified into 3 categories, as marked in different color in the figure in the next page);
For a given set of channel rasters and associated SS rasters (e.g. the ones with green in the figure), channels shift in the unit of 300 kHz and SSBs shift in the unit of 1200 kHz;
Every channel with min channel BW has one SSB within the BW (note that the global shift 150 kHz in SS raster design is essential to guarantee this);
5 sets of the relative location pattern of SSB, SSB after floating sync, CORESET BW, and min CH BW are illustrated in the figure, and the pattern begins to repeat from the 5th one (i.e., 5th is the same as 1st);
Conclusion: 3 configurations on the RB offset are sufficient (e.g. 0, 2, 4), and no change to the table is required

## Slide 5: {SSB SCS, RMSI SCS} = {15kHz, 30kHz}, CORESET BW = 24, CH BW = 10 MHz
For a given channel raster, the associated valid SS raster location with RE alignment is only one from the 3 shifts with a cluster (e.g. the SS rasters and channel rasters are classified into 3 categories, as marked in different color in the figure in the next page);
For a given set of channel rasters and associated SS rasters (e.g. the ones with green in the figure), channels shift in the unit of 300 kHz and SSBs shift in the unit of 1200 kHz;
5 sets of the relative location pattern of SSB, SSB after floating sync, CORESET BW, and min CH BW are illustrated in the figure, and the pattern begins to repeat from the 5th one (i.e., 5th is the same as 1st);
Note that this extra offset is also required if Option 2 in the LS to RAN4 is adopted.
Conclusion: 4 configurations on the RB offset are sufficient (e.g. 5, 6, 7, 8), and 2 reserved codepoints in Table 13-2 should be used to indicate the extra RB offset, i.e., 5, for the number of CORESET symbols as 2 and 3, correspondingly.

## Slide 7: Proposal
Adopt the following TP in TS 38.213
Index | SS/PBCH block and control resource set multiplexing pattern | Number of RBs | Number of Symbols | Offset (RBs)
0 | 1 | 24 | 2 | 6
1 | 1 | 24 | 2 | 7
2 | 1 | 24 | 2 | 8
3 | 1 | 24 | 3 | 6
4 | 1 | 24 | 3 | 7
5 | 1 | 24 | 3 | 8
6 | 1 | 48 | 1 | 18
7 | 1 | 48 | 1 | 20
8 | 1 | 48 | 2 | 18
9 | 1 | 48 | 2 | 20
10 | 1 | 48 | 3 | 18
11 | 1 | 48 | 3 | 20
12 | 1 | 24 | 2 | 5
13 | 1 | 24 | 3 | 5
12 | Reserved |  |  | 
13 | Reserved |  |  | 
14 | Reserved |  |  | 
15 | Reserved |  |  | 
Table 13-2: Set of resource blocks and slot symbols of control resource set for Type0-PDCCH search space when {SS/PBCH block, PDCCH} subcarrier spacing is {15, 30} kHz with minimum channel bandwidth 5 MHz