## Slide 1: Offline Summary on CA aspects
Samsung
R1-180xxxx
3GPP TSG RAN WG1#93
Busan, Korea, May 21 – 25, 2018
Agenda item 7.1.3.4.2

## Slide 2: Semi-static HARQ-ACK Codebook
For PDSCH with slot aggregation over R slots
  Alt1: Determine HARQ-ACK codebook size by non-overlapped PDSCH occasions in association set - HARQ-ACK codebook is compressed to ceil(N/R) where N is the number of available slots in HARQ association set (R1-1806073, R1-1806301, R1-1806525, R1-1806630, R1-1806838, Huawei)
    E.g.: Step 1: Find PDSCH candidate C1 having earliest end slot index among set of PDSCH candidates, and go to 2. Step 2: Find PDSCH candidate(s) C2 overlapping with C1 and allocate same HARQ-ACK bit for C1 and C2. step 3: Update set of PDSCH candidates by excluding C1 and C2, and go to Step 1.
  Alt2: Keep current specifications and include that number of slots can be >1 (R1-1806144, R1-1806740, Ericsson)
  Alt3: Keep current specifications by mapping HARQ-ACK bit for TB in each corresponding PDSCH occasion (R1-1806344, R1-1807241)
Determine PDSCH reception occasions per slot by pdsch-symbolAllocation table for DCI formats in USS - PDSCH reception occasions for PDSCHs scheduled by DCI formats in CSS are a subset of the ones for PDSCHs scheduled by DCI formats in a USS (R1-1806740)
  Coordinate with resource allocation session

## Slide 3: Semi-static HARQ-ACK Codebook
Exclude PDSCH candidates with time duration between last symbol and first symbol of PUCCH/PUSCH for HARQ-ACK smaller than the PDSCH processing time (R1-1807236, R1-1807067)
HARQ-ACK bits for PDSCHs scheduled by respective PDCCHs received after an UL grant scheduling PUSCH (for UCI on PUSCH) are set to NACK to maintain HARQ-ACK codebook size (R1-1807262)
To capture in TS 38.213 that “A UE is not expected to have HARQ-ACK bits to multiplex due to DCI that is no earlier by N2 symbols than current PUCCH resource” (R1-1806776)

## Slide 4: Semi-static HARQ-ACK Codebook
UE reports a PDSCH detection outcome (ACK/NACK) for a PDSCH occasion only in HARQ-ACK codebook indicated by PDSCH-to-HARQ timing field in corresponding DL DCI – UE reports NACK/DTX in other HARQ-ACK codebooks where UE reports HARQ-ACK for the PDSCH occasion
  Yes: R1-1805895, R1-1806144, R1-1806740, R1-1806838, [R1-1807399]
  No (UE reports actual HARQ-ACK in each corresponding codebook): R1-1807415
  No – also, UE reports NACK in PUCCH corresponding to larger k1 than indicated k1 in DL DCI (R1-1807399)
Reconsider inclusion of PDCCH monitoring occasions for determining HARQ-ACK codebook size (R1-1806740)

## Slide 5: Miscellaneous Aspects
Prioritize grant-based PUSCH over grant-free PUSCH for UCI multiplexing (R1-1806073, R1-1806630, R1-1806838, and Docomo)
  The PUSCHs are on different cells
  Offline proposal is to support
Support of 2 PUCCH transmissions in a slot for (different) HARQ-ACK (R1-1807067, R1-1806301)
  Overlaps with URLLC related topics
  Have a TP capturing that for the Dec. 2017 drop there is only one PUCCH that includes HARQ-ACK in a slot (UE is not expected to have more than one PUCCH with HARQ-ACK in a slot)