## Slide 1: CA Offline Session 2
Samsung
R1-189848
3GPP TSG RAN WG1#94
Gothenburg, Sweden, August 20 – 24, 2018
Agenda item 7.1.3.4

## Slide 2: Open Issues for HARQ-ACK Codebooks
R1-1808493: Specs are not consistent in describing fallback operation for semi-static HARQ-ACK codebook on PUSCH – 9.1.2 results to HARQ-ACK for only one PDSCH while 9.1.2.2 results to HARQ-ACK for all applicable PDSCH monitoring occasions (when DAI = 1)
  Comment: One possible resolution is to combine 9.1.2 and 9.1.2.2 and condition the description in 9.1.2.2 subject to the conditions in 9.1.2 not applying; otherwise, 9.1.2 applies for HARQ-ACK multiplexing in PUSCH
Offline conclusion
Align 9.1.2 and 9.1.2.2 to support fallback operation for semi-static HARQ-ACK codebook on a PUSCH subject to the following conditions
  DAI in UL grant is equal to 0 (when PUSCH is in response to detection of an UL grant)
  Include in section 9.1.2.2 the following (exact text subject to editorial adjustments)
    If a UE reports HARQ-ACK information in a PUSCH only for a SPS PDSCH release or only for a PDSCH reception within the occasions for candidate PDSCH receptions, as determined in Subclause 9.1.2.1, that is scheduled by DCI format 1_0 with a counter downlink assignment indicator (DAI) field value of 1 on the PCell, the UE determines a HARQ-ACK codebook only for the SPS PDSCH release or only for the PDSCH reception

## Slide 3: Open Issues for HARQ-ACK Codebooks
R1-1808756: PDSCH table (SLIVs) associated with DCI received in CORESET#0 is subset of PDSCH table associated with DCI received in CORESET other than CORESET#0
  Comment: Extend the agreement that K1 values for DCI format 1_0 are a subset of ones configured for DCI format 1_1 to the two PDSCH-TimeDomainResourceAllocation tables agreed at last RAN1 meeting
  Consult with PDSCH processing session whether SLIVs in default PDSCH table are needed after a table is provided by RRC and decide between
    A) SLIV values from the default PDSCH table are only ones included in the PDSCH table provided by RRC (default table is the one associated with CORESET#0)
    B) SLIV values are the union of SLIV values in default table and the table provided by RRC
Offline conclusion
For determination of Type 1 (semi-static) HARQ-ACK codebook, the SLIV values are the union of the SLIV values in the default table and the SLIV values in the table provided by UE-dedicated RRC

## Slide 4: Open Issues for HARQ-ACK Codebooks
R1-1808756/R1-1809323: HARQ-ACK multiplexing for multi-slot PUSCH
  R1-1808756: One UL DAI, DL association set is separate for each PUSCH repetition (same as if HARQ-ACK transmission was on individual PUCCHs)
  R1-1809323 – Alt1: Do not multiplex in later PUSCH repetitions HARQ-ACK bits multiplexed in earlier PUSCH repetitions (construct disjoint DL association sets)
  R1-1809323 – Alt2: Aggregate HARQ-ACK for all DL association sets into one DL association set and multiplex in first PUSCH repetition
Tentative offline conclusion
If the UE would not transmit PUCCH (with HARQ-ACK) in a slot of a multi-slot PUSCH transmission, the UE does not multiplex HARQ-ACK in the slot of the multi-slot PUSCH transmission even when the DAI value in the UL grant is not zero
Continue discussion to determine
Whether to allow HARQ-ACK multiplexing
  only in the first slot (DAI in UL grant is then applicable to the first slot), or
  in all slots (UL DAI is then ignored)
Whether to have reserved bits for HARQ-ACK in slots other than the first slot if HARQ-ACK multiplexing is only in the first slot
  Also consider grant-free PUSCH

## Slide 5: Open Issues for HARQ-ACK Codebooks
R1-1809323: Semi-static HARQ-ACK codebook may contain HARQ-ACK bit(s) for PDSCH that do not satisfy the processing time constraint Tproc,1  when checking the N+1 + d1,1 + d1,2 time constraint for overlapping PUSCH/PUCCH that include a PUCCH with HARQ-ACK, ignore PDSCH receptions not satisfying the Tproc,1 time constraint
  Comment: Further discussion for the necessity as N+1 + d1,1 + d1,2 symbol duration of each PDSCH (already accounts for different symbol durations that motivated the RAN1#93 agreement for the semi-static HARQ-ACK codebook)

## Slide 6: Timing k for Scell Activation/Deactivation
R1-1808104:
  μ is the minimum among the subcarrier spacings of SCells to be activated/deactivated
R1-1809144:
  μ is minimum of {μ of PDSCH with activation command, μ of PUCCH with HARQ-ACK for activation command}
R1-1809408: k is set to k1
  k1 is the PDSCH-to-HACK-ACK timing indicator in the DCI scheduling the PDSCH with the activation MAC CE
  k1 is defined in the numerology of the PUCCH containing the HARQ-ACK for the activation command

## Slide 7: Other
Multiple DCIs in same PDCCH monitoring occasion scheduling respective multiple PDSCH on same cell (R1-1808104, R1-1808493, R1-1809408)
  Comment: Previously discussed – not supported based on conclusion of UE feature discussion in RAN1#92bis
R1-1808381: Do not exclude from HARQ-ACK dynamic codebook HARQ-ACK for PDSCHs scheduled in PDCCH monitoring occasions before slot with DCI indicating DL BWP change
  Comment: HARQ-ACK before the BWP change for cells other than the cell with the DL BWP change are already not excluded from the HARQ-ACK codebook
R1-1808381: HARQ-ACK timing indication – Modify spec text to capture relative SCS for slot of PDSCH reception n and slot of PUCCH transmission n+k
  Comment: Current text in 38.213 is accurate/simple – slot n is wrt PUCCH SCS, not PDSCH SCS

## Slide 8: Other
R1-1808381: Clarify fallback operation for semi-static HARQ-ACK codebook
  Proposal: If UE detects a single SPS PDSCH release or PDSCH reception scheduled by DCI format 1_0 and C-DAI=1 within the set of candidate PDSCH receptions for corresponding PUCCH and there is no other detected PDSCH with same HARQ-ACK PUCCH slot, UE determines HARQ-ACK codebook only for the SPS PDSCH release or only the PDSCH reception
  Comment: Current text in 38.213 is accurate/clear (a minor modification was also mentioned in R1-1808953)
R1-1808381: For semi static codebook, there is no description of how a UE should determine the codebook when the UE receives only a SPS PDSCH – TP provided
  Comment: No need for special treatment of only SPS PDSCH – proposed text is not according to operation of semi-static HARQ-ACK codebook or according to fallback operation
R1-1808953: It was agreed that grant-based PUSCH prioritized over grant-free PUSCH – suggests this is not clear in the 38.213 and a TP
  Comment: This is already captured in section 9 of current 38.213
R1-1808894: Suggestion is to modify pseudo-code for second HARQ-ACK codebook (in case of CBG configuration)
  Comment: Unclear what the problem is – example provided in R1-1808894 seems incorrect

## Slide 9: References