## Slide 1: General principle of re-transmission of PUSCH with configured grant
NTT DOCOMO
R1-1809980
3GPP TSG RAN WG1#94
Gothenburg, Sweden, August 20th – 24th, 2018
Agenda item 7.1.3.3

## Slide 2: Issue
It was agreed the DCI size for DCI with CS-RNTI is the same as the DCI with C-RNTI
For DCI with CS-RNTI, NDI is used to differentiate (de)activation or retransmission
  NDI=0: activation or deactivation; NDI=1: re-transmission
C-RNTI
CS-RNTI
Same DCI size
identifier | CC indicator | UL/SUL indicator | BWP indicator | Freq. RA | Time domain RA | FH flag | MCS | NDI | RV | ……
CS-RNTI
Initial Tx
ConfiguredGrantConfig.
identifier | CC indicator | UL/SUL indicator | BWP indicator | Freq. RA | Time domain RA | FH flag | MCS | NDI | RV | ……
Re-Tx
???
Same position
The size can be different depending on the waveform, RA type, etc.
PUSCH-Config. and ConfiguredGrantConfig. Can be configured differently  Already agreed

## Slide 3: Proposal
For a scheduled retransmission of a TB previously transmitted on a configured PUSCH, the UE follows
  Option 1: the set of parameters provided in configuredGrantConfig IE that are common to both Type1 and Type2 configured grant. For all other parameters not provided in configuredGrantConfig, including those in rrc-ConfiguredUplinkGrant, the UE follows the transmission configuration provided by the PUSCH-Config IE.
    Pros: simple and no additional issues.
    Cons: May lose some scheduling flexibility
  Option 2: the set of transmission parameters provided by the PUSCH-Config IE.
    Pros: May have some scheduling flexibility
    Cons: ambiguity on the DCI scrambled by CS-RNTI is used for (de)activation/re-transmission or restriction on configured grant configuration

## Slide 4: Agreements
Agreements made in RAN1#93:
  For CS-RNTI DCI sizes
    For DCI format 1-1 with CS-RNTI, the DCI size are the same as the DCI format 1-1 with C-RNTI in respective search space.
    For DCI format 0-1 with CS-RNTI, the DCI size are the same as the DCI format 0-1 with C-RNTI in respective search space.
    For DCI format 1-0 with CS-RNTI, the DCI size are the same as the DCI format 1-0 with C-RNTI in respective search space.
    For DCI format 0-0 with CS-RNTI, the DCI size are the same as the DCI format 0-0 with C-RNTI in respective search space.
Agreements made in RAN2 #100:
For SPS and type 1, if the received uplink grant or DL assignment addressed to SPS C-RNTI. If the NDI in the received HARQ information is 1, consider the NDI for the HARQ process not to been toggled, as in LTE.
For SPS if the NDI in the received HARQ information is 0, it is for SPS activation/deactivation

## Slide 5: Agreements
Agreements made in RAN1#93:
For both initial transmission and re-transmissions for GF scheduling for URLLC,
  For UL configured grant, the MCS table is configured by the existing parameter associated with the RRC configured grant configuration, which is extended to include the new 64QAM MCS table.
  For DL SPS, RRC indicates whether or not the new 64QAM table is configured. The indication for the new MCS table for DL SPS is separate from the one for grant-based DL scheduling.

## Slide 6
Field | Payload [bits] | Fixed or flexible
Identifier | 1 | Fixed
Carrier indicator | 0 or 3 | Configurable
UL/SUL indicator | 0 or 1 | Configurable
Bandwidth part indicator | 0 or 1 or 2 | Configurable
Frequency-domain assignment |  | Configurable
Time-domain assignment | 0 or 1 or 2 or 3 or 4 | Configurable
Freq-hopping flag | 0 or 1 | Configurable
MCS | 5 | Fixed
NDI | 1 | Fixed
RV | 2 | Fixed
HPN | 4 | Fixed
1st UL DAI | 1 or 2 | Configurable (1 bit for semi-static CB, 2 bits for dynamic CB)
2nd UL DAI | 0 or 2 | Configurable (2 bits for dynamic CB with two sub-CBs)
TPC command | 2 | Fixed
SRS resource indicator |  | Configurable
Precoding information and number of layers | 0 or 1 or 2 or 3 or 4 or 5 or 6 | Configurable
Antenna ports | 2 or 3 or 4 or 5 | Configurable
SRS request | 2 or 3 | Eventually fixed (2 for non-SUL operation while 3 for SUL operation)
CSI request | 0 or 1 or 2 or 3 or 4 or 5 or 6 | Configurable
CBGTI | 0 or 2 or 4 or 6 or 8 | Configurable
PTRS-DMRS association | 0 or 2 | Configurable
Beta-offset indicator | 0 or 2 | Configurable
DMRS seq initialization | 0 or 1 | Configurable
UL-SCH indicator | 1 | Fixed
Padding bits if needed | Alignment b/w 0_1 for SUL/UL | Not impact on bit positions of the fields in the DCI
DCI format 0-1

## Slide 7
Agreements:
For UL transmission with grant,
  By UE-specific RRC signaling, a UE can be configured with UL waveform that is different from the one configured by RMSI for Msg3. Once configured;
    When the non-fallback DCI schedules the PUSCH transmission, the UE uses the UL waveform configured by the UE-specific RRC signaling; when the fallback DCI schedules the PUSCH transmission, the UE uses the UL waveform configured by RMSI for the PUSCH transmission.
  If the UE is not configured with UL waveform that is different from the one configured by RMSI for Msg3;
    The UE uses the UL waveform configured by RMSI for the PUSCH transmission.
  FFS: whether the fallback DCI is based on DCI format/size or on search space.
  RMSI informs single waveform to the UE
Agreements:
For Type 1 and Type 2 UL transmission without grant,
  By UE-specific RRC signaling, a UE can be separately configured with UL waveform that is different from the one configured by RMSI for Msg3.
  Note: even if the UE is configured with Type 1 and Type 2 UL transmission without grant, the UE may transmit PUSCH that is scheduled by UL grant, in which case the UL waveform determination for UL transmission with grant is used.