## Slide 1
Joint Proposal on Deterministic Sequence Hopping for /2 BPSK CGS Sequence
Intel, ZTE, Sanechips, Qualcomm
R1-195604

## Slide 2: Background
The following agreement was made in 3GPP RAN1#96:
To address the FFS point, a deterministic sequence hopping pattern is proposed for length 12, 18 and 24 CGS sequences for /2-BPSK modulated PUSCH DM-RS
Key Properties:
  Deterministic hopping pattern for single symbol FL DMRS with additional DMRS in the slot.
  The sequence ID for first DM-RS symbol can be chosen randomly using sequence hopping formula; the corresponding sequence for next occurring DM-RS symbol is chosen deterministically from the proposed tables.
  Key advantage is that the joint autocorrelation of the pair of sequences is better than the individual sequence autocorrelations.
Agreement
For the case of CGS sequence in case of two adjacent symbol DM-RS, the same CGS sets are used for both single and two symbol DM-RS for pi/2 BPSK modulation.
FFS: Whether or not to support deterministic sequence hopping pattern

## Slide 3: Deterministic Sequence Hopping for Length-12
CGS index for the first DMRS symbol | CGS index for the next DM-RS symbol | CGS index for the first DMRS symbol | CGS index for the next DM-RS symbol
0 | 16 | 15 | 0
1 | 1 | 16 | 19
2 | 7 | 17 | 21
3 | 15 | 18 | 23
4 | 4 | 19 | 12
5 | 29 | 20 | 14
6 | 24 | 21 | 17
7 | 26 | 22 | 10
8 | 27 | 23 | 2
9 | 22 | 24 | 3
10 | 6 | 25 | 20
11 | 25 | 26 | 9
12 | 8 | 27 | 18
13 | 28 | 28 | 13
14 | 11 | 29 | 5
Table 1: Deterministic hopping pattern for Length 12 DMRS
Auto Corr | Lag | Deterministic hopping | Random
mean | 2 | 0.022 | 0.052
 | 3 | 0.026 | 0.073
max | 2 | 0.167 | 0.333
 | 3 | 0.167 | 0.333
XCorr |  |  | 
mean | 2 | 0.157 | 0.158
 | 3 | 0.159 | 0.160
max | 2 | 0.667 | 0.667
 | 3 | 0.667 | 0.833

## Slide 4: Deterministic Sequence Hopping for Length-18
CGS index for the first DMRS symbol | CGS index for the next DM-RS symbol | CGS index for the first DMRS symbol | CGS index for the next DM-RS symbol
0 | 23 | 15 | 5
1 | 17 | 16 | 1
2 | 6 | 17 | 20
3 | 0 | 18 | 12
4 | 19 | 19 | 25
5 | 7 | 20 | 24
6 | 8 | 21 | 15
7 | 11 | 22 | 28
8 | 2 | 23 | 9
9 | 4 | 24 | 27
10 | 22 | 25 | 14
11 | 21 | 26 | 13
12 | 18 | 27 | 16
13 | 29 | 28 | 26
14 | 10 | 29 | 3
Table 2: Deterministic hopping pattern for Length 18 DMRS
Auto Corr | Lag | Deterministic hopping | Random
mean | 4 | 0.032 | 0.040
 | 5 | 0.040 | 0.053
max | 4 | 0.222 | 0.333
 | 5 | 0.222 | 0.444
XCorr |  |  | 
mean | 4 | 0.132 | 0.132
 | 5 | 0.133 | 0.133
max | 4 | 0.500 | 0.889
 | 5 | 0.500 | 0.889

## Slide 5: Deterministic Sequence Hopping for Length-24
CGS index for the first DMRS symbol | CGS index for the next DM-RS symbol | CGS index for the first DMRS symbol | CGS index for the next DM-RS symbol
0 | 18 | 15 | 7
1 | 19 | 16 | 10
2 | 5 | 17 | 11
3 | 23 | 18 | 0
4 | 21 | 19 | 1
5 | 2 | 20 | 28
6 | 27 | 21 | 8
7 | 22 | 22 | 29
8 | 14 | 23 | 16
9 | 26 | 24 | 12
10 | 3 | 25 | 13
11 | 15 | 26 | 9
12 | 24 | 27 | 6
13 | 25 | 28 | 20
14 | 4 | 29 | 17
Table 3: Deterministic hopping pattern for Length 24 DMRS
Auto | Lag | Deterministic hopping | Random
mean | 5 | 0.021 | 0.021
 | 6 | 0.033 | 0.036
max | 5 | 0.083 | 0.167
 | 6 | 0.250 | 0.500
XCorr |  |  | 
mean | 5 | 0.115 | 0.116
 | 6 | 0.116 | 0.116
max | 5 | 0.500 | 0.667
 | 6 | 0.500 | 0.667