## Slide 1: R2-164412 Way Forward #2 on PDCCH Occasions in NB-IOT
MediaTek Inc.

## Slide 2: Discussion
Alignment issues are already resolved
  The eNB always configures the offset properly so that starting point of onDurationTimer aligns with that of PDCCH USS. If not, this is bad eNB behavior.
  For drx-InactivityTimer and drx-retransmissinTimer, we agreed that “When UE need to continue PDCCH monitoring after a transmission, UE should start PDCCH monitoring at the first PDCCH occasion 4ms after HARQ feedback and/or PUSCH transmission, i.e. after RTT timer expiry. ”
MAC timers and windows may be specified in unit of T=Rmax*G (RAN1 def). In case T>10.24s, there may be more than one PDCCH in each T:
  For DRX-related timers, this is not a problem since max DRX cycle is 10.24s and no DRX-related timer is configured longer than that
  For ra-ResponseWindowSize and mac-ContentionResolutionTimer, we have Min(.,10.24s)
  For other timers (logicalChannelSR-ProhibitTimer-NB-r13, periodicBSRTimer, etc), we don’t have additional limits, but the UE can go DRX/eDRX if the value is set too long

## Slide 3: Discussion
  When a timer is configured as pp_n/ss_n, its duration is given by the signaled value*T
  Note: the interval between the starting points of two consecutive NPDCCH USSs may not be equal to T, in case (1) T>10.24s, or (2) two USSs are located in different hyper frames.
  In some cases, automatic extension is needed. Example: Rmax = 256, G = 1.5, (T = 384), onDurationTimer = uss2
X
PDCCH USS, 256ms
...
10240ms
10240ms
...
2T
Extended onDurationTimer
UE monitors only 1 USS
UE monitors 2 USSs

## Slide 4: Proposals
Proposal 1: When a MAC timer or window is specified as pp_n/ss_n, its length is given by the signaled value*T, where T=Rmax*G
Proposal 2: When the ending point of a MAC timer or window is within a PDCCH CSS/USS, it is automatically extended to the end of the CSS/USS.