## Slide 1
Proposals on IAB Architecture
Qualcomm, AT&T, KDDI, Ericsson, Nokia, Nokia Shanghai Bell, Intel, Samsung, Huawei
3GPP TSG-RAN WG2 NR Ad hoc 1801 R2-1801606 Vancouver, Canada, 22nd January – 26th January 2018
Agenda Item: 11.1

## Slide 2: Multi-hop backhauling
Motivation
Multi-hop backhauling provides more range extension than single hop.
Above-6 frequencies have limited range and can profit from such larger range extension.
Multi-hop backhauling enables backhauling around obstacles, e.g. buildings in urban environment for in-clutter deployments.
Since hop count depends on many factors (e.g. deployment scenario, traffic load, frequency,…) flexibility in hop-count ensures future proofness.
The study can provide an understanding on the scalability of signaling and performance with increasing hop count.
Proposal 1: IAB design shall support multiple backhaul hops
The architecture should not impose limits on the number of backhaul hops.
The study should consider scalability to hop-count an important KPI.
Single hop is considered a special case of multiple backhaul hops.
IAB Donor
IAB Node
IAB Node
IAB Node
1st hop
2nd hop
2nd hop
Supporting contributions:
Nokia, Nokia Shanghai Bell | R2-1800389 R2-1800417
Qualcomm Inc | R2-1800411
KDDI | R2-1800571
Huawei, HiSilicon | R2-1801131 R2-1801132
AT&T | R2-1801214

## Slide 3: Topology adaptation
IAB Node
IAB Donor 1
IAB Donor 2
X
IAB Node 3
IAB Node 1
IAB Node 2
IAB Donor
Motivation
Wireless backhaul links are vulnerable to blockage, e.g. due to moving objects such as vehicles, trucks, etc.
Traffic variations can create uneven load distributions on wireless backhaul links leading to link or node congestion.
Topology adaptation allows the backhaul network to autonomously reconfigure under such circumstances without discontinuing services for UEs.
Proposal 2: Topology adaptation for physically fixed relays is supported to enable robust operation, e.g., mitigate blockage and load variation on backhaul links
Supporting contributions:
Qualcomm Inc | R2-1800411
Nokia, Nokia Shanghai Bell | R2-1800417
Ericsson | R2-1801021 R2-1801022
Huawei, HiSilicon | R2-1801130 R2-1801131
AT&T | R2-1801217
ITRI | R2-1801348
LG Electronics | R2-1801402

## Slide 4: L2- and L3-relay architectures
Motivation
There has been extensive work in 3GPP on L2 and L3 relay architectures.
Leveraging this work may reduce the standardization effort for IAB.
The study can establish an understanding of the tradeoff between L2- and L3-relaying in the context of IAB.
Proposal 3: L2 and L3 relay architectures will be studied
Definitions of L2- and L3-relaying in the context of IAB is FFS
Supporting contributions:
OPPO | R2-1800156 | L2
Nokia, Nokia Shanghai Bell | R2-1800389 R2-1800392 R2-1800393 | L2 + L3
Qualcomm Inc | R2-1800413 | L2
KDDI Corp | R2-1800568 | L2 + L3
VIVO | R2-1800854 | L2
Intel | R2-1800953 | L2 + L3
Ericson | R2-1801022 | L2 + L3
Huawei, HiSilicon | R2-1801131 R2-1801132 | L2 + L3
LG Electronics | R2-1801428 | L2 + L3

## Slide 5: Core-network impact
Motivation
IAB-node integration, IAB topology adaptation and potentially other IAB features may require new core-network specifications.
Dependent on design, IAB features may further create additional core-network signaling load.
Proposal 4: The IAB design should minimize the impact to core network specifications
Proposal 5: The study should consider the impact to the core network signaling load as an important KPI
Qualcomm Inc | R2-1800412
Intel | R2-1800953
Sony | R2-1801094
AT&T | R2-1801217
Supporting contributions:

## Slide 6: Reuse of Rel-15 NR
Motivation
Leveraging existing Rel-15 NR specifications can greatly reduce the standardization effort for the backhaul link.
The backhaul link may have additional requirements, which are not addressed in Rel-15 NR.
  Opposed to the access link, both link end points of the backhaul link are expected to have similar capabilities.
Proposal 6: Strive to maximize reuse of Rel-15 NR specifications for the design of the backhaul link
Enhancement can also be considered.
Qualcomm Inc | R2-1800411
KDDI Corp | R2-1800571
Ericsson | R2-1801022
Huawei, HiSilicon | R2-1801131
AT&T | R2-1801214
Supporting contributions:

## Slide 7: Supporting Contributions
R2-1800156 | OPPO | Discussion on flexible routing support in IAB
R2-1800389 | Nokia, Nokia Shanghai Bell | General views on the scope of the IAB study
R2-1800392 | Nokia, Nokia Shanghai Bell | Architecture and Protocols: MAC adaptation layer based IAB
R2-1800393 | Nokia, Nokia Shanghai Bell | Architecture and Protocols: Connectivity Service Solution for IAB
R2-1800411 | Qualcomm Inc | IAB deployment considerations
R2-1800413 | Qualcomm Inc | IAB – User-plane Aspects
R2-1800417 | Nokia, Nokia Shanghai Bell | Nokia IAB topology discussion
R2-1800568 | KDDI | High level overview on IAB
R2-1800571 | KDDI | Use cases for IAB
R2-1800854 | vivo | Preference for Protocol Stack of NR Relay
R2-1800953 | Intel | Scenario and architecture for IAB Intel Corporation
R2-1801021 | Ericsson | Deployment scenarios and use cases for Integrated Access Backhaul
R2-1801022 | Ericsson | Architecture for integrated access and backhaul
R2-1801094 | Sony | Initial considerations on Remote node connectivity in IAB
R2-1801130 | Huawei, HiSilicon | Consideration on IAB Scenarios and Use Cases
R2-1801131 | Huawei, HiSilicon | Overall high layer design of IAB
R2-1801132 | Huawei, HiSilicon | Overall high layer design of IAB
R2-1801214 | AT&T | Use cases and deployment scenarios for IAB
R2-1801217 | AT&T | Architecture requirements for IAB
R2-1801348 | ITRI | Discussion on the topology and protocol stack of IAB
R2-1801402 | LG Electronics | Consideration on route selection