## Slide 1: Way forward on TNL Address Discovery for Option 3
NTT DOCOMO, INC.
R3-182894
3GPP TSG-RAN WG3 RAN3#100
Busan, South Korea, 21-25 May 2018

## Slide 2: Background
TNL address discovery function is very beneficial from operators as discussed in [1].
  e.g. ANR function, which relieve the operator from the burden of manually managing neighbor Relations (NRs).
Considering multi-vendor operability, it is desirable for operators to introduce standardized approach i.e. C-plane solution.
However, there was no agreement for C-plane solutions.
Note that this contribution is resubmission of R3-181165/R3-181784, which was not treated in RAN3#99/RAN3#99bis

## Slide 3: Options over C-plane and comment for them
Several options were discussed in previous meetings.
  eNB proxy (eNB serve as proxy towards the MME)
  Direct connection between gNB and MME
  X2 GW
Proposed option in RAN3 NR AH1801 [2][3] was only “3. X2 GW”
  However, there was offline comment about concern on following aspects.
    Increase of delay over X2; X2 GW approach seems to transfer all X2 messages via X2GW.
    Not prefer to deploy new node; X2 GW approach seems to have new node.
MME
Forwarding
table
gNB
eNB
gNB
X2 GW
Forwarding
table
eNB
gNB
MME
Forwarding
table
eNB
Registration:
TNL address discovery:

## Slide 4: Wayforward
RAN3 to introduce “X2 GW” solution in Rel-15 with the clarification of following.
  Only TNL address discovery related messages are transferred via “X2 GW”.
  “X2 GW” function can be included in a current logical node as far as connected with X2.
  Exact name of this solution (i.e. whether to call this function as “X2 GW”) is FFS
  Further technical details are FFS

## Slide 5: Reference
[1] R3-180319, “TNL address discovery for NSA”, NTT DOCOMO, INC.
[2] R3-180223, “TNL address discovery based on intermediate node, for option 3”, Nokia, Nokia Shanghai Bell
[3] R3-180150, “En-gNB X2 TNL Address Discovery”, Huawei